## Slide 1: Realtime Programming

## Slide 2: Housekeeping
Labor
  Alles bei Frau Glönkler
  Nur offen für das aktuelle Semester laut SPO
Klausur
  Beinhaltet Lab
  +5% bei kompletter erfolgreicher Bearbeitung des Labors
Hardware
  Nutzen um zu üben!

## Slide 3: Real-Time Programming - Motivation
Software Engineering
+ Electronics Engineer
+ Automotive / Mechanical / Electrical Engineering
--------------------------------------
= Embedded Software
= Real-Time Programming
+ Signal Processing
+ Control Engineering
The ten most frequently sought jobs in Germany:
Software developer and programmer
Electronics engineer, electrician
Healthcare worker and nurse
IT consultant, IT analyst
Economist, business administrator
Account manager, client consultant
Production assistant
Sales representative, sales assistant
Sales manager, product manager
Architect, structural engineer
Source: DEKRA Akademie 2018
Germany’s most important industries
4 sectors dominate industry in Germany: the automotive, mechanical engineering, chemical and electrical industries. The global players are Volkswagen, Daimler, BMW (all automotive), BASF (chemical) and Siemens (electrical). Mechanical engineering is characterized by small and medium-sized enterprises.

## Slide 4: Realtime Systems
Automotive Door Contol Unit
with Anti-Squeeze

## Slide 5: Traffic-Light Control in Hardware
A1
A2
A3
1
2
Problem Analysis Finite State Machine (FSM)
Phase 1: 0 ≤ t < T1  State 1
Phase 2 T1 ≤ t < 2·T1  State 2
State 1: A1 = red A2 = A3 = green
State 2: A1 = green A2 = A3 = red
t
Advantages
Realization relatively cost effective with standard logic PLA or FPGA
Real-Time aspects are usually uncritical
Disadvantages
Inflexible solution: Adaptations more features e.g.: yellow-phases synchronization priority control... involve hardware changes !
Variants are relatively expensive
Realization in Hardware state encoding: 1:Q = 0 2:Q = 1
output encoding: red: 1 green: 0
D
Q
Q
Timer
Period T1
D-FlipFlop
Driver
A1
A2
A3
typ. Delay ~ 10 ns

## Slide 6: Traffic-Light Control in Software
A1
A2
A3
1
2
Problem Analysis Finite State Machine (FSM)
Phase 1: 0 ≤ t < T1  State 1
Phase 2 T1 ≤ t < 2·T1  State 2
State 1: A1 = red A2 = A3 = green
State 2: A1 = green A2 = A3 = red
t
Realization in Software (FSM) state encoding: 1:Q = 0 2:Q = 1
output encoding: red: 1 green: 0
// called periodic with T1
void AmpelTask() {
static int state = 0;
state = !state; // state change
if (state == 0) {
A1 = 1;
A2 = A3 = 0;
} else {
A1 = 0;
A2 = A3 = 1;
}
}
critical
Delays can appear !
Delay: 1 µs .. x ms !
Advantages
Realization very cost effective with µC (Embedded System with/without network „IoT)
Standard-Hardware + Embedded Software (C/C++)
Flexible solutions: Adaptations more features e.g.: yellow phases synchronization priority control... by software-updates without changing hardware !
Disadvantages
Real-Time Requirements have to be fulfilled  Real-Time Programming

## Slide 7: Traffic-Light Control – Real-Time Requirements
critical state
transition
A1
A2
A3
1
2
t
A1
A2
A3
Phase1
Phase2
Phase1
DT
Real-Time Requirement for Concurrency:
DT always (!) must be smaller than the human reaction time (10 .. 50 ms) !!
t
v = 50 km/h
= 14 m/s
Ds = v·0.1 s
= 1.4 m
Problem Analysis Finite State Machine (FSM)
Phase 1: 0 ≤ t < T1  State 1
Phase 2 T1 ≤ t < 2·T1  State 2
State 1: A1 = red A2 = A3 = green
State 2: A1 = green A2 = A3 = red

## Slide 8: Traffic-Light Control - Real-Time Requirements - 2
critical state
transition
A1
A2
A3
1
2
t
A1
A2
A3
Phase1
Phase2
Phase1
DT
Real-Time Requirement for Safety:
A1 must always switch after A2 and A3 AND
DT always (!) must be small wrt the human reaction time (10 .. 50 ms) !!
t
v = 50 km/h
= 14 m/s
Ds = v·0.1 s
= 1.4 m
Problem Analysis Finite State Machine (FSM)
Phase 1: 0 ≤ t < T1  State 1
Phase 2 T1 ≤ t < 2·T1  State 2
State 1: A1 = red A2 = A3 = green
State 2: A1 = green A2 = A3 = red

## Slide 9: Topics Covered:
Concepts of Realtime
Task management
Inter-task communication
Scheduling
RTOS
Timestamping / Clocks
Communication
Approaching multi core systems

## Slide 10: Realtime Concepts

## Slide 11: Definitions
Wikipedia:
  In computer science real-time computing (RTC) or reactive computing is the study of hardware and software systems that are subject to a real-time constraint i.e. operational deadlines from event to system response.
  By contrast a non-real-time system is one for which there is no deadline even if fast response or high performance is desired or preferred.
  Real-time computations can be said to have failed if they are not completed before their deadline where their deadline is relative to an event.
  A real-time deadline must be met regardless of system load

## Slide 12: Realtime and Processes
Materials
Energy
Information
Materials
Energy
Information
Process Control
e.g. process
computer
Process:
- convert (transform)
- transport
Operator
Process Control Data
Actors
Sensors
Input Data Process State
Z
ZD
U
Disturbances
Real-time Computer
Control
Technical Process
Output data
Input data
must read calculate and output data in time
defines deadlines

## Slide 13: Time Conditions
time t
t0
Precise time Exact time
Latest Time deadline
time t
tmax
time t
tmin
Earliest Time
Time Interval
time t
tmin
tmax
Periodic Time Condition
time t
kts
(k+1)ts
(k+2)ts
time t
t1
t2
t3
Non-Periodic Time Condition

## Slide 14: Realtime Requirements
Hard Realtime
  the time conditions must be met or catastrophes occur ! Deviations from the time-conditions are not allowed and represent a serious error.
Soft Realtime
  the deadlines must be met but with a degree of flexibility. The deadlines can contain varying levels of tolerance average timing deadlines and even statistical distribution of response times with different degrees of acceptability
Concurrency
  Real-time systems must generally treat multiple inputs and outputs simultaneously

## Slide 15: Realization of RT systems
Task 1
Processor 1
Task n
Processor n
...
...
...
Real-Time Scheduler
Processor 1
Processor m
...
Task 1
Task n
...
n > m
Real-Time Scheduler
Processor 1
Task 1
Task n
...
1. complete parallel processing multiprocessor system
2. quasi-parallel processing multiprocessor system
3. quasi-parallel processing
uniprocessor system

## Slide 16: Availability
Reorganization (e.g. Garbage Collection) en bloc
Operations
Events
missed
Events
/* reorganization free algorithm
for calculation of a factorial */
int fact(int n)
{
int f = 1;
for (i = 1; i < n; i++) {
f *= i;
} return f;
}
/* algorithm needs reorganization
with calculation of a factorial */
int fact(int n)
{
if (n > 1) return n*fact(n-1); // dynamic
else // memory
return 1; // needed here
}
OK with Real-Time programming Not OK with Real-Time programming !

## Slide 17: Processing Time
Events
TP
t0
TV
TR
TZ: allowed Reaction Time
TV: Processing/Execution Time
TR: Reaction Time TL: Latency Time
TP: Prozess Time
TL
TZmax
Timeliness Response time and Maximum Response Time
Timeliness means that a task required at the time t0
is done not before a specified time t0 + TZmin and
is done no later than a specified time t0 + TZmax (timeliness).
The processing/execution time needed for a certain number of operations N is inverse to the computing power P (in ops / sec) a processor core (CPU) offers.
TV = N / P [TV] = ops / (ops / s) = s.

## Slide 18: Process Time Load
The time between two requests of the same type (TP)
Utilization or Load
  ρ = TV/TP
  Is always less than 1 !!

## Slide 19: Real and Soft Time
Principles of Real-Time Programming
Christoph M. Kirsch
Department of Electrical Engineering and Computer Sciences
University of California, Berkeley

## Slide 20: Models for RTP

## Slide 21: Models for RTP
Synchronous
  Zero time computation
  Needs to react in a well defined way
  Always follows the speed of the context
Scheduled
  Controlled by a scheduler and split in tasks
  Schedulability and Deadlines cannot be assessed at compile time
Timed
  Soft-Time is equalled to realtime by controlling execution time
  Most ofteh tasks are periodic

## Slide 22: Implementations

## Slide 23: MCU Components
Source: Introduction to Logic Circuits and Logic Design with VHDL, LaMeres

## Slide 24: MCU Parts
Instruction Register (IR) – The instruction register holds the current binary code of the instruction being executed. This code is read from program memory as the first part of instruction execution. The IR is used by the control unit to decide which states in its FSM to traverse in order to execute the instruction.
Memory Address Register (MAR) – The memory address register is used to hold the current address being used to access memory. The MAR can be loaded with addresses in order to fetch instructions from program memory or with addresses to access data memory and/or I/O ports.
Program Counter (PC) – The program counter holds the address of the current instruction being executed in program memory. The program counter will increment sequentially through the program memory reading instructions until a dedicated instruction is used to set it to a new location.
General-Purpose Registers – These registers are available for temporary storage by the program. Instructions exist to move information from memory into these registers and to move information from these registers into memory. Instructions also exist to perform arithmetic and logic operations on the information held in these registers.
Condition Code Register (CCR) – The condition code register holds status flags that provide information about the arithmetic and logic operations performed in the CPU. The most common flags are negative (N), zero (Z), two’s complement overflow (V), and carry (C). This register can also contain flags that indicate the status of the computer, such as if an interrupt has occurred or if the computer has been put into a low-power mode.

## Slide 25: CPU Organization

## Slide 26: Memory Mapped System

## Slide 27: Concept Issues

## Slide 28: Memory Organisation

## Slide 29: Software

## Slide 30: Adressing
Immediate Addressing (IMM)
Immediate addressing is when the operand of an instruction is the information to be used by the´instruction. For example, if an instruction existed to put a constant into a register within the CPU using immediate addressing, the operand would be the constant. When the CPU reads the operand, it simply inserts the contents into the CPU register and the instruction is complete.
Direct Addressing (DIR)
Direct addressing is when the operand of an instruction contains the address of where the information to be used is located. For example, if an instruction existed to put a constant into a register within the
CPU using direct addressing, the operand would contain the address of where the constant was located in memory. When the CPU reads the operand, it puts this value out on the address bus and performs an
additional read to retrieve the contents located at that address. The value read is then put into the CPU register and the instruction is complete.
Inherent Addressing (INH)
Inherent addressing refers to an instruction that does not require an operand because the opcode itself contains all of the necessary information for the instruction to complete. This type of addressing is used on instructions that perform manipulations on data held in CPU registers without the need to access the memory system. For example, if an instruction existed to increment the contents of a register (A), then once the opcode is read by the CPU, it knows everything it needs to know in order to accomplish the
task. The CPU simply asserts a series of control signals in order to increment the contents of A, and then the instruction is complete. Notice that no operand is needed for this task. Instead, the location of the register to be manipulated (i.e., A) is inherent within the opcode.
Indexed Addressing (IND)
Indexed addressing refers to instructions that will access information at an address in memory to complete the instruction, but the address to be accessed is held in another CPU register. In this type of addressing, the operand of the instruction is used as an offset that can be applied to the address located in the CPU register. For example, let’s say an instruction existed to put a constant into a register (A) within the CPU using indexed addressing. Let’s also say that the instruction was designed to use
the contents of another register (B) as part of the address of where the constant was located. When the CPU reads the opcode, it understands what the instruction is, and that B holds part of the address to be accessed. It also knows that the operand is applied to B to form the actual address to be accessed. When the CPU reads the operand, it adds the value to the contents of B and then puts this new value out on the address bus and performs an additional read. The value read is then put into the CPU register A, and the instruction is complete.

## Slide 31: Decoding

## Slide 32: Decoding

## Slide 33: Decoding

## Slide 34: Execution

## Slide 35: Branching

## Slide 36: Top Level

## Slide 37: Instruction Set

## Slide 38: Memory System

## Slide 39: CPU Block

## Slide 40: State Machine

## Slide 41: State Machine 2

## Slide 42: IO

## Slide 43: Buffer

## Slide 44: Introduction to how things actually work
Assembly using the AVR microprocessor

## Slide 45: A really simple program
Some variables (ij)
Set variables to initial values
A loop
  Check a condition to see if we are finished
  Do some arithmetic
  Output some information
  Increment the loop counter
int main(void)
{
char i;
char j;
i=0;
j=0;
while (i<10) {
j = j + i;
PORTB = j;
PORTB = i;
i++;
}
return 0;
}

## Slide 46: Running a program on a microprocessor
When you want to turn your program into something which runs on a microprocessor you typically compile the program
This creates a program in the machine language of the microprocessor
  A limited set of low level instructions which can be executed directly by the microprocessor
We can also program in this language using an assembler
We can have a look at the assembly language the c compiler generates for our simple program to understand how this works

## Slide 47: Translating our program into assembly language
000000be <main>:
be: 80 e0 ldi r24 0x00 ; 0
c0: 90 e0 ldi r25 0x00 ; 0
c2: 98 0f add r25 r24
c4: 92 bb out 0x18 r25 ; 18
c6: 82 bb out 0x18 r24 ; 18
c8: 8f 5f subi r24 0xFF ; 255
ca: 8a 30 cpi r24 0x0A ; 10
cc: d1 f7 brne .-12 ; 0xc2 <main+0x4>
ce: 80 e0 ldi r24 0x00 ; 0
d0: 90 e0 ldi r25 0x00 ; 0
d2: 08 95 ret
int main(void)
{
char i;
char j;
i=0;
j=0;
while (i<10) {
j = j + i;
PORTB = j;
PORTB = i;
i++;
}
return 0;
}
Location in program memory (Address)
Opcodes – the program code
The Assembly language equivalent of the opcodes

## Slide 48: AVR Microprocessor architecture
Program Memory
Your code goes here
Registers
Storage for numbers the processor will perform arithmetic on
Arithmetic Logic Unit (ALU)
  The heart of the processor which handles logic/math
Input/Output
Interface to the outside world

## Slide 49: Numbers on a microprocessor
We’ve seen that our program is converted into a series of numbers for execution on the microprocessor
Numbers are stored in a microprocessor in memory
  They can be moved in an out of registers and memory
  Calculations can be done
  Numbers can be sent to Output devices and read from Input devices
The numbers are stored internally in binary representations.
  We will study precisely how this is done shortly and even build some simple memory devices.

## Slide 50: Binary/Hexadecimal Numbers
A Bit can be a 0 or 1
  The value is set using transistors in the hardware
Bits are organized into groups to represent numbers
  4 Bits is a Nybble
    Can store numbers 0-15
  8 Bits is a Byte
    Can store numbers 0-255
  16 Bits is a word
    Can store numbers 0-65535
Hexadecimal is a very handy representation for binary numbers
  Each 4 bits maps onto a HEX number
  Can quickly convert from HEX to binary
Binary | Hex | Decimal
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | 8
1001 | 9 | 9
1010 | A | 10
1011 | B | 11
1100 | C | 12
1101 | D | 13
1110 | E | 14
1111 | F | 15

## Slide 51: Binary Representation
This representation is based on powers of 2. Any number can be expressed as a string of 0s and 1s
Example: 9 = 10012 = 1* 23 + 0* 22 + 0*21 + 1*20
Example: 5 = 1012 = 1* 22 + 0*21 + 1*20
Exercise: Convert the numbers
19 38 58 from decimal to binary.
(use an envelope a calculator or C program)

## Slide 52: Hexadecimal Representation
This representation is based on powers of 16. Any number can be expressed in terms of:
012…9ABCDEF (012…9101112131415)
Example: 1002 = 3EA16 = 3* 162 + 14*161 + 10*160
Example: 256 = 10016 = 1* 162 + 0*161 + 0*160
Exercise: Convert the numbers
1492 3481 558 from decimal to hex.
(use calculator or maths package)

## Slide 53: HEX/Binary Conversion
Converting HEX/Binary to Decimal is a bit painful but converting HEX/Binary is trivial
We often use the notations 0x or $ to represent a HEX number
  Example 0x15AB for the HEX number 15AB
  In assember language we see the notation $A9 for the HEX number A9
Exercise: Convert the numbers
0xDEAD 0xBEEF from Hex to binary.
Now convert them to Decimal

## Slide 54: 8 Bit Microprocessors
The AVR microprocessor we will be using is an 8 bit processor
The operations the processor performs work on 8 bit numbers
  Data is copied from memory into the processors internal registers 8 bits at a time
  Operations (addition/subtraction/etc..) can be performed on the 8 bit registers
  We can of course do calculation with bigger numbers but we will have to do this as a sequence of operations on 8 bit numbers
    We will see how to do this later – using a carry bit

## Slide 55: Operations
The processor can perform several operations
  Including Boolean algebra
Exercise: (1) Find NOT(AAA)
(2) Find OR(AAA; 555)
(3) Find AND (AEB123; FFF000)
Why is shift important ?
Try ShiftR(011) ShiftL(011)
(what do SHIFTR and ShiftL do in base 10?)
Operation | Register A | Register B | Result
Add AB | 00001111 | 00000001 | 00010000
Not A | 01010101 |  | 10101010
OR AB | 00010101 | 00101010 | 00111111
ShiftL A | 00001111 |  | 00011110
ShiftR A | 00001111 |  | 00000111
AND AB | 01010101 | 10101010 | 00000000

## Slide 56: What About Subtraction: Negative Numbers
With 4 bits you can represent
  0 to +15
  -8 to + 7
    There are three ways to represent these negative numbers
Integer | Sign Magnitude | 1’s complement | 2’s complement
+7 | 0111 | 0111 | 0111
+6 | 0110 | 0110 | 0110
+5 | 0101 | 0101 | 0101
+4 | 0100 | 0100 | 0100
+3 | 0011 | 0011 | 0011
+2 | 0010 | 0010 | 0010
+1 | 0001 | 0001 | 0001
0 | 0000 | 0000 | 0000
-1 | 1001 | 1110 | 1111
-2 | 1010 | 1101 | 1110
-3 | 1011 | 1100 | 1101
-4 | 1100 | 1011 | 1100
-5 | 1101 | 1010 | 1011
-6 | 1110 | 1001 | 1010
-7 | 1111 | 1000 | 1001
-8 | 1000 (-0) | 11111 | 1000
Sign/Magnitude: Set the top bit to 1
1’s complement : Take the complement of the number
2’s complement : Take the complement of the number and then add 1

## Slide 57: What About Subtraction: Negative Numbers
There is a good reason to use a 2’s complement representation
  Binary addition of a two’s complement numbers just works whether the numbers are positive or negative
Exercise: Fill out the same table using sign magnitude numbers. Do you understand now why 2’s complement is a useful representation!
3 + 4 | 3 + -4 | -3 + 4 | -3 + -4
0011 | 0011 | 1101 | 1101
+ 0100 | + 1100 | + 0100 | + 1100
= 0111 | = 1111 | = 0001 | = 1001
(7) | (-1) | (+1) | (-7)

## Slide 58: 8 Bit representations
8 bits can be used to represent any 256 different symbols
The numbers 0-255
The numbers -128 to + 127
Part of a longer number
A Character
  Hence char in c
  This is a bit out of date
  Unicode uses 16 bits

## Slide 59: Back to our program
The program is stored in program memory
There are 64Kilobytes of program memory (2^16 bytes)
Each location stores an 8 bit number
The location is specified with a 16 bit Address
  (0x0000-0xFFFF)
000000be <main>:
be: 80 e0 ldi r24 0x00 ; 0
c0: 90 e0 ldi r25 0x00 ; 0
c2: 98 0f add r25 r24
c4: 92 bb out 0x18 r25 ; 18
c6: 82 bb out 0x18 r24 ; 18
c8: 8f 5f subi r24 0xFF ; 255
ca: 8a 30 cpi r24 0x0A ; 10
cc: d1 f7 brne .-12 ; 0xc2 <main+0x4>
ce: 80 e0 ldi r24 0x00 ; 0
d0: 90 e0 ldi r25 0x00 ; 0
d2: 08 95 ret
Address | Value
00BE | 80
00BF | E0
00C0 | 90
00C1 | E0
00C2 | 98
00C3 | 0F
00C4 | 92

## Slide 60: Registers on the AVR
AVR Registers – where the numerical work is done in a program
There are 32 General purpose registers on the AVR microprocessor (R0-R31)
Each of these can hold an 8 bit number
R26:R27 is also a 16 bit register called X
R28:R29 is Y
R30:R31 is Z
You can perform calculations on these registers very quickly

## Slide 61: Back to our program: Loading a register
000000be <main>:
be: 80 e0 ldi r24 0x00 ; 0
c0: 90 e0 ldi r25 0x00 ; 0
c2: 98 0f add r25 r24
c4: 92 bb out 0x18 r25 ; 18
c6: 82 bb out 0x18 r24 ; 18
c8: 8f 5f subi r24 0xFF ; 255
ca: 8a 30 cpi r24 0x0A ; 10
cc: d1 f7 brne .-12 ; 0xc2 <main+0x4>
ce: 80 e0 ldi r24 0x00 ; 0
d0: 90 e0 ldi r25 0x00 ; 0
d2: 08 95 ret
Address | Value
00BE | 80
00BF | E0
00C0 | 90
00C1 | E0
00C2 | 98
00C3 | 0F
00C4 | 92
The first instruction is loading a value of 0x00 into register r24
This instruction is encoded in the 16 bit opcode stored at address 00BE
The Assember code is
  ldi r240x00
  LoaD Immediate r24 with 0x00

## Slide 62: Decoding an Opcode
be: 80 e0 ldi r24 0x00
Words are stored little endian
Read into the processor as E080
E080=1110 0000 1000 0000
dddd: 1000=8 -> 16+8 = r24
KKKKKKKK=0x00
Exercise: what is the opcode for
ldi r19 0x3F

## Slide 63: Compare assembly language to c
000000be <main>:
be: 80 e0 ldi r24 0x00 ; 0
c0: 90 e0 ldi r25 0x00 ; 0
c2: 98 0f add r25 r24
c4: 92 bb out 0x18 r25 ; 18
c6: 82 bb out 0x18 r24 ; 18
c8: 8f 5f subi r24 0xFF ; 255
ca: 8a 30 cpi r24 0x0A ; 10
cc: d1 f7 brne .-12 ; 0xc2 <main+0x4>
ce: 80 e0 ldi r24 0x00 ; 0
d0: 90 e0 ldi r25 0x00 ; 0
d2: 08 95 ret
int main(void)
{
char i;
char j;
i=0;
j=0;
while (i<10) {
j = j + i;
PORTB = j;
PORTB = i;
i++;
}
return 0;
}
Here the variables are stored in registers r24 r25
Pretty easy to see how this program is translated
More complex programs quickly become very complicated to understand in assembly language
This is fetched by the MCU in reverse order
So reads E0 first
E0 identifies the byte as Command ldi with lsb 0
MCU then knows to get 80 as register 16+8 = 25 msb 0

## Slide 64: Back to our program: The rest
000000be <main>:
be: 80 e0 ldi r24 0x00 ; 0
c0: 90 e0 ldi r25 0x00 ; 0
c2: 98 0f add r25 r24
c4: 92 bb out 0x18 r25 ; 18
c6: 82 bb out 0x18 r24 ; 18
c8: 8f 5f subi r24 0xFF ; 255
ca: 8a 30 cpi r24 0x0A ; 10
cc: d1 f7 brne .-12 ; 0xc2 <main+0x4>
ce: 80 e0 ldi r24 0x00 ; 0
d0: 90 e0 ldi r25 0x00 ; 0
d2: 08 95 ret
The second instruction is loading a value of 0x00 into register r25
This adds r24 to r25 and stores the result into register r24
The next instructions output r24 and r25 (we’ll learn where later)
This is subtracting a value of 0xFF from register r24
This is the compiler cleverly adding 1
This instruction is comparing the value 0x0A to register r24
If they are not equal the next instruction will branch back to location 0xC2 that is loop back if they are equal it continues on (and returns from main)

## Slide 65: Arithmetic and Logic Instructions
Addition
  add r20r21
  R20  r20+r21
Increment
  inc r20
  R20  r20+1
Subtraction
  subi r20$22
  R20  r20-$22
  sub r20r21
  R20  r20-r21
Logic
  and r20r24
  R20  AND(r20r24)
Many instructions work either with two registers or with immediate data values (stored in the opcode)

## Slide 66: Arithmetic and Logic Instructions – The full set

## Slide 67: The Status Register
Every time the processor performs an operation it sets bits in the Status Register (SREG)
  Example cpi r01$77
  This register is in the I/O region
SREG can be examined/set with the in and out instructions
  in r17SREG
  out SREGr22
The status bits are also tested by branch instructions to decide whether or not to jump to a different location

## Slide 68: Branch Instructions
Branch
  breq label1
  Branch if equal to location label1
  brlo label2
  Branch if lower to location label2
  If the Branch test fails – the next line of code is executed
  If the Branch test is successful the program jumps to the location specified
Call Return
  rcall mysub
  ret
  Call subroutine mysub. The program saves information about where it currently is executing and then jumps to the code at mysub. When the subroutine is finished it calls ret which then returns to where the rcall was made.
Jump
  jmp label3
  Jump to label3 – no information about where we jumped from is saved. This is a one way trip

## Slide 69: All Branch Instructions

## Slide 70: Data Transfer Instructions
Load
  ldi r20$73
  R20  $73
  ld r20X
  R20  (X)
Copy Register
  mov r20r21
  R20  r21
Input
  in r20PIND
  R20  PIND
Output
  out PORTDr24
  PORTD  r24
There are a few quirks about loading and storing to memory. We will cover this in detail soon.

## Slide 71: Simulating Assembly
EdSIM – Simulation of an 8051 Processor

## Slide 72: Keypad Example
The following program shows how to scan the keypad. The program halts (to be precise, sits in an endless loop) once a key is pressed.
; While no key is pressed the program scans row0, row1, row2, row3 and back to row0, continuously. ; When a key is pressed the key number is placed in R0. ; For this program, the keys are numbered as: ; +----+----+----+ ; | 11 | 10 | 9 | row3 ; +----+----+----+ ; | 8 | 7 | 6 | row2 ; +----+----|----+ ; | 5 | 4 | 3 | row1 ; +----+----+----+ ; | 2 | 1 | 0 | row0 ; +----+----+----+ ; col2 col1 col0 ; The pressed key number will be stored in R0. Therefore, R0 is initially cleared. Each key is scanned, and if it is not pressed R0 is incremented. In that way, when the pressed key is found, R0 will contain the key's number.
The general purpose flag, F0, is used by the column-scan subroutine to indicate whether or not a pressed key was found in that column. If, after returning from colScan, F0 is set, this means the key was found.

## Slide 73: ADC Example
This program reads the analogue input ; voltage on the ADC and displays it on ; the scope via the DAC. ; A sample is taken from the ADC every 50 us ; This is achieved by setting timer 0 ; to interrupt the main program every 50 us. ; The timer 0 ISR then initiates an ADC ; conversion. ; When the conversion is complete the ; ADC interrupt line goes low. This line ; is interfaced with the 8051 external 0 ; interrupt line. The external 0 ISR ; therefore takes the reading from the ADC ; on P2 and passes it to the DAC on P1. ; Therefore, while the program is running, ; the scope voltage level should be the ; same as the ADC input voltage. ; However, when a change is made to the ; ADC input voltage it will take some time ; for the scope to update (ie: until the ; next timer 0 interrupt). ; Note: when running this program make sure ; the ADC is enabled (not the comparator).

## Slide 74: Realtime Evidence

## Slide 75: Realtime Evidence
In principle the real-time evidence is based on
1. evaluate the relevant characteristics of the technical process
  a. number of different requirements
  b. Minimum processing time for each request
  c. Minimum allowable response time for each request TZmin
  d. Maximum allowable response time for each request TZmax
  e. dependencies between events
2. identify the maximum processing time TVMax (WCET = Worst Case Execution Time) for each request
3. check the load condition (1.3)
4. verify the timeliness condition (determination of TRmin and TRmax).
With verifying the timeliness condition in particular it is not trivial to determine the maximum response time TRmax.

## Slide 76: Worst Case Execution Time
WCET is determined by measuring the time that a specific section of the code takes to run.
Each run measures the difference between t1 and t2 as TVmax . Subsequent runs overwrite TVmax if the latest result is greater.
TVmax = max(TVi)

## Slide 77: WCET – external measurement
Mesure Event and Response using port-toggle and an oscilloscope.
For a WCET measure appropriate input values and events must are generated.
In addition the entire system must be put under load (e.g. by an automatic tester).

## Slide 78: WCET – Pros and Cons
Advantages of the method:
  Independent of a programming language
  Relatively easy to implement
  Can run as autonomous self-diagnosis
Disadvantages of the method:
  The WCET of a code sequence can not be guaranteed after all it depends on many factors (background loop iterations caches branches etc ..).
  The measurement is WCET is time consuming and ultimately expensive. Measure out the piece of code needs to be theoretically charged with all input data (in any combination).
  This method can be carried out with the running code on the target platform only. Thus an assessment at an early stage of development can be difficult.
  A test environment is required (which provides the input data to create).
  The code sequence to be measured out must be modified (for storing time stamps)  timers.
  It is sometimes difficult to put the system under the required load.

## Slide 79: Static Code Analysis
Here the code itself is analyzed. Therefore most often object (machine) code is used so that the duration of each code sequences to be estimated. After that the number of loop iterations are considered a bound of the number of cycles is generated and using the clock frequency of the MCU the estimated execution time TSA is printed.
Under safety requirements code measured can not be changed after static code analysis.
As a safety margin factors of c = 2 3 sometimes are used to state an upper limit
tVmax ≤ TSA · c
A manual determination of the number of cycles can be done in simple cases by inspection of the C-compiler generated assembler code:

## Slide 80: Nassi-Shneiderman Charts

## Slide 81: Background
Nassi-Shneiderman (N-S) charts were initially developed in the early 1970’s by Ike Nassi and Ben Shneiderman
They are based on and perform a function similar to flowcharts
The initial purpose was to develop a technique to chart the logic design of structured programs
N-S Charts are also know as Program Structure Diagrams (PSD) and Chapin Charts.
Notes: But as we will see they have some distinct differences from flowcharts.
Not simply chart the structure of the data but also chart the logic behind the program.
What it did was help force programmers to design reliable and maintainable programs. Used BEFORE coding.

## Slide 82: Agenda
Overview
Primary Uses
Advantages
Disadvantages
Relationship with Other Techniques
Symbols
Examples
Resources/Tools
Group projects

## Slide 83: Overview
Nassi-Shneiderman charts have four primary uses:
  Creating the logic design
  Programming from the charts
  Writing program documentation
  Maintenance of the program
Notes: I will go into further detail about each of these used in the next 4 slides.

## Slide 84: 1. Creating the Logic Design
As mentioned previously this was the initial purpose of Nassi-Shneiderman charts
They can be thought of as the building blocks of the design
The completed chart is the blueprint for the program code
Notes: Think about your program as a building and having a good blueprint lays a good foundation on which to start your construction. The same is true with N-S charts.
We have heard in many other presentations how much time and money an organization can save if they just spend a little more time in the beginnings of the system development lifecycle. N-S charts are a great to fit into your requirements phase

## Slide 85: 2. Programming From the Charts
The N-S chart can be use to do the actual programming
It can be considered as a type of “pictorial” pseudocode
Some of the N-S editors convert the diagram directly into source code
Notes: A picture tells a thousand words…
We will look at screen shots for a couple editors later in the presentation
The source code might need some tweeking but it is a place to start

## Slide 86: 3. Writing Program Documentation
The N-S chart is a pictorial representation of the logical design of the program
Using the N-S chart as an actual part of the documentation is a great idea!
Notes: which makes it ideal for documenting the program
It can also be used for documenting procedures which is what the article I gave you talked about.
For a user, it is much easier to look at the N-S diagram then to just read documentation manuals.

## Slide 87: 4. Maintenance of the Program
N-S charts provide a quick reference to the structure and design of the program which helps during on-going maintenance and upgrades.
Notes: As mentioned, N-S charts are the blueprint for the program code. To go back to our building example, could you imagine adding a heating and cooling system to a building without using the blueprints?
Using one of the editors helps to keep the N-S diagram up to date

## Slide 88: Advantages - General
One main advantage is that N-S charts adopt the structured programming philosophy
N-S charts use only a few symbols which make them easier to learn then traditional flowcharts
They help to recognize missing policies or procedures from business rules
Completed charts should fit on one page, there are no complex arrows to follow
Notes: But even if you are doing object oriented design, Nassi-Shneiderman charts can be very helpful.
But they do require more forethought which makes the developer’s job a little harder in the beginning.
Again, the article touched on this issue. Basically N-S charts are so comprehensive that it is easy to recognize gaps in procedures.
No connectors to lead you astray…

## Slide 89: Advantages – General (cont.)
Have one entry point and one exit point
They can be nested to show complex procedures
N-S charts are independent of any specific programming language
Notes: Next I am going to talk about a few of the advantages specifically related to programming

## Slide 90: Advantages – Programming
The logic is documented in the N-S chart so regardless of the coding language used, N-S charts make coding much easier then starting from scratch
Clearly displays sequence, selection, and repetition (such as nested loops) to make debugging easier
Confusing “GOTOs” are not represented
Notes: Ever gotten stuck in an endless loop, NS charts clearly display where all of your loops are so it makes it easier to go to those lines of code

## Slide 91: Disadvantages
They can be difficult to draw
They can be harder to update or change then traditional flow charts because everything stays together
They must be comprehensive to be understood
Notes: When can developers really be comprehensive? Takes a lot of prep work which can sometimes make the client feel like nothing is getting done. But again, we have heard over and over again that it is worth the time, effort, and money to do the work in the beginning.
But to address these first two points, I will review a couple of editors that are available for drawing and updating N-S charts.

## Slide 92: Relationship with Other Techniques
Data Modeling
Entity Relation Diagram, I-graphs, Information Structure Diagram
A N-S can model operations on the objects/entities defined in a data model.
Process Modeling
Data Flow Diagram, A-graphs, Information Flow Diagram
Object Oriented
Object Diagram, OOA model, Object schema
N-S charts can be used as a further description of action or object.
State Modeling
State Transition, Petri-nets
N-S can be used as a representation of a transition by using conditions.
The activities/processes defined
in the process models can be further
described in detail in a N-S chart
A N-S chart can also be used as a
translation of process model
Kind of Technique
Example Technique
Relation
wwwis.cs.utwente.nl
Notes: Here is an interesting table. It shows the relationship of N-S charts with other system development techniques.

## Slide 93: Symbols
Only 3 basic symbols used in N-S charts
  Process (Sequence)
  Decision (Selection)
  Iteration (Repetition)
Other symbols are used but they are based on these three symbols
Notes: Which is true in structured programming: Sequence, Selection, and Repetition

## Slide 94: Process
A stackable box is used to represent a sequence or process
Step 1
Step 2
Step 3
Notes: Easy enough. Do one thing then do the next thing.

## Slide 95: Decision (Selection)
The “if-then-else”
If…
(then)
(else)
Notes: If the first condition is true, do everything below the TRUE. If the first condition is not true then do everything below the FALSE

## Slide 96: Decision (Selection)
The case/switch/selection statement
Notes: If your criteria meets 1, do 1. If it meets 2, do 2

## Slide 97: Iteration
These symbols show loops
While
Repeat Until
Notes: The while loop is a “test your condition before entering the loop”
The repeat until is a “test your condition as you are exiting the loop”
Now we are going to move on to some examples of completed N-S diagrams. First an easy diagram that you really don’t even need to know how to read these charts to figure out.

## Slide 98: Graduation Example N-S Chart
Notes: I know this was in your reading but I thought we could look at it as an example of a really easy Nassi-Shneiderman chart.
Because I have mentioned before how N-S diagrams can be thought of as pictorial pseudocode, lets look at the pseudocode for the same example.

## Slide 99: Graduation Example Pseudocode
While “FOR ALL SECOND-YEAR STUDENTS” do
if “ENOUGH CREDITS? then “YES”:
if “BILLS PAID?” then “YES”:
“GRANT DIPLOMA”
else “NO”:
“NO DIPLOMA”
end if
else “NO”:
“NO DIPLOMA”
end if
end while
Notes: One thing that I think makes this harder to read is that you have to go all the way down before you can find what applies to you. You need to look at all of the nested layers before you find what you need.

## Slide 100: Newspaper Subscription N-S Chart
Notes: This was the first Nassi-Shneiderman chart I saw. My first thought was “oh great, what have I gotten myself into now…”
But then I learned about the symbols and this chart became amazingly easy to read. Walk through the chart
Now I am going to show you the pseudocode for this same program

## Slide 101: Newspaper Subscription Pseudocode
Notes: Which one do you think is easier to read?
The N-S chart is much easier to read, in part because you can go directly to the area in question. For example if you want to know what to do about cancellations, you can go directly there without having to read through all this pseudocode

## Slide 102: Drawing “Hints”
The size of the final rectangle has no bearing on the program
Fit one drawing to a page
They work the best with small or medium-sized programs
Draw the major loops first, complete the inner loops later
Notes: This is basically true for structured programming. Start with the outer loops before working on the inner loops.

## Slide 103: Drawing “Hints”
Nested loops are indented, of course as the number of nested loops increase, the width of the chart changes
Sub-procedures can be drawn using a different N-S chart
If the N-S diagram is cluttered it may be the policy you are diagramming is unclear
Notes: This is basically true for structured programming. Start with the outer loops before working on the inner loops.
You can always identify a sub-task as being diagrammed on another N-S chart.
“Remember: Clean documentation can not change messy systems”

## Slide 104: User Comments
The University of Liverpool develop a N-S editor using a VAX based Pascal complier called NSEDIT
User responses:
  60% agreed that it helped to ensure the correct syntax
  21% said it enforced structured programming
  12% felt it made the transition from design to code easier
Notes: I am not going to go into the details about their program, rather I am reporting on the comments that I thought applied to Nassi-Shneiderman charts in general
They surveyed 53 of their 3rd year and beyond Software Engineering students about NSEDIT
The negative comments were primarily related to the NSEDIT editor, and not the N-S charts. The most prevalent negative comment was 43% felt the nested boxes got too narrow which hindered comprehension. This is related to the NSEDIT but I could see how it would be applicable to N-S charts in general.
In general they thought N-S charts are particularly helpful for novice programmers

## Slide 105: Editor Downloads/Tools
Microsoft Visio 2000 supports N-S charts
Latex Struktex Package
Notes: Here is a web page for a N-S editor for Unix. You can see that the price is relatively cheap.
I didn’t look at the Unix Editor since I don’t have a Unix box.
I did use MS Visio for N-S charts. To be honest with you, I didn’t like Visio that much but…

## Slide 106: Visio Screen Shot
Notes: I know this example is hard to see but here is a screen shot from Microsoft Visio of the Nassi-Shneiderman drawing tool.
You can see that it has all of the standard navigation tools and toolbars as any other Microsoft product.
It was relatively easy to use, but it was obvious that the StruktoGraff editor was more clearly devoted to N-S diagrams. Visio didn’t seem to have as many of the features, but… Visio also has other tools that you may use.

## Slide 107: MS Visio Example
Notes: Here is an example of a Visio N-S diagram.

## Slide 108: Summary
We have seen some of the advantages and disadvantages of using Nassi-Shneiderman charts
I think you can clearly see the benefits to using N-S charts for system design as well as documentation and maintenance
Notes: Advantages: ease of programming, finding “holes” in procedures, easy to read and develop documentation
Disadvantages: difficult to update and draw, must know the entire process to be complete

## Slide 109: References
Beek, Marcel, Koolen, Hans, Van Setten, Mark: (1996), “Program Structure Diagrams”, (visited 3/18/01), wwwis.cs.utwente.nl:8080/dmrg/mee/misop.htm
Cary, David (2000): “Nassi-Shneiderman on the Web”, (visited 3/18/01), www.rdrop.com/~cary/html/psd.html
Coenen, Frans: “Comp101 – Design and Style Review”, (visited 3/6/01), www.csc.liv.ac.uk/~frans/comp101/week9/designAndStyle.htm.
Halewood, K. and Woodward M.R.: (1988), “NSEDIT: A Syntax-directed Editor and Testing Tool based on Nassi-Shneiderman Charts”, Software-Practice and Experience, Vol. 18, No.10, pp. 987-998
Juch, Forschungszentrum: (1997) “Nassi Tutorial”,(visited 3/12/01), www.kfa-juelich.de/zam/nassi/tutorial.html
Kendall, Kenneth E. and Kendall, Julie E.: (1999) System Analysis and Design, Prentice Hall, New Jersey
Notes: I also included a section for tutorial downloads. TESTING ????

## Slide 110: References (cont.)
Seesing, Paul R.: (1993), “Basic System Analysis Tools for Computer Users”, (visited 4/9/01), www.open.org/~prslkg/sy_chap.htm
Tiemann, Peter: “Nassi-Shneiderman Charts”, (visited 4/9/01), www.preview.org/software/sc_help/nassishneiderman
“Why Should I Use Structograms?”: (visited 4/9/01), www.blue-river-software.com/products/whystructs.htm
Weiss, Edmond H.: (1990). “Visualizing a Procedure with Nassi-Schneiderman Charts”, Journal of Technical Writing and Communication, Vol. 20, No.3, pp. 237-254
Woodward, M.R.: (1987) “The Use of Nassi-Shneiderman Charts and Supporting Tools in Software Engineering Education”, Computer Education, Vol. 11, No. 4, pp. 267-279

## Slide 111: Simple Scheduling
Sans operating system

## Slide 112: Realtime requirements
A real-time scheduler must divide all ready (runnable) tasks to the processor so that all all time conditions are met. The set of tasks managed by the real-time scheduler is called taskset.
For the evaluation of various scheduling strategies the processor demand H (=utilization) is an important quantity for the load of the processor it is defined as
Each CPU can be utilized up to 100 % at maximum.

## Slide 113: Tasks and Deadlines
Example: A periodic task 1 with a period of TP1 = 200 ms and an execution time of Te1 = 100 ms causes a processor demand of H1 = 50 %
t
TP1
Task 1
A second periodic task with a period of TP2 = 100 ms and an execution time of Te2 = 50 ms also causes a processor demand of H2 = 50 %.
t
TP2
Task 2
An implicit timing condition for each periodic task is: task execution must be finished before the next period starts (deadline) !
t
TP2
2
1
2
1
2
1
2
Task 2 deadline
Task 12 deadline
Both tasks cause a total processor demand H = H1 + H2 = 100 %.

## Slide 114: Tasks and Deadlines continued
t
2
1
2
1
blocked
running
ready
Task 1
2
1
2
Task 2
Task 2 deadline
Task 12 deadline
One possible schedule for executing both tasks is to displace task 1 after exactly half of its execution time by task 2 which is never displaced. Thus task 1 must be displaceable.

## Slide 115: Scheduling without OS
No OS functions there for task management
Task management has to be implemented manually
Time Slice Scheduling

## Slide 116: Time-Slice-Scheduling Example
Example 1: 3 Tasks with Hmax < 0.778:
Task T1: period Tp1 = 10 ms execution time Te1 = 1 ms with H1 = 0.1
Task T2: period Tp2 = 10 ms execution time Te2 = 5 ms with H2 = 0.5
Task T3: non-periodic period Tp3 = deadline Td3 = 15.4 ms Te3 = 2.62 ms with H3 = 0.17
By (2.2) the total CPU utilization H = 0.1 + 0.5 + 0.17 = 0.77
One chooses a basic time-slice TTS = 1 ms and assigns individual time slices as multiples of TTS with ΣTTS = 9 ms:
Task T1: TTS1 = 1 TTS = 1 ms H1 = TTS1/ΣTTS = 1 ms / 9 ms = 11 %
Task T2: TTS2 = 5 TTS = 5 ms H2 = TTS2/ΣTTS = 5 ms / 9 ms = 55 %
Task T3: TTS3 = 3 TTS = 3 ms H3 = TTS3/ΣTTS = 3 ms / 9 ms = 33 %

## Slide 117: Fixed-Time-Slice Schedule
FT scheduling is based on a TDMA approach requires no priorities and is therefore frequently used in embedded microcontroller applications without an operating system.
A strictly periodic schedule is created with a periodic time N·TTS i.e. with N integer multiples of the basic TTS time slice. Each task gets assigned one (ore more) basic time slots large enough to hold the WCET of each
Conditions for Events are polled within each task if a task is not finished at the end of its timeslice it can be preempted (preemptive FTS) or not (cooperative FTS).

## Slide 118: FTS Example
The previous example with three tasks and an idle task T4 at a period N∙TTS = ΣTTS = 10 ms is realized the time slices are chosen as multiples of TTS = 1 ms as follows
  Task T1: TTS1 = 1 TTS = 1 ms  H1 = TTS1/ΣTTS = 1 ms / 10 ms = 10 %
  Task T2: TTS2 = 5 TTS = 5 ms  H2 = TTS2/ΣTTS = 5 ms / 10 ms = 50 %
  Task T3: TTS3 = 3 TTS = 3 ms  H3 = TTS3/2ΣTTS = 3 ms / 10 ms = 30 %
  Task T4 (idle) TTS4 = 1 TTS = 1 ms  H4 = 10 %
  T3 runs for the second time at t = 26 ms the delay of 10 ms does not result in a T3-deadline violation. The idle task T4 provides a placeholder for unused CPU load which can be used in modern CPUs for power saving features

## Slide 119: Code Example
// ---------------------------------------------------
// the fixed time-slice scheduler
// ---------------------------------------------------
void tSlice_schedule (void)
{
if (MOD2(1 T_ts) == 1) { // ( T_ts & 1 ) {
// timeslice 2^1 = 2: (T_Ts % 2^N) == 2^(N-1) = 135 ...
// TODO ... }
else if (MOD2(10 T_ts) == 512) { //( ( T_ts & 0x3FF ) == 512 ) {
// timeslice 2^10 = 1024: (T_Ts % 2^N) == 2^(N-1) = 512 1036 2060 ...
// TODO ... }
T_ts++ ; // Tick counter increment
return ;
}
// ---------------------------------------------------
// timer 0 compare interrupt
// ---------------------------------------------------
ISR ( TIMER0_COMP_vect )
{
tSlice_schedule ();
}

## Slide 120: Simulation
https://www.tinkercad.com/dashboard?type=circuits&collection=designs
Go to www.tinkercad.com
Click on Klasse beitreten
Enter the Classcode ALRAII7KC858
Enter your nickname

## Slide 121: FreeRTOS

## Slide 122: FreeRTOS
FreeRTOS is a real-time kernel/scheduler on top of which MCU applications can be built to meet their hard real-time requirements.
  Allows MCU applications be organized as a collection of independent threads of execution.
  Decides which thread should be executed by examining the priority assigned to each thread.
    Assume a single core MCU where only a single thread can be executing at one time.

## Slide 123: The simplest case of task priority assignments
Assign higher priorities (lower priorities) to threads that implement hard real-time (soft real-time) requirements
  As a result hard real-time threads are always executed ahead of soft real-time threads.
But priority assignment decision are not always that simple.
In general task prioritization can help ensure an application meet its processing deadline.

## Slide 124: Why use a real-time kernel
For a simple system many well-established techniques can provide an appropriate solution without the use of a kernel.
For a more complex embedded application a kernel would be preferable.
But where the crossover point occurs will always be subjective.
Besides ensuring an application meets its processing deadline a kernel can bring other less obvious benefits.

## Slide 125: Benefits of using real-time kernel 1
Abstracting away timing information
  Kernel is responsible for execution timing and provides a time-related API to the application. This allows the application code to be simpler and the overall code size be smaller.
Maintainability/Extensibility
  Abstracting away timing details results in fewer interdependencies between modules and allows sw to evolve in a predictable way.
  Application performance is less susceptible to changes in the underlying hardware.
Modularity
  Tasks are independent modules each of which has a well-defined purpose.
Team development
  Tasks have well-defined interfaces allowing easier development by teams

## Slide 126: Benefits of using real-time kernel 2
Easier testing
  Tasks are independent modules with clean interfaces they can be tested in isolation.
Idle time utilization
  The idle task is created automatically when the kernel is started. It executes whenever there are no application tasks to run.
  Be used to measure spare processing capacity perform background checks or simply place the process into a low-power mode.
Flexible interrupt handling
  Interrupt handlers can be kept very short by deferring most of the required processing to handler tasks.

## Slide 127: Standard FreeRTOS features
Pre-emptive or co-operative operation
Very flexible task priority assignment
Queues
Binary/Counting / Recursive semaphores
Mutexes
Tick/Idle hook functions
Stack overflow checking
Trace hook macros
Interrupt nesting

## Slide 128: FreeRTOS
Architecture

## Slide 129: FreeRTOS – RT and Embedded
"Embedded" and "real-time" can mean different things to different people, so let's define them as FreeRTOS uses them.
An embedded system is a computer system that is designed to do only a few things, like the system in a TV remote control, in-car GPS, digital watch, or pacemaker. Embedded systems are typically smaller and slower than general purpose computer systems, and are also usually less expensive. A typical low-end embedded system may have an 8-bit CPU running at 25MHz, a few KB of RAM, and maybe 32KB of flash memory. A higher-end embedded system may have a 32-bit CPU running at 750MHz, a GB of RAM, and multiple GB of flash memory.
Real-time systems are designed to do something within a certain amount of time; they guarantee that stuff happens when it's supposed to.
A pacemaker is an excellent example of a real-time embedded system. A pacemaker must contract the heart muscle at the right time to keep you alive; it can't be too busy to respond in time. Pacemakers and other real-time embedded systems are carefully designed to run their tasks on time, every time.

## Slide 130: Architecture
FreeRTOS is a relatively small application. The minimum core of FreeRTOS is only three source (.c) files and a handful of header files, totalling just under 9000 lines of code, including comments and blank lines. A typical binary code image is less than 10KB.
FreeRTOS's code breaks down into three main areas: tasks, communication, and hardware interfacing.
Tasks: Almost half of FreeRTOS's core code deals with the central concern in many operating systems: tasks. A task is a user-defined C function with a given priority. tasks.c and task.h do all the heavy lifting for creating, scheduling, and maintaining tasks.
Communication: Tasks are good, but tasks that can communicate with each other are even better! Which brings us to the second FreeRTOS job: communication. About 40% of FreeRTOS's core code deals with communication. queue.c and queue.h handle FreeRTOS communication. Tasks and interrupts use queues to send data to each other and to signal the use of critical resources using semaphores and mutexes.
The Hardware Whisperer: The approximately 9000 lines of code that make up the base of FreeRTOS are hardware-independent; the same code runs whether FreeRTOS is running on the humble 8051 or the newest, shiniest ARM core. About 6% of FreeRTOS's core code acts a shim between the hardware-independent FreeRTOS core and the hardware-dependent code. We'll discuss the hardware-dependent code in the next section.

## Slide 131: Hardware Considerations
The hardware-independent FreeRTOS layer sits on top of a hardware-dependent layer. This hardware-dependent layer knows how to talk to whatever chip architecture you choose.

## Slide 132: Configurations
Configuration options are selected in FreeRTOSConfig.h by setting various #defines. Clock speed, heap size, mutexes, and API subsets are all configurable in this file, along with many other options. Here are a few examples that set the maximum number of task priority levels, the CPU frequency, the system tick frequency, the minimal stack size and the total heap size:
#define configMAX_PRIORITIES ( ( unsigned portBASE_TYPE ) 5 )
#define configCPU_CLOCK_HZ ( 12000000UL )
#define configTICK_RATE_HZ ( ( portTickType ) 1000 )
#define configMINIMAL_STACK_SIZE ( ( unsigned short ) 100 )
#define configTOTAL_HEAP_SIZE ( ( size_t ) ( 4 * 1024 ) )

## Slide 133: Hardware Dependency
Hardware-dependent code lives in separate files for each compiler toolchain and CPU architecture.
For example, if you're working with the IAR compiler on an ARM Cortex-M3 chip, the hardware-dependent code lives in the FreeRTOS/Source/portable/IAR/ARM_CM3/ directory.
portmacro.h declares all of the hardware-specific functions, while port.c and portasm.s contain all of the actual hardware-dependent code.
The hardware-independent header file portable.h #include's the correct portmacro.h file at compile time. FreeRTOS calls the hardware-specific functions using #define'd functions declared in portmacro.h.

## Slide 134: Example
Let's look at an example of how FreeRTOS calls a hardware-dependent function. The hardware-independent file tasks.c frequently needs to enter a critical section of code to prevent preemption. Entering a critical section happens differently on different architectures, and the hardware-independent tasks.c does not want to have to understand the hardware-dependent details.
So tasks.c calls the global macro portENTER_CRITICAL(), glad to be ignorant of how it actually works.
Assuming we're using the IAR compiler on an ARM Cortex-M3 chip, FreeRTOS is built with the file
FreeRTOS/Source/portable/IAR/ARM_CM3/portmacro.h which defines portENTER_CRITICAL() like this:
#define portENTER_CRITICAL() vPortEnterCritical()

## Slide 135: Example 2
vPortEnterCritical() is actually defined in FreeRTOS/Source/portable/IAR/ARM_CM3/port.c. The port.c file is hardware-dependent, and contains code that understands the IAR compiler and the Cortex-M3 chip. vPortEnterCritical() enters the critical section using this hardware-specific knowledge and returns to the hardware-independent tasks.c.
The portmacro.h file also defines an architecture's basic data types. Data types for basic integer variables, pointers, and the system timer tick data type are defined like this for the IAR compiler on ARM Cortex-M3 chips:
#define portBASE_TYPE long // Basic integer variable type
#define portSTACK_TYPE unsigned long // Pointers to memory locations
typedef unsigned portLONG portTickType; // The system timer tick type

## Slide 136: Example 3
This method of using data types and functions through thin layers of #defines may seem a bit complicated, but it allows FreeRTOS to be recompiled for a completely different system architecture by changing only the hardware-dependent files. And if you want to run FreeRTOS on an architecture it doesn't currently support, you only have to implement the hardware-dependent functionality which is much smaller than the hardware-independent part of FreeRTOS.
As we've seen, FreeRTOS implements hardware-dependent functionality with C preprocessor #define macros. FreeRTOS also uses #define for plenty of hardware-independent code. For non-embedded applications this frequent use of #define is a cardinal sin, but in many smaller embedded systems the overhead for calling a function is not worth the advantages that "real" functions offer.

## Slide 137: Full task state machine

## Slide 138: Scheduling Tasks – Ready List

## Slide 139: Tasks – Task Control Block in tasks.c
typedef struct tskTaskControlBlock
{
volatile portSTACK_TYPE *pxTopOfStack; /* Points to the location of
the last item placed on
the tasks stack. THIS
MUST BE THE FIRST MEMBER
OF THE STRUCT. */
xListItem xGenericListItem; /* List item used to place
the TCB in ready and
blocked queues. */
xListItem xEventListItem; /* List item used to place
the TCB in event lists.*/
unsigned portBASE_TYPE uxPriority; /* The priority of the task
where 0 is the lowest
priority. */
portSTACK_TYPE *pxStack; /* Points to the start of
the stack. */
signed char pcTaskName[ configMAX_TASK_NAME_LEN ]; /* Descriptive name given
to the task when created.
Facilitates debugging
only. */
#if ( portSTACK_GROWTH > 0 )
portSTACK_TYPE *pxEndOfStack; /* Used for stack overflow
checking on architectures
where the stack grows up
from low memory. */
#endif
#if ( configUSE_MUTEXES == 1 )
unsigned portBASE_TYPE uxBasePriority; /* The priority last
assigned to the task -
used by the priority
inheritance mechanism. */
#endif
} tskTCB;

## Slide 140: Lists

## Slide 141: Scheduling Tasks – Priorities and Ready List
Each task has a user-assigned priority between 0 (the lowest priority) and the compile-time value of configMAX_PRIORITIES-1 (the highest priority). For instance, if configMAX_PRIORITIES is set to 5, then FreeRTOS will use 5 priority levels: 0 (lowest priority), 1, 2, 3, and 4 (highest priority).
FreeRTOS uses a "ready list" to keep track of all tasks that are currently ready to run. It implements the ready list as an array of task lists like this:
static xList pxReadyTasksLists[ configMAX_PRIORITIES ]; /* Prioritised ready tasks. */
pxReadyTasksLists[0] is a list of all ready priority 0 tasks, pxReadyTasksLists[1] is a list of all ready priority 1 tasks, and so on, all the way up to pxReadyTasksLists[configMAX_PRIORITIES-1].

## Slide 142: Scheduling Tasks – System Tick
The heartbeat of a FreeRTOS system is called the system tick. FreeRTOS configures the system to generate a periodic tick interrupt. The user can configure the tick interrupt frequency, which is typically in the millisecond range. Every time the tick interrupt fires, the vTaskSwitchContext() function is called. vTaskSwitchContext() selects the highest-priority ready task and puts it in the pxCurrentTCB variable like this:
/* Find the highest-priority queue that contains ready tasks. */
while( listLIST_IS_EMPTY( &( pxReadyTasksLists[ uxTopReadyPriority ] ) ) )
{
configASSERT( uxTopReadyPriority );
--uxTopReadyPriority;
}
/* listGET_OWNER_OF_NEXT_ENTRY walks through the list, so the tasks of the same
priority get an equal share of the processor time. */
listGET_OWNER_OF_NEXT_ENTRY( pxCurrentTCB, &( pxReadyTasksLists[ uxTopReadyPriority ] ) );

## Slide 143: Scheduling Tasks – Ready List
Before the while loop starts, uxTopReadyPriority is guaranteed to be greater than or equal to the priority of the highest-priority ready task. The while() loop starts at priority level uxTopReadyPriority and walks down through the pxReadyTasksLists[] array to find the highest-priority level with ready tasks. listGET_OWNER_OF_NEXT_ENTRY() then grabs the next ready task from that priority level's ready list.
Now pxCurrentTCB points to the highest-priority task, and when vTaskSwitchContext() returns the hardware-dependent code starts running that task.
Those nine lines of code are the absolute heart of FreeRTOS. The other 8900+ lines of FreeRTOS are there to make sure those nine lines are all that's needed to keep the highest-priority task running.

## Slide 144: Schuling Tasks – Ready List

## Slide 145: Tasks – Task Control Block in tasks.c
typedef struct tskTaskControlBlock
{
volatile portSTACK_TYPE *pxTopOfStack; /* Points to the location of
the last item placed on
the tasks stack. THIS
MUST BE THE FIRST MEMBER
OF THE STRUCT. */
xListItem xGenericListItem; /* List item used to place
the TCB in ready and
blocked queues. */
xListItem xEventListItem; /* List item used to place
the TCB in event lists.*/
unsigned portBASE_TYPE uxPriority; /* The priority of the task
where 0 is the lowest
priority. */
portSTACK_TYPE *pxStack; /* Points to the start of
the stack. */
signed char pcTaskName[ configMAX_TASK_NAME_LEN ]; /* Descriptive name given
to the task when created.
Facilitates debugging
only. */
#if ( portSTACK_GROWTH > 0 )
portSTACK_TYPE *pxEndOfStack; /* Used for stack overflow
checking on architectures
where the stack grows up
from low memory. */
#endif
#if ( configUSE_MUTEXES == 1 )
unsigned portBASE_TYPE uxBasePriority; /* The priority last
assigned to the task -
used by the priority
inheritance mechanism. */
#endif
} tskTCB;

## Slide 146: Tasks - TCB
The TCB stores the address of the stack start address in pxStack and the current top of stack in pxTopOfStack. It also stores a pointer to the end of the stack in pxEndOfStack to check for stack overflow if the stack grows "up" to higher addresses. If the stack grows "down" to lower addresses then stack overflow is checked by comparing the current top of stack against the start of stack memory in pxStack.
The TCB stores the initial priority of the task in uxPriority and uxBasePriority. A task is given a priority when it is created, and a task's priority can be changed. If FreeRTOS implements priority inheritance then it uses uxBasePriority to remember the original priority while the task is temporarily elevated to the "inherited" priority. (See the discussion about mutexes below for more on priority inheritance.)
Each task has two list items for use in FreeRTOS's various scheduling lists. When a task is inserted into a list FreeRTOS doesn't insert a pointer directly to the TCB. Instead, it inserts a pointer to either the TCB's xGenericListItem or xEventListItem. These xListItem variables let the FreeRTOS lists be smarter than if they merely held a pointer to the TCB. We'll see an example of this when we discuss lists later.
A task can be in one of four states: running, ready to run, suspended, or blocked. You might expect each task to have a variable that tells FreeRTOS what state it's in, but it doesn't. Instead, FreeRTOS tracks task state implicitly by putting tasks in the appropriate list: ready list, suspended list, etc. The presence of a task in a particular list indicates the task's state. As a task changes from one state to another, FreeRTOS simply moves it from one list to another.

## Slide 147: Tasks Setup
We've already touched on how a task is selected and scheduled with the pxReadyTasksLists array; now let's look at how a task is initially created. A task is created when the xTaskCreate() function is called. FreeRTOS uses a newly allocated TCB object to store the name, priority, and other details for a task, then allocates the amount of stack the user requests (assuming there's enough memory available) and remembers the start of the stack memory in TCB's pxStack member.
The stack is initialized to look as if the new task is already running and was interrupted by a context switch. This way the scheduler can treat newly created tasks exactly the same way as it treats tasks that have been running for a while; the scheduler doesn't need any special case code for handling new tasks.
The way that a task's stack is made to look like it was interrupted by a context switch depends on the architecture FreeRTOS is running on, but this ARM Cortex-M3 processor's implementation is a good example:

## Slide 148: Tasks - Stack
unsigned int *pxPortInitialiseStack( unsigned int *pxTopOfStack,
pdTASK_CODE pxCode,
void *pvParameters )
{
/* Simulate the stack frame as it would be created by a context switch interrupt. */
pxTopOfStack--; /* Offset added to account for the way the MCU uses the stack on
entry/exit of interrupts. */
*pxTopOfStack = portINITIAL_XPSR; /* xPSR */
pxTopOfStack--;
*pxTopOfStack = ( portSTACK_TYPE ) pxCode; /* PC */
pxTopOfStack--;
*pxTopOfStack = 0; /* LR */
pxTopOfStack -= 5; /* R12, R3, R2 and R1. */
*pxTopOfStack = ( portSTACK_TYPE ) pvParameters; /* R0 */
pxTopOfStack -= 8; /* R11, R10, R9, R8, R7, R6, R5 and R4. */
return pxTopOfStack;
}

## Slide 149: Tasks - Stack
The ARM Cortex-M3 processor pushes registers on the stack when a task is interrupted. pxPortInitialiseStack() modifies the stack to look like the registers were pushed even though the task hasn't actually started running yet. Known values are stored to the stack for the ARM registers xPSR, PC, LR, and R0. The remaining registers R1 -- R12 get stack space allocated for them by decrementing the top of stack pointer, but no specific data is stored in the stack for those registers. The ARM architecture says that those registers are undefined at reset, so a (non-buggy) program will not rely on a known value.
After the stack is prepared, the task is almost ready to run. First though, FreeRTOS disables interrupts: We're about to start mucking with the ready lists and other scheduler structures and we don't want anyone else changing them underneath us.
If this is the first task to ever be created, FreeRTOS initializes the scheduler's task lists. FreeRTOS's scheduler has an array of ready lists, pxReadyTasksLists[], which has one ready list for each possible priority level. FreeRTOS also has a few other lists for tracking tasks that have been suspended, killed, and delayed. These are all initialized now as well.
After any first-time initialization is done, the new task is added to the ready list at its specified priority level. Interrupts are re-enabled and new task creation is complete.

## Slide 150: Lists

## Slide 151: Lists
The FreeRTOS list is a standard circular doubly linked list with a couple of interesting additions. Here's a list element:
struct xLIST_ITEM
{
portTickType xItemValue; /* The value being listed. In most cases
this is used to sort the list in
descending order. */
volatile struct xLIST_ITEM * pxNext; /* Pointer to the next xListItem in the
list. */
volatile struct xLIST_ITEM * pxPrevious; /* Pointer to the previous xListItem in
the list. */
void * pvOwner; /* Pointer to the object (normally a TCB)
that contains the list item. There is
therefore a two-way link between the
object containing the list item and
the list item itself. */
void * pvContainer; /* Pointer to the list in which this list
item is placed (if any). */
};

## Slide 152: Lists
Each list element holds a number, xItemValue, that is the usually the priority of the task being tracked or a timer value for event scheduling. Lists are kept in high-to-low priority order, meaning that the highest-priority xItemValue (the largest number) is at the front of the list and the lowest priority xItemValue (the smallest number) is at the end of the list.
The pxNext and pxPrevious pointers are standard linked list pointers. pvOwner is a pointer to the owner of the list element. This is usually a pointer to a task's TCB object. pvOwner is used to make task switching fast in vTaskSwitchContext(): once the highest-priority task's list element is found in pxReadyTasksLists[], that list element's pvOwner pointer leads us directly to the TCB needed to schedule the task.
pvContainer points to the list that this item is in. It is used to quickly determine if a list item is in a particular list. Each list element can be put in a list, which is defined as:
typedef struct xLIST
{
volatile unsigned portBASE_TYPE uxNumberOfItems;
volatile xListItem * pxIndex; /* Used to walk through the list. Points to
the last item returned by a call to
pvListGetOwnerOfNextEntry (). */
volatile xMiniListItem xListEnd; /* List item that contains the maximum
possible item value, meaning it is always
at the end of the list and is therefore
used as a marker. */
} xList;

## Slide 153: Lists
The size of a list at any time is stored in uxNumberOfItems, for fast list-size operations. All new lists are initialized to contain a single element: the xListEnd element. xListEnd.xItemValue is a sentinel value which is equal to the largest value for the xItemValue variable: 0xffff when portTickType is a 16-bit value and 0xffffffff when portTickType is a 32-bit value. Other list elements may also have the same value; the insertion algorithm ensures that xListEnd is always the last item in the list.
Since lists are sorted high-to-low, the xListEnd element is used as a marker for the start of the list. And since the list is circular, this xListEnd element is also a marker for the end of the list.
Most "traditional" list accesses you've used probably do all of their work within a single for() loop or function call like this:
for (listPtr = listStart; listPtr != NULL; listPtr = listPtr->next) {
// Do something with listPtr here...
}
FreeRTOS frequently needs to access a list across multiple for() and while() loops as well as function calls, and so it uses list functions that manipulate the pxIndex pointer to walk the list. The list function listGET_OWNER_OF_NEXT_ENTRY() does pxIndex = pxIndex->pxNext; and returns pxIndex. (Of course it does the proper end-of-list-wraparound detection too.) This way the list itself is responsible for keeping track of "where you are" while walking it using pxIndex, allowing the rest of FreeRTOS to not worry about it.

## Slide 154: Lists

## Slide 155: Lists
The pxReadyTasksLists[] list manipulation done in vTaskSwitchContext() is a good example of how pxIndex is used. Let's assume we have only one priority level, priority 0, and there are three tasks at that priority level. This is similar to the basic ready list picture we looked at earlier, but this time we'll include all of the data structures and fields.
As you can see in Figure 3.3, pxCurrentTCB indicates that we're currently running Task B. The next time vTaskSwitchContext() runs, it calls listGET_OWNER_OF_NEXT_ENTRY() to get the next task to run. This function uses pxIndex->pxNext to figure out the next task is Task C, and now pxIndex points to Task C's list element and pxCurrentTCB points to Task C's TCB, as shown in Figure 3.4.
Note that each struct xListItem object is actually the xGenericListItem object from the associated TCB.

## Slide 156: Queues
FreeRTOS allows tasks to communicate and synchronize with each other using queues.
Interrupt service routines (ISRs) also use queues for communication and synchronization.
The basic queue data structure is:
typedef struct QueueDefinition
{
signed char *pcHead; /* Points to the beginning of the queue storage area. */
signed char *pcTail; /* Points to the byte at the end of the
queue storage area. One more byte is
allocated than necessary to store the
queue items; this is used as a marker. */
signed char *pcWriteTo; /* Points to the free next place in the
storage area. */
signed char *pcReadFrom; /* Points to the last place that a queued
item was read from. */
xList xTasksWaitingToSend; /* List of tasks that are blocked waiting
to post onto this queue. Stored in
priority order. */
xList xTasksWaitingToReceive; /* List of tasks that are blocked waiting
to read from this queue. Stored in
priority order. */
volatile unsigned portBASE_TYPE uxMessagesWaiting; /* The number of items currently
in the queue. */
unsigned portBASE_TYPE uxLength; /* The length of the queue
defined as the number of
items it will hold, not the
number of bytes. */
unsigned portBASE_TYPE uxItemSize; /* The size of each items that
the queue will hold. */
} xQUEUE;

## Slide 157: Queues
This is a fairly standard queue with head and tail pointers, as well as pointers to keep track of where we've just read from and written to.
When creating a queue, the user specifies the length of the queue and the size of each item to be tracked by the queue. pcHead and pcTail are used to keep track of the queue's internal storage. Adding an item into a queue does a deep copy of the item into the queue's internal storage.
FreeRTOS makes a deep copy instead of storing a pointer to the item because the lifetime of the item inserted may be much shorter than the lifetime of the queue. For instance, consider a queue of simple integers inserted and removed using local variables across several function calls. If the queue stored pointers to the integers' local variables, the pointers would be invalid as soon as the integers' local variables went out of scope and the local variables' memory was used for some new value.
The user chooses what to queue. The user can queue copies of items if the items are small, like in the simple integer example in the previous paragraph, or the user can queue pointers to the items if the items are large. Note that in both cases FreeRTOS does a deep copy: if the user chooses to queue copies of items then the queue stores a deep copy of each item; if the user chooses to queue pointers then the queue stores a deep copy of the pointer. Of course, if the user stores pointers in the queue then the user is responsible for managing the memory associated with the pointers. The queue doesn't care what data you're storing in it, it just needs to know the data's size.

## Slide 158: Queues
FreeRTOS supports blocking and non-blocking queue insertions and removals. Non-blocking operations return immediately with a "Did the queue insertion work?" or "Did the queue removal work?" status. Blocking operations are specified with a timeout. A task can block indefinitely or for a limited amount of time.
A blocked task—call it Task A—will remain blocked as long as its insert/remove operation cannot complete and its timeout (if any) has not expired. If an interrupt or another task modifies the queue so that Task A's operation could complete, Task A will be unblocked. If Task A's queue operation is still possible by the time it actually runs then Task A will complete its queue operation and return "success". However, by the time Task A actually runs, it is possible that a higher-priority task or interrupt has performed yet another operation on the queue that prevents Task A from performing its operation. In this case Task A will check its timeout and either resume blocking if the timeout hasn't expired, or return with a queue operation "failed" status.
It's important to note that the rest of the system keeps going while a task is blocking on a queue; other tasks and interrupts continue to run. This way the blocked task doesn't waste CPU cycles that could be used productively by other tasks and interrupts.
FreeRTOS uses the xTasksWaitingToSend list to keep track of tasks that are blocking on inserting into a queue. Each time an element is removed from a queue the xTasksWaitingToSend list is checked. If a task is waiting in that list the task is unblocked.
Similarly, xTasksWaitingToReceive keeps track of tasks that are blocking on removing from a queue. Each time a new element is inserted into a queue the xTasksWaitingToReceive list is checked. If a task is waiting in that list the task is unblocked.

## Slide 159: Semaphores and Mutexes
FreeRTOS uses its queues for communication between and within tasks.
FreeRTOS also uses its queues to implement semaphores and mutexes.
What's The Difference?
Semaphores and mutexes may sound like the same thing, but they're not. FreeRTOS implements them similarly, but they're intended to be used in different ways. How should they be used differently?
Embedded systems guru Michael Barr says it best in his article, "Mutexes and Semaphores Demystified":
The correct use of a semaphore is for signaling from one task to another. A mutex is meant to be taken and released, always in that order, by each task that uses the shared resource it protects. By contrast, tasks that use semaphores either signal ["send" in FreeRTOS terms] or wait ["receive" in FreeRTOS terms] - not both.
A mutex is used to protect a shared resource. A task acquires a mutex, uses the shared resource, then releases the mutex. No task can acquire a mutex while the mutex is being held by another task. This guarantees that only one task is allowed to use a shared resource at a time.
Semaphores are used by one task to signal another task. To quote Barr's article:
For example, Task 1 may contain code to post (i.e., signal or increment) a particular semaphore when the "power" button is pressed and Task 2, which wakes the display, pends on that same semaphore. In this scenario, one task is the producer of the event signal; the other the consumer.

## Slide 160: Semaphores and Mutexes
FreeRTOS implements an N-element semaphore as a queue that can hold N items. It doesn't store any actual data for the queue items; the semaphore just cares how many queue entries are currently occupied, which is tracked in the queue's uxMessagesWaiting field. It's doing "pure synchronization", as the FreeRTOS header file semphr.h calls it. Therefore the queue has a item size of zero bytes (uxItemSize == 0). Each semaphore access increments or decrements the uxMessagesWaiting field; no item or data copying is needed.
Like a semaphore, a mutex is also implemented as a queue, but several of the xQUEUE struct fields are overloaded using #defines:
/* Effectively make a union out of the xQUEUE structure. */
#define uxQueueType pcHead
#define pxMutexHolder pcTail
Since a mutex doesn't store any data in the queue, it doesn't need any internal storage, and so the pcHead and pcTail fields aren't needed. FreeRTOS sets the uxQueueType field (really the pcHead field) to 0 to note that this queue is being used for a mutex. FreeRTOS uses the overloaded pcTail fields to implement priority inheritance for mutexes.

## Slide 161: Priority Inheritance
In case you're not familiar with priority inheritance, I'll quote Michael Barr again to define it, this time from his article, "Introduction to Priority Inversion":
[Priority inheritance] mandates that a lower-priority task inherit the priority of any higher-priority task pending on a resource they share. This priority change should take place as soon as the high-priority task begins to pend; it should end when the resource is released.
FreeRTOS implements priority inheritance using the pxMutexHolder field (which is really just the overloaded-by-#define pcTail field). FreeRTOS records the task that holds a mutex in the pxMutexHolder field. When a higher-priority task is found to be waiting on a mutex currently taken by a lower-priority task, FreeRTOS "upgrades" the lower-priority task to the priority of the higher-priority task until the mutex is available again.

## Slide 162: Task management

## Slide 163: Introduction and scope
Main topics to be covered
  How FreeRTOS allocates processing time to each task within an application
  How FreeRTOS chooses which task should execute at any given time
  How the relative priority of each task affects system behavior
  The states that a task can exist in.

## Slide 164: More specific topics
How to implement tasks
How to create one or more instances of a task
How to use the task parameter
How to change the priority of a task that has already been created.
How to delete a task.
How to implement periodic processing.
When the idle task will execute and how it can be used.

## Slide 165: 1.2 Task functions
Tasks are implemented as C functions.
  Special: Its prototype must return void and take a void pointer parameter as the following
  void ATaskFunction (void *pvParameters);
Each task is a small program in its own right.
  Has an entry point
  Normally runs forever within an infinite loop
  Does not exit

## Slide 166: Special features of task function
FreeRTOS task
  Must not contain a ‘return’ statement
  Must not be allowed to execute past the end of the function
  If a task is no longer required it should be explicitly deleted.
  Be used to create any number of tasks
    Each created task is a separate execution instance with its own stack and its own copy of any automatic variables defined within the task itself.

## Slide 168: Top level task states
A task can exist in one of two states: Running and Not Running
Scheduler is the only entity that can switch a task in and out a running state.
Running state: the processor is
executing its code.
Not Running state: the task is dormant its status having been saved ready for resuming execution the next time
Notes: If MCU contains a single core only one task can be executing at any given time so

## Slide 169: Creating Tasks
xTaskCreate() API function
  the most fundamental component in a multitasking system
    Probably the most complex of all API functions
  portBASE_TYPE xTaskCreate(
    pdTASK_CODE pvTaskCode
    const signed char * const pcName
    unsigned short usStackDepth
    void *pvParameters
    unsigned portBASE_TYPE uxPriority
    xTaskHandle *pxCreatedTask
  );

## Slide 170: All parameters
pvTaskCode
  a pointer to the function (just the function name) that implements the task.
pcName
  A descriptive name for the task. It is not used by FreeRTOS but a debugging aid.
  configMAX_TASK_NAME_LEN: the application defined constant that defines the maximum length a task name can task including the NULL terminator.

## Slide 171: All parameters
usStackDepth
  Each task has its own unique stack that is allocated by the kernel to the task when the task is created.
  The value specifies the number of words the task stack can hold.
    E.g. Cortex-M3 stack is 32 bits wide if usStackDepth is passed in as 100 400 bytes of stack space will be allocated (100*4 bytes)
  Size of the stack used by the idle task is defined by configMINIMAL_STACK_SIZE.
    Adjustable w.r.t. applications
Notes:   No easy way to determine the stack space required by a task.
    Must be adequate and that RAM is not being wasted unnecessarily

## Slide 172: All parameters
pvParameters
  The value assigned to pvParameters will be the values passed into the task.
uxPriority
  defines the priority at which the task will execute.
  Priorities can be assigned from 0 which is the lowest priority to (configMAX_PRIOIRTIES-1) which is the highest priority.
  Passing a value above (configMAX_PRIOIRTIES -1) will result in the priority being capped the maximum legitimate value.
Notes:   Task functions accept a parameter of type pointer to void (void*).

## Slide 173: All parameters
pxCreatedTask
  pass out a handle to the created task then be used to refer the created task in API calls.
    E.g. change the task priority or delete the task
  Be set to NULL if no use for the task handle
Two possible return values
  pdTRUE : task has been created successfully.
  errCOULD_NOT_ALLOCATE_REQUIRED_MEMORY
    Task has not been created as there is insufficient heap memory available for FreeRTOS to allocate enough RAM to hold the task data structures and stack.

## Slide 174: Example: Creating tasks
To demonstrate the steps of creating two tasks then starting the tasks executing.
  Tasks simply print out a string periodically using a crude null loop to create the periodic delay.
  Both tasks are created at the same priority and are identical except for the string they print out.

## Slide 175: Execution pattern of two Example 1 tasks
Both tasks are rapidly entering and exiting the Running state.
Only one task can exist in the Running state at any one time.

## Slide 176: Example 2 Using the task parameter
The two tasks in Example 1 are almost identical the only difference between them being the text string they print out.
  Remove such duplication by creating two instances of a single task implementation vTaskFunction.
    Each created instance will execute independently under the control of the FreeRTOS scheduler.
  The task parameter can then be used to pass into each task the string that it should print out.

## Slide 177: Example 2 Using the task parameter
First define a char string pcTextForTask1
static const char *pcTextForTask1 = Task 1 is running.;
Then in main(void) function change
xTaskCreate( vTask1 Task 1 240 NULL 1 NULL );
to
xTaskCreate( vTaskFunction Task 1 240 (void*)pcTextForTask1 1 NULL );
Create a task function vTaskFunction(void * pvParameters)
char *pcTaskName;
pcTaskName = (char *) pvParameters;

## Slide 178: Task priorities
uxPriority parameter of xTaskCreate() assigns an initial priority to the task being created.
  It can be changed after the scheduler has been started by using vTaskPrioritySet() API function
configMAX_RPIORITIES in FreeRTOSConfig.h
  Maximum number of priorities
  Higher this value more RAM consumed
  Range: [0(low) configMAX-PRIORITIES-1(high)]
  Any number of tasks can share the same priority

## Slide 179: Task priorities
To select the next task to run the scheduler itself must execute at the end of each time slice.
  Use a periodic interrupt called the tick (interrupt).
  Effectively set the length of time slice by the tick interrupt frequency -- configTICK_RATE_HZ in FreeRTOSConfig.h
configTICK_RATE_HZ
  If it is 100(Hz) the time slice will be 10 ms.
  API always calls specify time in tick interrupts (ticks)
portTICK_RATE_MS
  Convert time delays from milliseconds into the number of tick interrupts.
Notes:   Tick count is the total number of tick interrupts that have occurred since the scheduler was started

## Slide 180: Task priorities
When kernel itself is running the arrows in the above figure show the sequence of execution from task interrupt then from interrupt back to a next task.

## Slide 181: Example 3. Experimenting with priorities
Scheduler always ensures that the highest priority task is able to run is the task selected to enter the Running state.
  In Example 1 and 2 two tasks have been created at the same priority so both entered and exited the Running state in turn.
  In this example the second task is set at priority 2.

## Slide 182: Example 3. Experimenting with priorities
In main() function change
  xTaskCreate( vTaskFunction Task 2 240 (void*)pcTextForTask2 1 NULL );
  To
  xTaskCreate( vTaskFunction Task 2 240 (void*)pcTextForTask2 2 NULL );

## Slide 183: Example 3. Experimenting with priorities
The scheduler always selects the highest priority task that is able to run.
  Task 2 has a higher priority than Task 1; so Task 2 is the only task to ever enter the Running state.
  Task 1 is to be ‘starved’ of processing time of Task 2.

## Slide 184: ‘Continuous processing’ task
So far the created tasks always have work to perform and have never had to wait for anything
  Always able to enter the Running state.
This type of task has limited usefulness as they can only be created at the very lowest priority.
  If they run at any other priority they will tasks of lower priority ever running at all.
Solution: Event-driven tasks

## Slide 185: Expanding the ‘Not Running’ state
An event-driven task
  has work to perform only after the occurrence of the event that triggers it
  Is not able enter the Running state before that event has occurred.
The scheduler selects the highest priority task that is able to run.
  High priority tasks not being able to run means that the scheduler cannot select them and
  Must select a lower priority task that is able to run.
Using event-driven tasks means that
  tasks can be created at different priorities without the highest priority tasks starving all the lower priority tasks.

## Slide 186: Full task state machine

## Slide 187: Blocked state
Tasks enter this state to wait for two types of events
  Temporal (time-related) events: the event being either a delay expiring or an absolute time being reached.
    A task enter the Blocked state to wait for 10ms to pass
  Synchronization events: where the events originate from another task or interrupt
    A task enter the Blocked state to wait for data to arrive on a queue.
  Can block on a synchronization event with a timeout effectively block on both types of event simultaneously.
    A task waits for a maximum of 10ms for data to arrive on a queue. It leaves the Blocked state if either data arrives within 10ms or 10ms pass with no data arriving.

## Slide 188: Suspended state
Tasks in this state are not available to the scheduler.
  The only way into this state is through a call to the vTaskSuspend() API function
  The only way out this state is through a call to the vTaskResume() or vTaskResumeFromISR() API functions

## Slide 189: Ready state
Tasks that are in the ‘Not Running’ state but are not Blocked or Suspended are said to be in the Ready state.
  They are able to run and therefore ‘ready’ to run but are not currently in the Running state.

## Slide 190: Example 4 Using the Block state to create a delay
All tasks in the previous examples have been periodic
  They have delayed for a period and printed out their string before delay once more and so on.
  Delayed generated using a null loop
    the task effectively polled an incrementing loop counter until it reached a fixed value.

## Slide 191: Example 4 Using the Block state to create a delay
Disadvantages to any form of polling
  While executing the null loop the task remains in the Ready state ‘starving’ the other task of any processing time.
  During polling the task does not really have any work to do but it still uses maximum processing time and so wastes processor cycles.
This example corrects this behavior by
  replacing the polling null loop with a call to vTaskDelay() API function.
  setting INCLUDE_vTaskDelay to 1 in FreeRTOSConfig.h

## Slide 192: vTaskDelay() API function
Place the calling task into the Blocked state for a fixed number of tick interrupts.
  The Blocked state task does not use any processing time so processing time is consumed only when there is work to be done.
  void vTaskDelay(portTickType xTicksToDelay);
xTicksToDelay: the number of ticks that the calling task should remain in the Blocked state before being transitioned back into the Ready state.
E.g if a task called vTaskDelay(100) while the tick count was 10000 it enters the Blocked state immediately and remains there until the tick count is 10100.

## Slide 193: vTaskDelay() API function
In void vTaskFunction(void *pvParameters)
  Change a NULL loop
  for( ul = 0; ul < mainDELAY_LOOP_COUNT; ul++ ) { }
  To
  vTaskDelay(250 / portTICK_RATE_MS);
  // a period of 250ms is being specified.
  Although two tasks are being created at different priorities both will now run.

## Slide 194: vTaskDelay() API function
Each time the tasks leave the Blocked state they execute for a fraction of a tick period before re-entering the Blocked state.
  Most of the time no application tasks are able to run and so no tasks can be selected to enter the Running state.
  The idle task will run to ensure there is always at least one task that is able to run.
Notes: The idle task is created automatically when the scheduler is started to ensure there is always at least one task that is able to run.

## Slide 195: Bold lines indicate the state transitions performed by the tasks in Example 4
Tasks 1+2
Idle Task

## Slide 196: vTaskDelayUntil() API Function
Parameters to vTaskDelayUntil()
  specify the exact tick count value at which the calling task should be moved from the Blocked state into the Ready state.
  Be used when a fixed execution period is required.
    The time at which the calling task is unblocked is absolute rather than relative to when the function was called (as vTaskDelay())
void vTaskDelayUntil(
portTickType *pxPreviousWakeTime
portTickType xTimeIncrement);

## Slide 197: vTaskDelayUntil() prototype
pxPreviousWakeTime
  Assume that vTaskDelayUtil() is being used to implement a task that executes periodically and with a fixed frequency.
  Holds the time at which the task left the Blocked state.
  Be used as a reference point to compute the time at which the task next leaves the Blocked state.
  The variable pointed by pxPreviousWakeTime is updated automatically not be modified by application code other than when the variable is first initialized.

## Slide 198: vTaskDelayUntil() prototype
xTimeIncrement
  Assume that vTaskDelayUtil() is being used to implement a task that executes periodically and with a fixed frequency – set by xTimeIncrement.
  Be specified in ‘ticks’. The constant portTICK_RATE_MS can be used to convert ms to ticks.

## Slide 199: Example 5 Converting the example tasks to use vTaskDelayUntil()
Two tasks created in Example 4 are periodic tasks.
vTaskDelay() does not ensure that the frequency at which they run is fixed
  as the time at which the tasks leave the Blocked state is relative to when they call vTaskDelay().

## Slide 200: Example 5 Converting the example tasks to use vTaskDelayUntil()
In void vTaskFunction(void *pvParameters)
  Change
  vTaskDelay(250 / portTICK_RATE_MS);
  // a period of 250ms is being specified.
  To
  vTaskDelayUntil( &xLastWakeTime (vTaskDelay(250 / portTICK_RATE_MS));
  /*xLastWakeTime is initialized with the current tick count before entering the infinite loop. This is the only time it is written to explicitly. */
  xLastWakeTime = xTaskGetTickCount();
  /*It is then updated within vTaskDelayUntil(); automatically */

## Slide 201: Example 6 Combining blocking and non-blocking tasks
Two tasks are created at priority 1.
  Always be either the Ready or the Running state as never making any API function calls.
  Tasks of this nature are called continuous processing tasks they always have work to do.
A Third task is created at priority 2.
  Periodically prints out a string by using vTaskDelayUntil() to place itself into the Blocked state (blocking time 5) between each print iteration.

## Slide 202: Combining blocking and non-blocking tasks
void vContinuousProcessingTask(void * pvParameters) {
char *pcTaskName;
pcTaskName = (char *) pvParameters;
for (;;){ vPrintString(pcTaskName);
for( ul = 0; ul < 0xfff; ul++ ) { }
}}
void vPeriodicTask(void * pvParameters) {
portTickType xLastWakeTime;
xLastWakeTime = xTaskGetTickCount();
for (;;){ vPrintString(Periodic task is running);
vTaskDelayUntil(&xLastWakeTime
(10/portTICK_RATE_MS));
}}

## Slide 203: Scheduling operations

## Slide 204: 1.7 Idle Task and the Idle task hook
An idle task is automatically created by the scheduler when vTaskStartScheduler() is called.
  Does very little more than site in a loop
  Has the lowest possible priority (zero) to ensure it never prevents a higher priority application task from entering the Running state
  Be transitioned out of the Running state as soon as a higher priority task enters the Ready state

## Slide 205: Idle Task
The Idle task is immediately swapped out to allow Task 2 to execute at the instant Task 2 leaves the Blocked state.
  Task 2 pre-empts the idle task automatically.

## Slide 206: Idle Task Hook Functions
Add application specific functionality directly into the idle task by the use of an idle hook
  A function called automatically by the idle task once per iteration of the idle task loop
Common uses for the Idle task hook
  Executing low priority background or continuous processing
  Measuring the amount of spare processing capacity
  Placing the processor into a low power mode providing an automatic method of saving power whenever no application processing to be performed.

## Slide 207: Limitations on the implementation of Idle Task Hook Functions
Rules idle task hook functions must adhere to
  Must never attempt to block or suspend.
  If the application uses vTaskDelete() the Idle task hook must always return to its caller within a reasonable time period.
    Idle task is responsible for cleaning up kernel resources after a task has been deleted.
    If the idle task remains permanently in the Idle hook function this clean-up cannot occur.
Idle task hook functions have the name and prototype as
    void vApplicationIdleHook(void);

## Slide 208: Example 7 Defining an idle task hook function
Set configUSE_IDLE_HOOK to 1
Add following function
unsigned long ulIdleCycleCount = 0UL;
/* must be called this name take no parameters and return void. */
void vApplicationIdleHook (void) {
ulIdleCycleCount++;
}
In vTaskFunction() change
vPrintString(pcTaskName) To
vPrintStringAndNumber(pcTaskName ulIdleCycleCount);

## Slide 209: 1.7 Idle task and Idle Task Hook
Has the lowest priority possible to add functionality into the idle task vi idle hook
  Execute continuous processing
  Measuring spare processing capacity
  Placing the processor into a low power mode
Two rules
  Never block or suspend; must return to its caller within a reasonable time period as it needs to clean up kernel resources after a deleted task.

## Slide 210: 1.8 Change the priority of a task
  vTaskPrioritySet(xTaskHandle pxTask unsigned portBASE_TYPE uxNewPriority);
  Be used to change the priority of any task after the scheduler has been started.
  Available if INCLUDE_vTaskPrioritySet is set 1.
Two parameters
  pxTask: Handle of the task whose priority is being modified. A task can change its own priority by passing NULL in place of a valid task handle.
  uxNewPriority: the priority to be set.

## Slide 211: 1.8 Change the priority of a task
unsigned portBASE_TYPE uxTaskPriorityGet(xTaskHandle pxTask);
  Be used to query the priority of a task
  Available if INCLUDE_vTaskPriorityGet is set 1
  pxTask: Handle of the task whose priority is being modified. A task can query its own priority by passing NULL in place of a valid task handle.
  Returned value: the priority currently assigned to the task being queried

## Slide 212: Example: Changing task priorities
Demonstrate the scheduler always selects the highest Ready state task to run
  by using the vTaskPrioritySet() API function to change the priority of two tasks relative to each other.
Two tasks are created at two different priorities.
  Neither task makes any API function calls that cause it to enter the Blocked state
    So both are in either Ready or Running state.
    So the task with highest priority will always be the task selected by the scheduler to be in Running state

## Slide 213: Expected Behavior of Example 8
Task 1 is created with the highest priority to be guaranteed to run first. Task 1 prints out a couple of strings before raising the priority of Task 2 to above its own priority.
Task2 starts to run as it has the highest relative priority.
Task 2 prints out a message before setting its own priority back to below that of Task 1.
Task 1 is once again the highest priority task so it starts to run and forcing Task 2 back into the Ready state.

## Slide 214
Declare a global variable to hold the handle of Task 2.
  xTaskHandle xTask2Handle;
In main() function create two tasks
  xTaskCreate(vTask1 Task 1 240
  NULL 2 NULL);
  xTaskCreate(vTask2 Task 2 240
  NULL 1 &xTask2Handle);

## Slide 215
Change vTask1 by initialization
  unsigned portBASE_TYPE uxPriority;
  uxPriority = uxTaskPriorityGet(NULL);
And adding to the infinite loop
  vTaskPrioritySet(xTaskHandl1 (uxPriority+1));
Change vTask2 by initialization
  unsigned portBASE_TYPE uxPriority;
  uxPriority = uxTaskPriorityGet(NULL);
And adding to the infinite loop
  vTaskPrioritySet(NULL (uxPriority-2));

## Slide 216: Task with changing priority: execution sequence

## Slide 217: 1.9 Deleting a task
Deleted tasks no longer exist and cannot enter the Running state again.
Idle task is responsible to automatically free memory allocated by kernel to tasks that have been deleted.
  Remember if applications use vTaskDelete() do not completely starve the idle task of all processing time.
Note: any memory or other resource that the application task allocates itself must by be freed explicitly by the application code.

## Slide 218: vTaskDelete() API function
Function prototype
  void vTaskDelete(xTaskHandle pxTaskToDelete);
  pxTaskToDelete: Handle of the task that is to be deleted. A task can delete itself by passing NULL in place of valid task handle.
Available only when INCLUDE_vTaskDelete set 1

## Slide 219: Example: Deleting tasks (Behavior)
Task 1 is created by main() with priority 1. When it runs it creates Task 2 at priority 2. Task 2 as the highest priority task starts to execute immediately.
Task 2 does nothing but delete itself by passing NULL or its own task handle.
When Task 2 has been deleted Task 1 is again the highest priority task so continues executing – at which point it calls vTaskDelay() to block for a short period.
The idle task executes while Task 1 is in the blocked state and frees the memory that was allocated to the now deleted Task 2.
When Task 1 leaves the blocked state it again becomes the highest priority Ready state task and preempts the Idle task. Then start from Step1 again.

## Slide 220: Execution sequence

## Slide 221: Memory Management
Does not permit memory to be freed once it has been allocated.
Subdivide a single array into smaller blocks. Total size of the array (heap) is set by configTOTAL_HEAP_SIZE
xPortGetFreeHeapSize() returns the total amount of heap space that remains unallocated.

## Slide 222: Heap_2.c
Allow previously allocated blocks to be freed.
Does not combine adjacent free blocks into a single large block.

## Slide 223: Summary – Prioritized pre-emptive scheduling
Examples illustrate how and when FreeRTOS selects which task should be in the Running state.
  Each task is assigned a priority.
  Each task can exist in one of several states.
  Only one task can exist in the Running state at any one time.
  The scheduler always selects the highest priority Ready state task to enter the Running state.

## Slide 224: Fixed priority Pre-emptive scheduling
Fixed priority
  Each task is assigned a priority that is not altered by the kernel itself (only tasks can change priorities)
Pre-emptive
  A task entering the Ready state or having its priority altered will always pre-empt the Running state task if the Running state task has a lower priority.

## Slide 225: Tasks in the Blocked state
Tasks can wait in the Blocked state for an event and are automatically moved back to the Ready state when the event occurs.
Temporal events
  Occur at a particular time e.g. a block time expires.
  Generally be used to implement periodic or timeout behavior.
Synchronization events
  Occur when a task or ISR sends info to a queue or to one of the many types of semaphore.
  Generally be used to signal asynchronous activity such as data arriving at a peripheral.

## Slide 226: Semaphores & Queues
Introduction to task synchronization
Semaphores and mutexs of FreeRTOS
Queues of FreeRTOS

## Slide 227: Why Synchronization?
Synchronization may be used to solve:
  Mutual exclusion
  Control flow
  Data flow
Synchronization mechanisms include:
  Message queues
  Semaphores
  Mutexs
  Events
Correct synchronization mechanism depends on the synchronization issue being addressed
EF
M

## Slide 228: Mutual Exclusion
Problem: multiple tasks may simultaneously need to access the same resource
  Resource may be code data peripheral etc.
  Need to allow the shared resource exclusively accessible to only one task at a time
How to do?
  Allowing only one task to lock the resource and the rest have to wait for the resource to be unlocked
  Common mechanisms: lock/unlock mutex semaphore

## Slide 229: Control Flow Synchronization
Problem: a task or ISR may need to resume the execution of one or more other tasks so that tasks execute in an application-controlled order
  Mutual exclusion is used to prevent another task from running while control flow is used to allow another task to run often specific tasks
How to do?
  Common mechanisms: post/wait signal event

## Slide 230: Data Flow Synchronization
Problem: a task or ISR may need to pass some data to one or more other specific tasks so that data may be processed in an application-specified order
How to do?
  May be accomplished indirectly through control flow synchronization
  Common mechanisms: queues signal post/wait

## Slide 231: Outline
Introduction to task synchronization
Semaphores and mutexs of FreeRTOS
  Binary semaphores
  Counting semaphores
  Mutex
Queues of FreeRTOS

## Slide 232: Semaphores
Semaphores are used to:
  Control access to a shared resource (mutual exclusion)
  Signal the occurrence of an event
  Allow two tasks to synchronize their activities
Basic idea
  A semaphore contains a number of tokens. The code needs to acquire one in order to continue execution
  If all the tokens of the semaphore are used the requesting task is suspended until some tokens are released by their current owners

## Slide 233: How Semaphores Work?
A semaphore has:
  Counter: maximum number of concurrent accesses
  Queue: for tasks that wait for access
If a task requests (waits for) a semaphore
  if counter > 0 then (1) the counter is decremented by 1 and (2) task gets the semaphore and proceed to do work
  Else task is blocked and put in the queue
If a task releases (posts) a semaphore
  if there are tasks in the semaphore queue then appropriate task is readied according to queuing policy
  Else counter is incremented by 1
Notes: 233
This should be a quick review from the basic RTOS section earlier
Mutex is special case where the count =1 so only one task can hold it at a time

## Slide 234: Binary Semaphores
Semaphores with counter = 1 used for mutual exclusion and synchronization
  For synchronization purpose a binary semaphore can be think of as a queue that can only hold one item
    The queue can only be empty or full (hence binary)
    Tasks using the queue don't care what the queue holds only want to know if the queue is empty or full
    If more than one task blocks on the same semaphore then the task with the highest priority will be the task that is unblocked the next time the semaphore becomes available

## Slide 235: Binary Semaphores and Interrupts
The best way to handle complex events triggered by interrupts is to not do the code in the ISR
  Create a task that is blocking on a binary semaphore
  When the interrupt happens the ISR just sets (gives) the semaphore and exits
  Task can now be scheduled like any other
    No need to worry about nesting interrupts and interrupt priority
This is called Deferred Interrupt Processing

## Slide 236: Binary Semaphores and Interrupts
Figure from Using the FreeRTOS Real Time Kernel (a pdf book) fair use claimed.

## Slide 237: Create a Binary Semaphore
SemaphoreHandle_t xSemaphoreCreateBinary(void);
Function to create a binary semaphore
  The semaphore is created in the 'empty' state
  A binary semaphore need not be given back once obtained so task synchronization can be implemented by one task/interrupt continuously 'giving' the semaphore while another continuously 'takes' the semaphore
  Binary semaphores are assigned to variables of type SemaphoreHandle_t and can be used in any API function that takes a parameter of this type

## Slide 238: Set a Binary Semaphore
xSemaphoreGiveFromISR(
SemaphoreHandle_t xSemaphore
signed BaseType_t *pxHigherPriorityTaskWoken)
Set (give) a semaphore
  Can be used from an ISR
  xSemaphore: handle to the semaphore being released
  pxHigherPriorityTaskWoken: set to pdTRUE if giving the semaphore caused a task of a higher priority to unblock causing a context switch

## Slide 239: Reset a Binary Semaphore
xSemaphoreTake( xSemaphoreHandle xSemaphore
portTickType xBlockTime)
Reset (take) a semaphore
  xSemaphore: handle to the semaphore being taken
  xBlockTime: time in ticks to wait for the semaphore to become available
    A block time of zero can be used to poll the semaphore

## Slide 240: Example of Binary Semaphores
vSemaphoreHandle binary_sem; //Global handler void one_sec_isr(void){ // an ISR xSemaphoreGiveFromISR(binary_sem NULL); } void sem_task(void *p){ while(1) if(xSemaphoreTake(binary_sem999999)) puts(Tick!); } int main(void){ vSemaphoreCreateBinary(binary_sem); xTaskCreate(sem_task (signed char*)) t1 2048 NULL 1 NULL); vTaskStartScheduler(); return 0; }
Notes: 240
240

## Slide 241: Counting Semaphores
Typically used for two things:
Counting events:
  An event handler will 'give' a semaphore each time an event occurs and a handler task will 'take' a semaphore each time it processes an event
Resource management:
  The count value indicates number of available resources
  To get a resource a task must obtain (take) a semaphore
  When a task finishes with the resource it 'gives' the semaphore back
SemaphoreHandle_t xSemaphoreCreateCounting( UBaseType_t uxMaxCount UBaseType_t uxInitialCount)

## Slide 242: Priority Inversion
LPT starts running and acquires the semaphore.
Now HPT is created and it preempts LPT and starts running. It makes the request to acquire the semaphore. Since the semaphore is already with LPT HPT goes to blocked state.
LPT starts executing again and releases the semaphore.
Immediately the HPT comes out of the blocked state and starts executing.
It releases the semaphore and runs for some time and deletes itself.
Now control goes back to LPT which completes its job and deletes itself.
Finally the scheduler is left out with the idle task and it keeps running.

## Slide 243: Priority Inversion

## Slide 244: Extended Priority Inversion
LPT starts running and acquires the semaphore.
Now HPT is created and it preempts LPT and starts running. It makes the request to acquire the semaphore. Since the semaphore is already with LPT HPT goes to blocked state.
LPT starts executing again and waits for an event(packet to be received).
Now the Idle task starts running. Now the HPT is starved because of LPT and Idle task.
LPT comes out of blocked state as the event(wait time/packet is received) has occurred. Now it releases the semaphore.
Immediately the HPT comes out of the blocked state and starts executing. It releases the semaphore and runs for some time and deletes itself.
Now control goes back to LPT which completes its job and deletes itself.
Finally the scheduler is left out with the idle task and it keeps running.

## Slide 245: Extended Priority Inversion

## Slide 246: Worst Case Priority Inversion
LPT starts running and acquires the semaphore.
Now HPT is created and it preempts LPT and starts running. It makes the request to acquire the semaphore. Since the semaphore is already with LPT HPT goes to blocked state.
LPT starts executing again and creates an MPT tasks.
MPT preempts the LPT and starts running. At this point the HPT is starved because of LPT and MPT. MPT completes its job and deletes itself.
LPT comes out of blocked state and releases the semaphore.
Immediately the HPT comes out of the blocked state and starts executing. It releases the semaphore and runs for some time and deletes itself.
Now control goes back to LPT which completes its job and deletes itself.
Finally the scheduler is left out with the idle task and it keeps running.

## Slide 247: Worst Case Priority Inversion

## Slide 248: Priority Inheritance
As soon as the HPT makes a request to semaphore which is allocated to an LPT then the priority of LPT is temporarily increased to that of HPT. Once the LPT releases the semaphore its priority will be restored. Because of this the MPT is never allowed to interfere during the priority inversion(between LPT&HPT). -> Mutex!
LPT starts running and acquires the semaphore.
Now HPT is created and it preempts LPT and starts running. It makes the request to acquire the semaphore. Since the semaphore is already with LPT HPT goes to blocked state and LPT's priority is temporarily raised to that of HPT.
LPT starts executing again and creates an MPT tasks. It keeps running as its priority is currently higher than MPT. It releases the semaphore and its priority is restored back to lower value.
Immediately the HPT comes out of the blocked state and starts executing.
HPT releases the semaphore and runs for some time and deletes itself.
Now scheduler is left with LPTMPT and IDLE task. MPT starts running and deletes itself after completing its job.
Now control goes back to LPT which completes its job and deletes itself.
Finally the scheduler is left out with the idle task and it keeps running.

## Slide 249: Priority Inheritance

## Slide 250: Mutex
Mutexes are used for mutual exclusion so that only one task at a time uses a shared resource e.g. file data device ...
  To access the shared resource a task locks the mutex associated with the resource
  The task owns the mutex until it unlocks the mutex

## Slide 251: Mutex
Mutex acts like a token used to guard a resource
  When a task wishes to access the resource it must first obtain ('take') the token
  When the task has finished with the resource it must 'give' the token back - allowing other tasks the opportunity to access the same resource
Mutexes are binary semaphores that include a priority inheritance mechanism
  If a high priority task blocks while attempting to obtain a mutex (token) that is currently held by a lower priority task then the priority of the task holding the token is temporarily raised to that of the blocking task

## Slide 252: Priority Inversion
Assume priority of T1 > priority of T9
  If T9 has exclusive access T1 has to wait until T9 releases resource  inverting priority  can raise priority of T9
T1 has higher priority and preempts T9
Critical section
(critical section)

## Slide 253: Example of Mutex (1/3)
xSemaphoreHandle gatekeeper = 0; //Global handler void task_1(void *p){ while(1){ if(xSemaphoreTake(gatekeeper 1000)){ puts(Task 1 got access); access_precious_resource(); // critical section xSemaphoreGive(gatekeeper); } else{ puts(Task 1 failed to get access within 1000ms); } vTaskDelay(1000); /*Without delay Task 1 will get key immediately after releasing the key */ } }
Notes: 253
253

## Slide 254: Example of Mutex (2/3)
void task_2(void *p){ while(1){ if(xSemaphoreTake(gatekeeper 1000)){ puts(Task 2 got access); access_precious_resource(); // critical section xSemaphoreGive(gatekeeper); } else{ puts(Task 2 failed to get access within 1000ms); } vTaskDelay(1000); /*Without delay task 2 will get key immediately after releasing the key */ } }
Notes: 254
254

## Slide 255: Example of Mutex (3/3)
int main(void){ gatekeeper = xSemaphoreCreateMutex(); /*Create tasks with priority 1 for both users*/ xTaskCreate(task_1 (signed char*)) t1 1024 NULL 1 NULL); xTaskCreate(task_2 (signed char*)) t2 1024 NULL 1 NULL); vTaskStartScheduler(); return 0; }
Notes: 255
255

## Slide 256: Outline
Introduction to task synchronization
Semaphores and mutexs of FreeRTOS
Queues of FreeRTOS

## Slide 257: FreeRTOS Queues
Queues are the primary form of inter-task communications in FreeRTOS
  Can be used to send messages between tasks and between interrupts and tasks
  In most cases used as thread safe FIFO (First In First Out) buffers with new data being sent to the back of the queue although data can also be sent to the front.

## Slide 258: FreeRTOS Queues
Queues store a finite number of fixed-size data
  May be read and written by different tasks but do not belong to any task
  # of items and item size determined at queue create time
  Sending/receiving items are by copy not reference
Queue functions
  Create queues: xQueueCreate() vQueueDelete()
  Send/receive data to/from queues: xQueueSend() xQueueSendToBack() xQueueReceive() xQueueReceiveFromISR()
  Queue management/number of items in a queue
  Blocking on a queue/effect of priority

## Slide 259: Blocking on Queues
Queue APIs permit a block time to be specified
When read from an empty queue
  Task will be placed into the Blocked state
  Until data is available on the queue or block time expires
When write to a full queue
  Task will be placed into the Blocked state
  Until space is available in the queue or block time expires
If more than one task block on the same queue then the task with the highest priority will be the task that is unblocked first

## Slide 260: Queue Creation
QueueHandle_t xQueueCreate(
UBaseType_t uxQueueLength
UBaseType_t uxItemSize);
Creates a new queue instance
  Allocates queue storage and returns a handle
  uxQueueLength: maximum number of items that the queue can contain
  uxItemSize: number of bytes that each item in the queue will require
    Items are queued by copy not by reference so this is the number of bytes that will be copied for each posted item
  Each item on the queue must be the same size

## Slide 261: Send Data through Queues
BaseType_t xQueueSend(QueueHandle_t xQueue
const void * pvItemToQueue
TickType_t xTicksToWait);
Post an item on a queue
  The item is queued by copy not by reference
  Must not be called from an interrupt service routine
  xQueue: queue handle to which the item is to be posted
  pvItemToQueue: pointer to item to be placed on queue
  xTicksToWait: max. time (in ticks) that task should block waiting for space to become available should it is full
  If INCLUDE_vTaskSuspend is set to '1‘ then specifying the block time as portMAX_DELAY will block task indefinitely

## Slide 262: Receive Data through Queues
BaseType_t xQueueReceive(
QueueHandle_t xQueue void *pvBuffer
TickType_t xTicksToWait);
Receive an item from a queue
  The item is received by copy so a buffer of adequate size must be provided
  Must not be used in an interrupt service routine
  xQueue: queue handle from which to receive item
  pvBuffer: pointer to the buffer into which the received item will be copied.
  xTicksToWait: max. amount of time the task should block waiting for an item should the queue be empty

## Slide 263: Example of Queues (1/2)
xQueueHandle Global_Queue_Handle = 0; //Global Handler void sender_task(void *p){ int i=0; while(1){ printf(Send %i to receiver task i); if(!xQueueSend(Global_Queue_Handle &i 1000)) printf(Failed to send to queue); i++; vTaskDelay(3000); } } void receiver_task(void *p){ int rx_int = 0; while(1){ if(xQueueReceive(Global_Queue_Handle&rx_int1000)) printf(Received %i rx_int); else puts(Failed to receive data from queue); } }
Notes: 263
263

## Slide 264: Example of Queues (2/2)
int main(void){ Global_Queue_Handle = xQueueCreate(3 sizeof(int)); /*Create tasks with priority 1 for both users*/ xTaskCreate(sender_task (signed char*)) sx 1024 NULL 1 NULL); xTaskCreate(receiver_task (signed char*)) rx 1024 NULL 1 NULL); vTaskStartScheduler(); return 0; }
Notes: 264
264

## Slide 265: Scheduling

## Slide 266: CPU Scheduling
Earlier we talked about the life-cycle of a thread
  Active threads work their way from Ready queue to Running to various waiting queues.
Question: How is the OS to decide which of several threads to take off a queue?
  Obvious queue to worry about is ready queue
  Others can be scheduled as well however
Scheduling: deciding which threads are given access to resources

## Slide 267: Scheduling Assumptions
CPU scheduling big area of research in early 70’s
Many implicit assumptions for CPU scheduling:
  One program per user
  One thread per program
  Programs are independent
In general unrealistic but they simplify the problem
  For instance: is fair about fairness among users or programs?
    If I run one compilation job and you run five you get five times as much CPU on many operating systems
The high-level goal: Dole out CPU time to optimize some desired parameters of system
USER1
USER2
USER3
USER1
USER2
Time

## Slide 268: Assumption: CPU Bursts
Execution model: programs alternate between bursts of CPU and I/O
  Program typically uses the CPU for some period of time then does I/O then uses CPU again
  Each scheduling decision is about which job to give to the CPU for use by its next CPU burst
  With timeslicing thread may be forced to give up CPU before finishing current CPU burst
Weighted toward small bursts

## Slide 269: Scheduling Metrics
Waiting Time: time the job is waiting in the ready queue
  Time between job’s arrival in the ready queue and launching the job
Service (Execution) Time: time the job is running
Response (Completion) Time:
  Time between job’s arrival in the ready queue and job’s completion
  Response time is what the user sees:
    Time to echo a keystroke in editor
    Time to compile a program
Response Time = Waiting Time + Service Time
Throughput: number of jobs completed per unit of time
  Throughput related to response time but not same thing:
    Minimizing response time will lead to more context switching than if you only maximized throughput
Notes: What does CPU scheduling have to do with efficient use of the disk?
A lot! Have to have the CPU to make a disk request
Fairness: Minimize # of angry phone calls? Minimize my response time?

## Slide 270: Scheduling Policy Goals/Criteria
Minimize Response Time
  Minimize elapsed time to do an operation (or job)
Maximize Throughput
  Two parts to maximizing throughput
    Minimize overhead (for example context-switching)
    Efficient use of resources (CPU disk memory etc)
Fairness
  Share CPU among users in some equitable way
  Fairness is not minimizing average response time:
    Better average response time by making system less fair
Notes: What does CPU scheduling have to do with efficient use of the disk?
A lot! Have to have the CPU to make a disk request
Fairness: Minimize # of angry phone calls? Minimize my response time?

## Slide 271: First-Come First-Served (FCFS) Scheduling
First-Come First-Served (FCFS)
  Also First In First Out (FIFO) or Run until done
    In early systems FCFS meant one program scheduled until done (including I/O)
    Now means keep CPU until thread blocks
Example: Process Burst Time P1 24 P2 3 P3 3
  Suppose processes arrive in the order: P1 P2 P3 The Gantt Chart for the schedule is:
  Waiting time for P1 = 0; P2 = 24; P3 = 27
  Average waiting time: (0 + 24 + 27)/3 = 17
  Average completion time: (24 + 27 + 30)/3 = 27
Convoy effect: short process behind long process
P1
P2
P3
24
27
30
0

## Slide 272: FCFS Scheduling (Cont.)
  Suppose that processes arrive in order: P2 P3 P1 Now the Gantt chart for the schedule is:
  Waiting time for P1 = 6; P2 = 0; P3 = 3
  Average waiting time: (6 + 0 + 3)/3 = 3
  Average Completion time: (3 + 6 + 30)/3 = 13
In second case:
  Average waiting time is much better (before it was 17)
  Average completion time is better (before it was 27)
FCFS Pros and Cons:
  Simple (+)
  Short jobs get stuck behind long ones (-)
    Safeway: Getting milk always stuck behind cart full of small items
P1
P3
P2
6
3
30
0

## Slide 273: Time Slice / Round Robin (RR)
FCFS Scheme: Potentially bad for short jobs!
  Depends on submit order
  If you are first in line at supermarket with milk you don’t care who is behind you on the other hand…
Round Robin Scheme
  Each process gets a small unit of CPU time (time quantum) usually 10-100 milliseconds
  After quantum expires the process is preempted and added to the end of the ready queue
  n processes in ready queue and time quantum is q 
    Each process gets 1/n of the CPU time
    In chunks of at most q time units
    No process waits more than (n-1)q time units
Performance
  q large  FCFS
  q small  Interleaved
  q must be large with respect to context switch otherwise overhead is too high (all overhead)

## Slide 274: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 53 P2 8 8 P3 68 68 P4 24 24
  The Gantt chart is:

## Slide 275: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 33 P2 8 8 P3 68 68 P4 24 24
  The Gantt chart is:
P1
0
20

## Slide 276: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 33 P2 8 0 P3 68 68 P4 24 24
  The Gantt chart is:
P1
0
20
P2
28

## Slide 277: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 33 P2 8 0 P3 68 48 P4 24 24
  The Gantt chart is:
P1
0
20
P2
28
P3
48

## Slide 278: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 33 P2 8 0 P3 68 48 P4 24 4
  The Gantt chart is:
P1
0
20
P2
28
P3
48
P4
68

## Slide 279: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 13 P2 8 0 P3 68 48 P4 24 4
  The Gantt chart is:
P1
0
20
P2
28
P3
48
P4
68
P1
88

## Slide 280: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 13 P2 8 0 P3 68 28 P4 24 4
  The Gantt chart is:
P1
0
20
P2
28
P3
48
P4
68
P1
88
P3
108

## Slide 281: Example of RR with Time Quantum = 20
Example: Process Burst Time Remaining Time P1 53 0 P2 8 0 P3 68 0 P4 24 0
  The Gantt chart is:
  Waiting time for P1=(68-20)+(112-88)=72 P2=(20-0)=20 P3=(28-0)+(88-48)+(125-108)=85 P4=(48-0)+(108-68)=88
  Average waiting time = (72+20+85+88)/4=66¼
  Average completion time = (125+28+153+112)/4 = 104½
Thus Round-Robin Pros and Cons:
  Better for short jobs Fair (+)
  Context-switching time adds up for long jobs (-)
P1
0
20
P2
28
P3
48
P4
68
P1
88
P3
108
P4
112
P1
125
P3
145
P3
153

## Slide 282: Round-Robin Discussion
How do you choose time slice?
  What if too big?
    Response time suffers
  What if infinite ()?
    Get back FCFS/FIFO
  What if time slice too small?
    Throughput suffers!
Actual choices of timeslice:
  Initially UNIX timeslice one second:
    Worked ok when UNIX was used by one or two people.
    What if three compilations going on? 3 seconds to echo each keystroke!
  In practice need to balance short-job performance and long-job throughput:
    Typical time slice today is between 10ms – 100ms
    Typical context-switching overhead is 0.1ms – 1ms
    Roughly 1% overhead due to context-switching

## Slide 283: Comparisons between FCFS and Round Robin
Job # | FIFO | RR
1 | 100 | 991
2 | 200 | 992
… | … | …
9 | 900 | 999
10 | 1000 | 1000
Assuming zero-cost context-switching time is RR always better than FCFS?
Simple example:
  10 jobs each takes 100s of CPU time RR scheduler quantum of 1s All jobs start at the same time
Completion Times:
P1
P2
P9
P10
…
0
100
800
900
1000
200
FCFS
…
0
10
980
990
1000
20
…
…
…
…
999
991
RR

## Slide 284: Comparisons between FCFS and Round Robin
Assuming zero-cost context-switching time is RR always better than FCFS?
Simple example: 10 jobs each takes 100s of CPU time RR scheduler quantum of 1s All jobs start at the same time
Both RR and FCFS finish at the same time
Average response time is much worse under RR!
  Bad when all jobs same length
Also: Cache state must be shared between all jobs with RR but can be devoted to each job with FCFS
  Total time for RR longer even for zero-cost switch!
P1
P2
P9
P10
…
0
100
800
900
1000
200
FCFS
…
0
10
980
990
1000
20
…
…
…
…
999
991
RR

## Slide 285: Earlier Example with Different Time Quantum
Quantum
Completion
Time
Wait
Time
Average
P4
P3
P2
P1
P2
[8]
P4
[24]
P1
[53]
P3
[68]
0
8
32
85
153
Best FCFS:
31¼
8
85
0
32
Best FCFS
69½
32
153
8
85
Best FCFS

## Slide 286: Earlier Example with Different Time Quantum
Quantum
Completion
Time
Wait
Time
Average
P4
P3
P2
P1
31¼
8
85
0
32
Best FCFS
69½
32
153
8
85
Best FCFS
121¾
145
68
153
121
Worst FCFS
83½
121
0
145
68
Worst FCFS
P2
[8]
P4
[24]
P1
[53]
P3
[68]
0
68
121
145
153
Worst FCFS:

## Slide 287
Quantum
Completion
Time
Wait
Time
Average
P4
P3
P2
P1
62
57
85
22
84
Q = 1
104½
112
153
28
125
Q = 20
100½
81
153
30
137
Q = 1
66¼
88
85
20
72
Q = 20
31¼
8
85
0
32
Best FCFS
121¾
145
68
153
121
Worst FCFS
69½
32
153
8
85
Best FCFS
83½
121
0
145
68
Worst FCFS
95½
80
153
16
133
Q = 8
57¼
56
85
8
80
Q = 8
99½
92
153
18
135
Q = 10
99½
82
153
28
135
Q = 5
61¼
68
85
10
82
Q = 10
61¼
58
85
20
82
Q = 5
P1
0
8
56
P2
P3
P4
P1
P3
P4
P1
P3
P4
P1
P3
P1
P3
P3
P3
16
24
32
40
48
64
72
80
88
96
104
112
P1
P3
P1
120
128
133
141
149
P3
153

## Slide 288: What if we Knew the Future?
Could we always mirror best FCFS?
Shortest Job First (SJF):
  Run whatever job has the least amount of computation to do
Shortest Remaining Time First (SRTF):
  Preemptive version of SJF: if job arrives and has a shorter time to completion than the remaining time on the current job immediately preempt CPU
These can be applied either to a whole program or the current CPU burst of each program
  Idea is to get short jobs out of the system
  Big effect on short jobs only small effect on long ones
  Result is better average response time
Notes: Rich get richer and poor get poorer = short jobs get through the system faster long jobs take even longer

## Slide 289: Discussion
SJF/SRTF are the best you can do at minimizing average response time
  Provably optimal (SJF among non-preemptive SRTF among preemptive)
  Since SRTF is always at least as good as SJF focus on SRTF
Comparison of SRTF with FCFS and RR
  What if all jobs the same length?
    SRTF becomes the same as FCFS (i.e. FCFS is best can do if all jobs the same length)
  What if jobs have varying length?
    SRTF (and RR): short jobs not stuck behind long ones

## Slide 290: SRTF Further discussion
Starvation
  SRTF can lead to starvation if many small jobs!
  Large jobs never get to run
Somehow need to predict future
  How can we do this?
  Some systems ask the user
    When you submit a job have to say how long it will take
    To stop cheating system kills job if takes too long
  But: even non-malicious users have trouble predicting runtime of their jobs
Bottom line can’t really know how long job will take
  However can use SRTF as a yardstick for measuring other policies
  Optimal so can’t do any better
SRTF Pros & Cons
  Optimal (average response time) (+)
  Hard to predict future (-)
  Unfair (-)

## Slide 291: Predicting the Length of the Next CPU Burst
Adaptive: Changing policy based on past behavior
  CPU scheduling in virtual memory in file systems etc.
  Works because programs have predictable behavior
    If program was I/O bound in past likely in future
    If computer behavior were random wouldn’t help
Example: SRTF with estimated burst length
  Use an estimator function on previous bursts: Let tn-1 tn-2 tn-3 etc. be previous CPU burst lengths. Estimate next burst n = f(tn-1 tn-2 tn-3 …)
  Function f could be one of many different time series estimation schemes (Kalman filters etc.)
  Example: Exponential averaging n = tn-1+(1-)n-1 with (0<1)

## Slide 292: Multi-Level Feedback Scheduling
Cambridge Time Sharing System (CTSS)
  Multiple queues each with different priority
    Higher priority queues often considered foreground tasks
  Each queue has its own scheduling algorithm
    e.g. foreground – RR background – FCFS
    Sometimes multiple RR priorities with quantum increasing exponentially (highest:1ms next:2ms next: 4ms etc.)
Adjust each job’s priority as follows (details vary)
  Job starts in highest priority queue
  If timeout expires drop one level
  If timeout doesn’t expire push up one level (or to top)
Long-Running
Compute tasks
demoted to low priority

## Slide 293: Scheduling Details
Result approximates SRTF:
  CPU bound jobs drop like a rock
  Short-running I/O bound jobs stay near top
Scheduling must be done between the queues
  Fixed priority scheduling:
    Serve all from highest priority then next priority etc.
  Time slice:
    Each queue gets a certain amount of CPU time
    e.g. 70% to highest 20% next 10% lowest

## Slide 294: Scheduling Fairness
What about fairness?
  Strict fixed-priority scheduling between queues is unfair (run highest then next etc):
    Long running jobs may never get CPU
    In Multics shut down machine found 10-year-old job
  Must give long-running jobs a fraction of the CPU even when there are shorter jobs to run
  Tradeoff: fairness gained by hurting average response time!
How to implement fairness?
  Could give each queue some fraction of the CPU
    What if one long-running job and 100 short-running ones?
    Like express lanes in a supermarket—sometimes express lanes get so long get better service by going into one of the other lines
  Could increase priority of jobs that don’t get service
    What is done in UNIX
    This is ad hoc—what rate should you increase priorities?

## Slide 295: How to Evaluate a Scheduling algorithm?
Deterministic modeling
  Takes a predetermined workload and compute the performance of each algorithm for that workload
Queuing models
  Mathematical approach for handling stochastic workloads
Implementation/Simulation:
  Build system which allows actual algorithms to be run against actual data. Most flexible/general.

## Slide 296: A Final Word On Scheduling
When do the details of the scheduling policy and fairness really matter?
  When there aren’t enough resources to go around
When should you simply buy a faster computer?
  (Or network link or expanded highway or …)
  One approach: Buy it when it will pay for itself in improved response time
    Assuming you’re paying for worse response time in reduced productivity customer angst etc…
    Might think that you should buy a faster X when X is utilized 100% but usually response time goes to infinity as utilization100%
An interesting implication of this curve:
  Most scheduling algorithms work fine in the linear portion of the load curve fail otherwise
  Argues for buying a faster X when hit knee of curve
Utilization
Response time
100%

## Slide 297: Summary
Scheduling: selecting a process from the ready queue and allocating the CPU to it
FCFS Scheduling:
  Run threads to completion in order of submission
  Pros: Simple (+)
  Cons: Short jobs get stuck behind long ones (-)
Round-Robin Scheduling:
  Give each thread a small amount of CPU time when it executes; cycle between all ready threads
  Pros: Better for short jobs (+)
  Cons: Poor when jobs are same length (-)

## Slide 298: Summary (cont’d)
Shortest Job First (SJF)/Shortest Remaining Time First (SRTF):
  Run whatever job has the least amount of computation to do/least remaining amount of computation to do
  Pros: Optimal (average response time)
  Cons: Hard to predict future Unfair
Multi-Level Feedback Scheduling:
  Multiple queues of different priorities
  Automatic promotion/demotion of process priority in order to approximate SJF/SRTF

## Slide 299: Scheduling Periodic Tasks
Job (unit of work)
  a computation a file read a message transmission etc
Attributes
  Resources required to make progress
  Timing parameters
Released
Absolute deadline
Relative deadline
Execution time

## Slide 300: Real-Time Periodic Task
Task : a sequence of similar jobs
  Periodic task (pe)
    Its jobs repeat regularly
    Period p = inter-release time (0 < p)
    Execution time e = maximum execution time (0 < e < p)
    Utilization U = e/p
5
10
15
0

## Slide 301: Deadlines: Hard vs. Soft
Hard deadline
  Disastrous or very serious consequences may occur if the deadline is missed
  Validation is essential : can all the deadlines be met even under worst-case scenario?
  Deterministic guarantees
Soft deadline
  Ideally the deadline should be met for maximum performance. The performance degrades in case of deadline misses.
  Best effort approaches / statistical guarantees

## Slide 302: Schedulability
Property indicating whether a real-time system (a set of real-time tasks) can meet their deadlines
(41)
(52)
(72)

## Slide 303: Real-Time Scheduling
Determines the order of real-time task executions
Static-priority scheduling
Dynamic-priority scheduling
(41)
(52)
(72)
5
5
10
10
15
15

## Slide 304: RM (Rate Monotonic)
Optimal static-priority scheduling
It assigns priority according to period
A task with a shorter period has a higher priority
Executes a job with the shortest period
(41)
(52)
(72)
5
5
10
10
15
15
T1
T2
T3

## Slide 305: RM (Rate Monotonic)
Executes a job with the shortest period
(41)
(52)
(72)
Deadline Miss !
5
5
10
10
15
15
T1
T2
T3

## Slide 306: Response Time
Response time
  Duration from released time to finish time
(41)
(52)
(102)
5
5
10
10
15
15
T1
T2
T3

## Slide 307: Response Time
Response time
  Duration from released time to finish time
(41)
(52)
(102)
Response Time
5
5
10
10
15
15
T1
T2
T3

## Slide 308: Response Time
Response Time (ri) [Audsley et al. 1993]
means ceiling of x i.e. the smallest integer larger than x.
HP(Ti) : a set of higher-priority tasks than Ti
(41)
(52)
(102)
5
5
10
10
T1
T2
T3
T | r | r | r | r | R
n | 1 | 2 | 3 | 4 | 5
1 | 1 |  |  |  | 
2 | 2 | 3 | 3 |  | 
3 | 2 | 5 | 6 | 8 | 8
r20=0
r21=2+0
r22=2+ceil(2/4)*1=3
r23=2+ceil(3/4)*1=3
End of iteration

## Slide 309: Response Time
Response Time (ri) [Audsley et al. 1993]
means ceiling of x i.e. the smallest integer larger than x.
HP(Ti) : a set of higher-priority tasks than Ti
(41)
(52)
(102)
5
5
10
10
T1
T2
T3
T | r | r | r | r | R
n | 1 | 2 | 3 | 4 | 5
1 | 1 |  |  |  | 
2 | 2 | 3 | 3 |  | 
3 | 2 | 5 | 6 | 8 | 8
r20=0
r21=2+0
r22=2+ceil(2/5)*1=3
r23=2+ceil(3/5)*1=3
End of iteration

## Slide 310: RM - Schedulability Analysis
Real-time system is schedulable under RM
if and only if ri ≤ pi for all task Ti(piei)
Joseph & Pandya
Finding response times in a real-time system
The Computer Journal 1986.

## Slide 311: RM – Utilization Bound
Real-time system is schedulable under RM if
∑Ui ≤ n (21/n-1)
Liu & Layland
Scheduling algorithms for multi-programming in a hard-real-time environment Journal of ACM 1973.

## Slide 312: RM – Utilization Bound
Real-time system is schedulable under RM if
∑Ui ≤ n (21/n-1)
Example: T1(41) T2(51) T3(101)
∑Ui = 1/4 + 1/5 + 1/10
= 0.55
3 (21/3-1) ≈ 0.78
Thus {T1 T2 T3} is schedulable under RM.

## Slide 313: RM – Utilization Bound
Real-time system is schedulable under RM if
∑Ui ≤ n (21/n-1)

## Slide 314: EDF (Earliest Deadline First)
Optimal dynamic priority scheduling
A task with a shorter deadline has a higher priority
Executes a job with the earliest deadline
(41)
(52)
(72)
5
5
10
10
15
15
T1
T2
T3

## Slide 315: EDF (Earliest Deadline First)
Executes a job with the earliest deadline
(41)
(52)
(72)
5
5
10
10
15
15
T1
T2
T3

## Slide 316: EDF (Earliest Deadline First)
Executes a job with the earliest deadline
(41)
(52)
(72)
5
5
10
10
15
15
T1
T2
T3

## Slide 317: EDF (Earliest Deadline First)
Executes a job with the earliest deadline
(41)
(52)
(72)
5
5
10
10
15
15
T1
T2
T3

## Slide 318: EDF (Earliest Deadline First)
Optimal scheduling algorithm
  if there is a schedule for a set of real-time tasks
  EDF can schedule it.
(41)
(52)
(72)
5
5
10
10
15
15
T1
T2
T3

## Slide 319: Interprocess Communication
Semaphore / Mutex revisited
Queue Revisited
Events
Socket Interface

## Slide 320: Task Synchronisation
Mutual Exclusion
  Regulating access to data peripherals or drivers
  One task only gets access
  No regulation of task order
Cooperation
  Regulating the order in which tasks or parts of tasks are processed
  Task order is regulated

## Slide 321: Task Synchronization
readout
n temperature sensors
write
n temperature values to a table
task 1
read
n temperature values from a table
print
n temperature values
task 2
competing­ access

## Slide 322: Task Synchronization - Mutex
readout
n temperature sensors
write
n temperature values to a table
task 1
acquire Mutex for temperature table
release Mutex for temperature table
task 2
mutex synchron-ization
acquire Mutex for temperature table
read
n temperature values from a table
release Mutex for temperature table
print
n temperature values
critical
section

## Slide 323: Task Synchronization - Cooperation
readout
n temperature sensors
write
n temperature values to a table
task 1
wait for table ready to read-object
set coop. object table ready to write
task 2
cooperation
read
n temperature values from a table
set coop. object table ready to read
print
n temperature values
block task while waiting
wait for table ready to write-object
block task while waiting

## Slide 324: Task Synchronization
Both Mutex and Cooperation are realized by Semaphores
Mutex is always a binary semaphore and adapts priority
Cooperation uses multiple semaphores to achieve task ordering

## Slide 325: Task Synchronisation - Deadlocks
Deadlock: One or more tasks are permanently blocked
Exercise (see deadlock.cpp):
Find the deadlock in the program and find a solution avoiding it.
task 1
task 2
Initialize Semaphore Sa = 1
Acquire(Sb)
block other task
Initialize Semaphore Sb = 1
access to resource b
Acquire(Sa)
access to resource a
Release(Sa)
Release(Sb)
Acquire(Sa)
Acquire(Sb)
access to resource a
access to resource b
Release(Sb)
Release(Sa)
risk for a deadlock
If several resources are to be protected at the same time all accessing tasks must acquire / release semaphores in the same order to avoid deadlocks.

## Slide 326: Task Synchronisation - Livelocks
Livelocks (starvation) designate a condition in which a task is constantly inhibited from running by the conspiracy of other tasks
Example: FPP Task 1 = High Priority Task 2 = Low Priority Task 3 = Medium Priority
Task 1
Task 2
mutex
object
Task 3
t
2
blocked
running
ready
Task 1
Task 2
1
2
Task 2 takes
mutex
Task 1 tries to
take mutex
Livelock situation
with priority inversion:
Task 1 is blocked for long time
3
Ev for
Task 1
Ev for
Task 3
Task 3

## Slide 327: Task Communication
Synchronisation = Communication with little Information
Task Communication Methods:
  Shared Memory
    Memory area to write / read
    Semaphore to regulate access
    Very fast – preferred
    Only if there is physically shared memory
  Messages (Events)
    Queues
    Events

## Slide 328: Task Communication - Events
Definition: An event is a synchronization object which allows computing processes to give free the processor (by going to the block-state) up to a certain condition is met.
Basic Operations are
  Wait for Event
  Send Event
Events are not stored (like Semaphores) so can get lost if no one is listening.
// Task AB und C
read(kanal_A buffer sizeof(buffer) );
P(S); // enter critical section
write( datenspeicher buffer sizeof(buffer) );
SendEvent( Task_W );
// Task W
while (1) {
WaitForEvent( Task_W );
read( datenspeicher buffer sizeof(buffer) );
V(S); // leave critical section after read
WorkOnData( buffer );}

## Slide 329: Task Communication - Events
task W is not waiting yet !!
WaitForEvent()
read()
V(S)
WorkOnData()
write()
P(S)
read()
Send-Event()
Send-Event()
write()
WaitForEvent()
C
W
A
t
task C causes task W to get running starting with read()  During read() in task W task A has read new data  task A is blocked by P(S) before W could release the semaphore
 task W releases V(S)
 task A continues with write() and SendEvent()  the event gets lost cause task W is busy WorkingOnData() not waiting: critical race condition !!
 data loss A
Race Condition: Function of the program depends on the relative timing of operations. Any change in execution speed of either task changes the behaviour of the system -> Hard to debug

## Slide 330: Task Communication - Events
Solution: Move WorkOnData into the critical section
// Task W
while (1) {
WaitForEvent( Task_W );
read( datenspeicher buffer sizeof(buffer) );
WorkOnData( buffer );
V(S); // leave critical section after work}
theoretical chance for a race condition
WaitForEvent()
read()
V(S)
WorkOnData()
write()
P(S)
read()
Send-Event()
Send-Event()
write()
WaitForEvent()
C
W
A
t

## Slide 331: Task Communication - Queues
Already discussed previously
Reminder: Create Queue Lenght N (N=∞ -> Mailbox)
b
a
c
x
in-pointer
Queue - RTOS-Object (N = 10)
z
QueueSend(obj)
QueueReceive()
y
QueueReceive() places the calling task into the blocked (waiting) state if the message queue is empty. If not it returns the object to which the read (out-) pointer points to and the read (out-) pointer set to the next message object
QueueSend() command places the calling task into the blocked (waiting) state only if the message queue is full. If not the object is being stored at the position the write (in-) pointer references and the pointer is set to the next free space in which the next transmitted (posted) message object is stored

## Slide 332: Ethernet

## Slide 333: Ethernet
Most successful local area networking technology of last 20 years.
Developed in the mid-1970s by researchers at the Xerox Palo Alto Research Centers (PARC).
Uses CSMA/CD technology
  Carrier Sense Multiple Access with Collision Detection.
  A set of nodes send and receive frames over a shared link.
  Carrier sense means that all nodes can distinguish between an idle and a busy link.
  Collision detection means that a node listens as it transmits and can therefore detect when a frame it is transmitting has collided with a frame transmitted by another node.

## Slide 334: Ethernet
Uses ALOHA (packet radio network) as the root protocol
  Developed at the University of Hawaii to support communication across the Hawaiian Islands.
  For ALOHA the medium was atmosphere, for Ethernet the medium is a coax cable.
DEC and Intel joined Xerox to define a 10-Mbps Ethernet standard in 1978.
This standard formed the basis for IEEE standard 802.3
More recently 802.3 has been extended to include a 100-Mbps version called Fast Ethernet and a 1000-Mbps version called Gigabit Ethernet.

## Slide 335: Ethernet
An Ethernet segment is implemented on a coaxial cable of up to 500 m.
  This cable is similar to the type used for cable TV except that it typically has an impedance of 50 ohms instead of cable TV’s 75 ohms.
Hosts connect to an Ethernet segment by tapping into it.
A transceiver (a small device directly attached to the tap) detects when the line is idle and drives signal when the host is transmitting.
The transceiver also receives incoming signal.
The transceiver is connected to an Ethernet adaptor which is plugged into the host.
The protocol is implemented on the adaptor.

## Slide 336: Ethernet
Ethernet transceiver and adaptor

## Slide 337: Ethernet
Multiple Ethernet segments can be joined together by repeaters.
A repeater is a device that forwards digital signals.
No more than four repeaters may be positioned between any pair of hosts.
  An Ethernet has a total reach of only 2500 m.

## Slide 338: Ethernet - Repeater

## Slide 339: Ethernet
Any signal placed on the Ethernet by a host is broadcast over the entire network
  Signal is propagated in both directions.
  Repeaters forward the signal on all outgoing segments.
  Terminators attached to the end of each segment absorb the signal.
Ethernet uses Manchester encoding scheme.

## Slide 340: Ethernet
New Technologies in Ethernet
  Instead of using coax cable, an Ethernet can be constructed from a thinner cable known as 10Base2 (the original was 10Base5)
    10 means the network operates at 10 Mbps
    Base means the cable is used in a baseband system
    2 means that a given segment can be no longer than 200 m

## Slide 341: Ethernet
New Technologies in Ethernet
  Another cable technology is 10BaseT
    T stands for twisted pair
    Limited to 100 m in length
  With 10BaseT, the common configuration is to have several point to point segments coming out of a multiway repeater, called Hub

## Slide 342: Ethernet
Ethernet Hub

## Slide 343: Access Protocol for Ethernet
The algorithm is commonly called Ethernet’s Media Access Control (MAC).
  It is implemented in Hardware on the network adaptor.
Frame format
  Preamble (64bit): allows the receiver to synchronize with the signal (sequence of alternating 0s and 1s).
  Host and Destination Address (48bit each).
  Packet type (16bit): acts as demux key to identify the higher level protocol.
  Data (up to 1500 bytes)
    Minimally a frame must contain at least 46 bytes of data.
    Frame must be long enough to detect collision.
  CRC (32bit)

## Slide 344: Ethernet Frame
Ethernet Frame Format

## Slide 345: Ethernet Addresses
Each host on an Ethernet (in fact, every Ethernet host in the world) has a unique Ethernet Address.
The address belongs to the adaptor, not the host.
  It is usually burnt into ROM.
Ethernet addresses are typically printed in a human readable format
  As a sequence of six numbers separated by colons.
  Each number corresponds to 1 byte of the 6 byte address and is given by a pair of hexadecimal digits, one for each of the 4-bit nibbles in the byte
  Leading 0s are dropped.
  For example, 8:0:2b:e4:b1:2 is
    00001000 00000000 00101011 11100100 10110001 00000010

## Slide 346: Ethernet Addresses
To ensure that every adaptor gets a unique address, each manufacturer of Ethernet devices is allocated a different prefix that must be prepended to the address on every adaptor they build
    AMD has been assigned the 24bit prefix 8:0:20

## Slide 347: Ethernet Addresses
Each frame transmitted on an Ethernet is received by every adaptor connected to that Ethernet.
Each adaptor recognizes those frames addressed to its address and passes only those frames on to the host.
In addition, to unicast address, an Ethernet address consisting of all 1s is treated as a broadcast address.
  All adaptors pass frames addressed to the broadcast address up to the host.
Similarly, an address that has the first bit set to 1 but is not the broadcast address is called a multicast address.
  A given host can program its adaptor to accept some set of multicast addresses.

## Slide 348: Ethernet Addresses
To summarize, an Ethernet adaptor receives all frames and accepts
  Frames addressed to its own address
  Frames addressed to the broadcast address
  Frames addressed to a multicast addressed if it has been instructed

## Slide 349: Ethernet Transmitter Algorithm
When the adaptor has a frame to send and the line is idle, it transmits the frame immediately.
  The upper bound of 1500 bytes in the message means that the adaptor can occupy the line for a fixed length of time.
When the adaptor has a frame to send and the line is busy, it waits for the line to go idle and then transmits immediately.
The Ethernet is said to be 1-persistent protocol because an adaptor with a frame to send transmits with probability 1 whenever a busy line goes idle.

## Slide 350: Ethernet Transmitter Algorithm
Since there is no centralized control it is possible for two (or more) adaptors to begin transmitting at the same time,
  Either because both found the line to be idle,
  Or, both had been waiting for a busy line to become idle.
When this happens, the two (or more) frames are said to be collide on the network.

## Slide 351: Ethernet Transmitter Algorithm
Since Ethernet supports collision detection, each sender is able to determine that a collision is in progress.
At the moment an adaptor detects that its frame is colliding with another, it first makes sure to transmit a 32-bit jamming sequence and then stops transmission.
  Thus, a transmitter will minimally send 96 bits in the case of collision
    64-bit preamble + 32-bit jamming sequence

## Slide 352: Ethernet Transmitter Algorithm
One way that an adaptor will send only 96 bit (called a runt frame) is if the two hosts are close to each other.
Had they been farther apart,
  They would have had to transmit longer, and thus send more bits, before detecting the collision.

## Slide 353: Ethernet Transmitter Algorithm
The worst case scenario happens when the two hosts are at opposite ends of the Ethernet.
To know for sure that the frame its just sent did not collide with another frame, the transmitter may need to send as many as 512 bits.
  Every Ethernet frame must be at least 512 bits (64 bytes) long.
    14 bytes of header + 46 bytes of data + 4 bytes of CRC

## Slide 354: Ethernet Transmitter Algorithm
Why 512 bits?
  Why is its length limited to 2500 m?
The farther apart two nodes are, the longer it takes for a frame sent by one to reach the other, and the network is vulnerable to collision during this time

## Slide 355: Ethernet Transmitter Algorithm
A begins transmitting a frame at time t
d denotes the one link latency
The first bit of A’s frame arrives at B at time t + d
Suppose an instant before host A’s frame arrives, host B begins to transmit its own frame
B’s frame will immediately collide with A’s frame and this collision will be detected by host B
Host B will send the 32-bit jamming sequence
Host A will not know that the collision occurred until B’s frame reaches it, which will happen at t + 2 * d
Host A must continue to transmit until this time in order to detect the collision
  Host A must transmit for 2 * d to be sure that it detects all possible collisions

## Slide 356: Ethernet Transmitter Algorithm
Worst-case scenario:
(a) A sends a frame at time t;
(b) A’s frame arrives at B at time t + d;
(c) B begins transmitting at time t + d and collides with A’s frame;
(d) B’s runt (32-bit) frame arrives at A at time t + 2d.

## Slide 357: Ethernet Transmitter Algorithm
Consider that a maximally configured Ethernet is 2500 m long, and there may be up to four repeaters between any two hosts, the round trip delay has been determined to be 51.2 s
  Which on 10 Mbps Ethernet corresponds to 512 bits
The other way to look at this situation,
  We need to limit the Ethernet’s maximum latency to a fairly small value (51.2 s) for the access algorithm to work
    Hence the maximum length for the Ethernet is on the order of 2500 m.

## Slide 358: Ethernet Transmitter Algorithm
Once an adaptor has detected a collision, and stopped its transmission, it waits a certain amount of time and tries again.
Each time the adaptor tries to transmit but fails, it doubles the amount of time it waits before trying again.
This strategy of doubling the delay interval between each retransmission attempt is known as Exponential Backoff.

## Slide 359: Ethernet Transmitter Algorithm
The adaptor first delays either 0 or 51.2 s, selected at random.
If this effort fails, it then waits 0, 51.2, 102.4, 153.6 s (selected randomly) before trying again;
  This is k * 51.2 for k = 0, 1, 2, 3
After the third collision, it waits k * 51.2 for k = 0…23 – 1 (again selected at random).
In general, the algorithm randomly selects a k between 0 and 2n – 1 and waits for k * 51.2 s, where n is the number of collisions experienced so far.

## Slide 360: Experience with Ethernet
Ethernets work best under lightly loaded conditions.
  Under heavy loads, too much of the network’s capacity is wasted by collisions.
Most Ethernets are used in a conservative way.
  Have fewer than 200 hosts connected to them which is far fewer than the maximum of 1024.
Most Ethernets are far shorter than 2500m with a round-trip delay of closer to 5 s than 51.2 s.
Ethernets are easy to administer and maintain.
  There are no switches that can fail and no routing and configuration tables that have to be kept up-to-date.
  It is easy to add a new host to the network.
  It is inexpensive.
    Cable is cheap, and only other cost is the network adaptor on each host.

## Slide 361: IP - The Internet Protocol

## Slide 362: Orientation
IP (Internet Protocol) is a Network Layer Protocol.
IP’s current version is Version 4 (IPv4). It is specified in RFC 891.

## Slide 363: IP: The waist of the hourglass
IP is the waist of the hourglass of the Internet protocol architecture
Multiple higher-layer protocols
Multiple lower-layer protocols
Only one protocol at the network layer.

## Slide 364: Application protocol
IP is the highest layer protocol which is implemented at both routers and hosts

## Slide 365: IP Service
Delivery service of IP is minimal
IP provide provides an unreliable connectionless best effort service (also called: “datagram service”).
  Unreliable: IP does not make an attempt to recover lost packets
  Connectionless: Each packet (“datagram”) is handled independently. IP is not aware that packets between hosts may be sent in a logical sequence
  Best effort: IP does not make guarantees on the service (no throughput guarantee, no delay guarantee,…)
Consequences:
Higher layer protocols have to deal with losses or with duplicate packets
Packets may be delivered out-of-sequence

## Slide 366: IP Service
IP supports the following services:
    one-to-one (unicast)
    one-to-all (broadcast)
    one-to-several (multicast)
IP multicast also supports a many-to-many service.
IP multicast requires support of other protocols (IGMP, multicast routing)
unicast
broadcast
multicast

## Slide 367: IP Datagram Format
20 bytes ≤ Header Size < 24 x 4 bytes = 60 bytes
20 bytes ≤ Total Length < 216 bytes = 65536 bytes

## Slide 368: IP Datagram Format
Question: In which order are the bytes of an IP datagram transmitted?
Answer:
    Transmission is row by row
    For each row:
        1. First transmit bits 0-7
        2. Then transmit bits 8-15
        3. Then transmit bits 16-23
        4. Then transmit bits 24-31
This is called network byte order or big endian byte ordering.
Note: Many computers (incl. Intel processors) store 32-bit words in little endian format. Others (incl. Motorola processors) use big endian.

## Slide 369: Big endian vs. small endian
Little Endian
Stores the low-order byte at the lowest address and the highest order byte in the highest address.
Base Address+0 Byte0 Base Address+1 Byte1 Base Address+2 Byte2 Base Address+3 Byte3
Intel processors use this order
Big Endian
Stores the high-order byte at the lowest address, and the low-order byte at the highest address.
Base Address+0 Byte3 Base Address+1 Byte2 Base Address+2 Byte1 Base Address+3 Byte0
Motorola processors use big endian.
Conventions to store a multibyte work
Example: a 4 byte Long Integer Byte3 Byte2 Byte1 Byte0

## Slide 370: Fields of the IP Header
Version (4 bits): current version is 4, next version will be 6.
Header length (4 bits): length of IP header, in multiples of 4 bytes
DS/ECN field (1 byte)
  This field was previously called as Type-of-Service (TOS) field. The role of this field has been re-defined, but is “backwards compatible” to TOS interpretation
  Differentiated Service (DS) (6 bits):
    Used to specify service level (currently not supported in the Internet)
  Explicit Congestion Notification (ECN) (2 bits):
    New feedback mechanism used by TCP

## Slide 371: Fields of the IP Header
Identification (16 bits): Unique identification of a datagram from a host. Incremented whenever a datagram is transmitted
Flags (3 bits):
  First bit always set to 0
  DF bit (Do not fragment)
  MF bit (More fragments)
  Will be explained later Fragmentation

## Slide 372: Fields of the IP Header
Time To Live (TTL) (1 byte):
  Specifies longest paths before datagram is dropped
  Role of TTL field: Ensure that packet is eventually dropped when a routing loop occurs
  Used as follows:
  Sender sets the value (e.g., 64)
  Each router decrements the value by 1
  When the value reaches 0, the datagram is dropped

## Slide 373: Fields of the IP Header
Protocol (1 byte):
    Specifies the higher-layer protocol.
    Used for demultiplexing to higher layers.
Header checksum (2 bytes): A simple 16-bit long checksum which is computed for the header of the datagram.

## Slide 374: Fields of the IP Header
Options:
    Security restrictions
    Record Route: each router that processes the packet adds its IP address to the header.
    Timestamp: each router that processes the packet adds its IP address and time to the header.
    (loose) Source Routing: specifies a list of routers that must be traversed.
    (strict) Source Routing: specifies a list of the only routers that can be traversed.
Padding: Padding bytes are added to ensure that header ends on a 4-byte boundary

## Slide 375: Maximum Transmission Unit
Maximum size of IP datagram is 65535, but the data link layer protocol generally imposes a limit that is much smaller
Example:
  Ethernet frames have a maximum payload of 1500 bytes
   IP datagrams encapsulated in Ethernet frame cannot be longer than 1500 bytes
The limit on the maximum IP datagram size, imposed by the data link protocol is called maximum transmission unit (MTU)
MTUs for various data link protocols:
  Ethernet: 1500 FDDI: 4352
  802.3: 1492 ATM AAL5: 9180
  802.5: 4464 PPP: negotiated

## Slide 376: IP Fragmentation
MTUs: FDDI: 4352 Ethernet: 1500
Fragmentation:
  IP router splits the datagram into several datagram
  Fragments are reassembled at receiver
What if the size of an IP datagram exceeds the MTU?
IP datagram is fragmented into smaller units.
What if the route contains networks with different MTUs?

## Slide 377: Where is Fragmentation done?
    Fragmentation can be done at the sender or at intermediate routers
    The same datagram can be fragmented several times.
    Reassembly of original datagram is only done at destination hosts !!

## Slide 378: What’s involved in Fragmentation?
The following fields in the IP header are involved:
Identification When a datagram is fragmented, the identification is the same in all fragments
Flags
DF bit is set: Datagram cannot be fragmented and must be discarded if MTU is too small
MF bit set: This datagram is part of a fragment and an additional fragment follows this one

## Slide 379: What’s involved in Fragmentation?
The following fields in the IP header are involved:
Fragment offset Offset of the payload of the current fragment in the original datagram
Total length Total length of the current fragment

## Slide 380: Example of Fragmentation
A datagram with size 2400 bytes must be fragmented according to an MTU limit of 1000 bytes

## Slide 381: Determining the length of fragments
To determine the size of the fragments we recall that, since there are only 13 bits available for the fragment offset, the offset is given as a multiple of eight bytes.
a result, the first and second fragment have a size of 996 bytes (and not 1000 bytes). This number is chosen since 976 is the largest number smaller than 1000–20= 980 that is divisible by eight.
The payload for the first and second fragments is 976 bytes long, with bytes 0 through 975 of the original IP payload in the first fragment, and bytes 976 through 1951 in the second fragment.
The payload of the third fragment has the remaining 428 bytes, from byte 1952 through 2379.
With these considerations, we can determine the values of the fragment offset, which are 0, 976 / 8 = 122, and 1952 / 8 = 244, respectively, for the first, second and third fragment.

## Slide 382: IP Addressing

## Slide 383: What is an IP address?
An unique identifier for a computer or device (host) on a TCP/IP network
A 32-bit binary number usually represented as 4 decimal numbers separated by a period
Example:
206 . 40 . 185 . 73
11001110.00101000. 10111001.01001001

## Slide 384: What is an IP address?
Each address is 32 bits wide
Valid addresses can range from 0.0.0.0 to 255.255.255.255
WHY?
Because 11111111b = 25510

## Slide 385: What is an IP address?
Theoretically, a total of » 4.3 billion addresses are available
WHY?
Because 232 = 4,294,967,29610

## Slide 386: Two addresses in one…
Each address consists of two parts
  The network address
  The host address
Other systems may use more than one address (Ex: IPX)

## Slide 387: The Five Network Classes
Class A – begins with 0
  00000001 (110) to 01111111 (12610)*
Class B – begins with 10
  10000000 (12810) to 10111111 (19110)
Class C – begins with 110
  11000000 (19210) to 11011111 (22310)
*01111111 = 12710
Addresses beginning with 127 are reserved for loopback (127.0.0.1 is YOU)

## Slide 388: The Five Network Classes
Class D – begins with 1110
  22410 to 23910
  Reserved for multicasting
Class E – begins with 1111
  24010 to 25410
  Reserved for future use
These should not be used for host addressing

## Slide 389: Which part belongs to the network and which part belongs to the node?
Class A – XXXXXXXX.yyyyyyyy.yyyyyyyy.yyyyyyyy
Class B – XXXXXXXX.XXXXXXXX.yyyyyyyy.yyyyyyyy
Class C – XXXXXXXX.XXXXXXXX.XXXXXXXX.yyyyyyyy
Where X = Network and y = node

## Slide 390: IP Addresses*
Class | 1st Octet | Networks Ids | Host IDs
A | 1-126 | 27 = 126 | 224 = 16M
B | 128-191 | 214 = 16K | 216 = 64K
C | 192-223 | 221 = 2M | 28 = 255
*Numbers not exact

## Slide 391: There are three IP network addresses reserved for private networks
10.0.0.0/8
172.16.0.0/12
192.168.0.0/16
These can be used by anyone setting up an internal network.
Routers will never forward packets coming from these addresses.

## Slide 392: Subnetting
…can be done for a variety of reasons
  Organization
  Use of different physical media
  Preservation of address space
  Security
The most common reason is to control network traffic

## Slide 393: Subnetting
In an Ethernet network, all nodes on a segment see all packets transmitted by other nodes on that segment
Performance can be adversely affected under heavy traffic loads
A router is used to connect IP networks to minimize the amount of traffic each segment must receive

## Slide 394: Subnet masking
Applying a subnet mask allows you to identify the network and node parts of the address. A router will then determine whether the address is local or remote.
Network bits are masked as 1s
Node bits are masked as 0s
Class A – 255.0.0.0
  11111111.00000000.00000000.00000000
Class B – 255.255.0.0
  11111111.11111111.00000000.00000000
Class C – 255.255.255.0
  11111111.11111111.11111111.00000000

## Slide 395: Subnet masking

## Slide 396: Subnet masking
Performing a bitwise logical AND between the IP address and the subnet mask results in the network address
Ex: Class - B 140.179.240.200 10001100.10110011.11110000.11001000
11111111.11111111.00000000.00000000
10001100.10110011.00000000.00000000
Network Address = 140.179.000.000

## Slide 397: A Few Rules…
Each device on a node has a unique MAC address
Each device on a node needs a unique IP address
All devices on the same physical segment share a common network ID (subnet mask)
Each physical segment has a unique Network ID (subnet mask)

## Slide 398: Address Resolution Protocol (ARP)
Before an IP packet can be forwarded to another host, the MAC address (usually 6 bytes written in hex (Ex: 02-FE-87-4A-8C-A9) of the receiving machine must be known
ARP determines the MAC addresses that correspond to an IP address
A router will choose direct paths for the network packets based on the addressing of the IP frame it is handling (different routes to different networks)

## Slide 399: Address Resolution Protocol (ARP)

## Slide 400: Internet and Data Link Layer Addresses
Each host and router on a subnet needs a data link layer address to specify its address on the subnet
  This address appears in the data link layer frame sent on a subnet
  For instance, 48-bit 802.3 MAC layer frame addresses for LANs
Subnet DA
DL Frame for Subnet

## Slide 401: Addresses
Each host and router also needs an IP address at the internet layer to designate its position in the overall Internet
Subnet
Subnet
Subnet
128.171.17.13

## Slide 402: Internet and Data Link Addresses Serve Different Purposes
IP address
  To guide delivery to destination host across the Internet (across multiple networks)
Subnet Address
  To guide delivery between two hosts, two routers, and a host and router within a single subnet
  Same LAN, Frame Relay network, etc.

## Slide 403: Analogy
In company, each person has a company-wide ID number (like IP address)
In company, person also has a local office number in a building
Paychecks are made out to ID numbers
For delivery, also need to know office number

## Slide 404: Address Resolution
Problem
  Router knows that destination host is on its subnet based on the IP address of an arriving packet
  Does not know the destination host’s subnet address, so cannot deliver the packet across the subnet
Subnet
128.171.17.13
subnet address?
Destination Host

## Slide 405: Address Resolution Protocol (ARP)
Router creates an ARP Request message to be sent to all hosts on the subnet.
  Address resolution protocol message asks “Who has IP address 128.171.17.13?”
  Passes ARP request to data link layer process for delivery
Subnet
ARP Request

## Slide 406: Address Resolution Protocol (ARP)
Data link process of router broadcasts the ARP Request message to all hosts on the subnet.
  On a LAN, MAC address of 48 ones tells all stations to pay attention to the frame
Subnet
ARP Request

## Slide 407: Address Resolution Protocol )
Host with IP address 128.171.17.13 responds
  Internet process creates an ARP response message
  Contains the destination host’s subnet address (48-bit MAC address on a LAN)
Subnet
ARP Response

## Slide 408: Address Resolution Protocol
Router delivers the IP packet to the destination host
  Places the IP packet in the subnet frame
  Puts the destination host’s subnet address in the destination address field of the frame
Subnet
Deliver IP Packet
within a subnet frame

## Slide 409: Address Resolution Protocol
ARP Requests and Responses are sent between the internet layer processes on the router and the destination host
Internet
Process
Router
Internet
Process
Destination Host
ARP
Request
ARP Response

## Slide 410: Address Resolution Protocol
However, the data link processes deliver these ARP packets
  Router broadcasts the ARP Request
  Destination host sends ARP response to the subnet source address found in the broadcast frame
Internet
Process
Router
Internet
Process
Destination Host
Broadcast ARP Request
Direct ARP Response
Data Link
Process
Data Link
Process

## Slide 411: Direct and Indirect Routing
Direct – when nodes are on the same network
Indirect – used when the network numbers of the source and destination do not match
  Packet must be forwarded by a node that knows hot to reach the destination (a router)

## Slide 412: Transmission Control Protocol (TCP)

## Slide 413: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
reliable, in-order byte steam:
  no “message boundaries”
send & receive buffers
  buffer incoming & outgoing data
flow controlled:
  sender will not overwhelm receiver
congestion controlled:
  sender will not overwhelm network
point-to-point (unicast):
  one sender, one receiver
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
  State resides only at the END systems – Not a virtual circuit!
full duplex data:
  bi-directional data flow in same connection (A->B & B->A in the same connection)
  MSS: maximum segment size

## Slide 414: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 415: TCP Connection-oriented demux
TCP socket identified
by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
receiving host uses all four values to direct segment to appropriate socket

## Slide 416: TCP Demultiplexing Example
Client
IP:B
P
client
IP: A
P1
P
server
IP: C
SP: 80
DP: 9157
SP: 9157
DP: 80
SP: 80
DP: 5775
SP: 5775
DP: 80
P
P

## Slide 417: Typical TCP Transaction
Connection Termination
Reliable, In-Order
Data Exchange
Connection Establishment
Client
Server
time
time
A TCP Transaction consists of 3 Phases
  Connection Establishment
    Handshaking between client and server
  Reliable, In-Order Data Exchange
    Recover any lost data through retransmissions and ACKs
  Connection Termination
    Closing the connection

## Slide 418: TCP Connection Establishment
TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info (e.g. RcvWindow)
client: connection initiator
Socket clientSocket = new Socket("hostname", port#);
server: contacted by client
Socket connectionSocket = welcomeSocket.accept();

## Slide 419: Connection Establishment (cont)
Host A
Host B
SYN, Seq=42
SYN+ACK, Seq=79, ACK=43
ACK, Seq=43, ACK=80
time
Three-way handshake
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies a random initial seq #
  no data
Step 2: server host receives SYN, replies with SYNACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data
time
Connection
request
host ACKs and selects
its own initial seq #
host ACKs

## Slide 420: Connection Establishment (cont)
Host A
Host B
SYN, Seq=42
SYN+ACK, Seq=79, ACK=43
ACK, Seq=43, ACK=80
time
Three-way handshake
time
Connection
request
host ACKs and selects
its own initial seq #
host ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK

## Slide 421: TCP Starting Sequence Number Selection
Why a random starting sequence #? Why not simply choose 0?
  To protect against two incarnations of the same connection reusing the same sequence numbers too soon
  That is, while there is still a chance that a segment from an earlier incarnation of a connection will interfere with a later incarnation of the connection
How?
  Client machine seq #0, initiates connection to server with seq #0.
  Client sends one byte and client machine crashes
  Client reboots and initiates connection again
  Server thinks new incarnation is the same as old connection

## Slide 422: TCP Connection Termination
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Server might send some buffered but not sent data before closing the connection. Server then sends FIN and moves to Closing state.
client
FIN
server
ACK
ACK
FIN
close
Data
write
closed
timed wait
close
ACK
DATA

## Slide 423: TCP Connection Termination
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Why wait before closing the connection?
  If the connection were allowed to move to CLOSED state, then another pair of application processes might come along and open the same connection (use the same port #s) and a delayed FIN from an earlier incarnation would terminate the connection.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 424: TCP State-Transition Diagram
CLOSED
LISTEN
SYN_RCVD
SYN_SENT
ESTABLISHED
CLOSE_WAIT
LAST_ACK
CLOSING
TIME_WAIT
FIN_WAIT_2
FIN_WAIT_1
Passive open
Close
Send/
SYN
SYN/SYN + ACK
SYN + ACK/ACK
SYN/SYN + ACK
ACK
Close
/FIN
FIN/ACK
Close
/FIN
FIN/ACK
ACK + FIN/ACK
Timeout after two
segment lifetimes
FIN/ACK
ACK
ACK
ACK
Close
/FIN
Close
CLOSED
Active open
/SYN

## Slide 425: Typical TCP Client/Server Transitions
TCP client
lifecycle
TCP server
lifecycle

## Slide 426: How to program using the TCP?
TCP UDP
IP
LL
PL
Socket Layer
TCP UDP
IP
LL
PL
Socket Layer
TCP UDP
IP
LL
PL
Socket Layer
Socket Layer:
  Programmer’s API to the protocol stack
Typical network app has two pieces: client and server
Server: Passive entity. Provides service to clients
  e.g., Web server responds with the requested Web page
Client: initiates contact with server (“speaks first”)
  typically requests service from server, e.g., Web Browser

## Slide 427: Socket Creation
 | Family | Type | Protocol
TCP | PF_INET | SOCK_STREAM | IPPROTO_TCP
UDP |  | SOCK_DGRAM | IPPROTO_UDP
mySock = socket(family, type, protocol);
UDP/TCP/IP-specific sockets
Socket reference
  File (socket) descriptor in UNIX
  Socket handle in WinSock
Notes: Socket descriptors can be used just like file descriptors in UNIX. In WinSock, Socket handles and file handles are not the same thing.

## Slide 428: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
Server starts by getting ready to receive client connections…
Notes: Students should follow along with source code in the book

## Slide 429: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
/* Create socket for incoming connections */
if ((servSock = socket(PF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0)
DieWithError("socket() failed");
Notes: Students should follow along with source code in the book

## Slide 430: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
echoServAddr.sin_family = AF_INET; /* Internet address family */
echoServAddr.sin_addr.s_addr = htonl(INADDR_ANY);/* Any incoming interface */
echoServAddr.sin_port = htons(echoServPort); /* Local port */
if (bind(servSock, (struct sockaddr *) &echoServAddr, sizeof(echoServAddr)) < 0)
DieWithError("bind() failed");
Notes: Students should follow along with source code in the book

## Slide 431: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
/* Mark the socket so it will listen for incoming connections */
if (listen(servSock, MAXPENDING) < 0)
DieWithError("listen() failed");
Notes: Students should follow along with source code in the book

## Slide 432: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
for (;;) /* Run forever */
{
clntLen = sizeof(echoClntAddr);
if ((clntSock=accept(servSock,(struct sockaddr *)&echoClntAddr,&clntLen)) < 0)
DieWithError("accept() failed");
Notes: Students should follow along with source code in the book

## Slide 433: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
Server is now blocked waiting for connection from a client
Notes: Students should follow along with source code in the book

## Slide 434: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
Later, a client decides to talk to the server…
Notes: Students should follow along with source code in the book

## Slide 435: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
/* Create a reliable, stream socket using TCP */
if ((sock = socket(PF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0)
DieWithError("socket() failed");
Notes: Students should follow along with source code in the book

## Slide 436: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
echoServAddr.sin_family = AF_INET; /* Internet address family */
echoServAddr.sin_addr.s_addr = inet_addr(servIP); /* Server IP address */
echoServAddr.sin_port = htons(echoServPort); /* Server port */
if (connect(sock, (struct sockaddr *) &echoServAddr, sizeof(echoServAddr)) < 0)
DieWithError("connect() failed");
Notes: Students should follow along with source code in the book
A new socket is created on the server that is connected to the client socket

## Slide 437: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
echoStringLen = strlen(echoString); /* Determine input length */
/* Send the string to the server */
if (send(sock, echoString, echoStringLen, 0) != echoStringLen)
DieWithError("send() sent a different number of bytes than expected");
Notes: Students should follow along with source code in the book

## Slide 438: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
/* Receive message from client */
if ((recvMsgSize = recv(clntSocket, echoBuffer, RCVBUFSIZE, 0)) < 0)
DieWithError("recv() failed");
Notes: Students should follow along with source code in the book

## Slide 439: TCP Client/Server Interaction
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Bind socket to a port
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
close(sock); close(clntSocket)
Notes: Students should follow along with source code in the book
Note that server closes connection socket, not listening socket

## Slide 440: TCP Tidbits
Client
send(“Hello Bob”)
recv() -> “Hi Jane”
Server
recv() -> “Hello ”
recv() -> “Bob”
send(“Hi ”)
send(“Jane”)
Client knows server address and port
No correlation between send() and recv()
Notes: The client must know the server address and port
The server discovers the client’s address and port at connection

## Slide 441: Application Layer and Socket Programming

## Slide 442: Overview
Application layer
  Client-server
  Application requirements
Background
  TCP vs. UDP
  Byte ordering
Socket I/O
  TCP/UDP server and client
  I/O multiplexing

## Slide 443: Applications and Application-Layer Protocols
Application: communicating, distributed processes
  Running in network hosts in “user space”
  Exchange messages to implement app
  e.g., email, file transfer, the Web
Application-layer protocols
  One “piece” of an app
  Define messages exchanged by apps and actions taken
  User services provided by lower layer protocols
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 444: Client-Server Paradigm
Typical network app has two pieces: client and server
application
transport
network
data link
physical
application
transport
network
data link
physical
Client:
Initiates contact with server (“speaks first”)
Typically requests service from server,
For Web, client is implemented in browser; for e-mail, in mail reader
Server:
Provides requested service to client
e.g., Web server sends requested Web page, mail server delivers e-mail
request
reply

## Slide 445: Ftp: The File Transfer Protocol
Transfer file to/from remote host
Client/server model
  Client: side that initiates transfer (either to/from remote)
  Server: remote host
ftp: RFC 959
ftp server: port 21
file transfer
FTP
server
FTP
user
interface
FTP
client
local file
system
remote file
system
user
at host

## Slide 446: Ftp: Separate Control, Data Connections
Ftp client contacts ftp server at port 21, specifying TCP as transport protocol
Two parallel TCP connections opened:
  Control: exchange commands, responses between client, server.
    “out of band control”
  Data: file data to/from server
Ftp server maintains “state”: current directory, earlier authentication
FTP
client
FTP
server
TCP control connection
port 21
TCP data connection
port 20

## Slide 447: Ftp Commands, Responses
Sample Commands:
sent as ASCII text over control channel
USER username
PASS password
LIST return list of files in current directory
RETR filename retrieves (gets) file
STOR filename stores (puts) file onto remote host
Sample Return Codes
status code and phrase
331 Username OK, password required
125 data connection already open; transfer starting
425 Can’t open data connection
452 Error writing file

## Slide 448: What Transport Service Does an Application Need?
Data loss
Some apps (e.g., audio) can tolerate some loss
Other apps (e.g., file transfer, telnet) require 100% reliable data transfer
Timing
Some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Bandwidth
Some apps (e.g., multimedia) require minimum amount of bandwidth to be “effective”
Other apps (“elastic apps”) make use of whatever bandwidth they get

## Slide 449: Transport Service Requirements of Common Apps
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
elastic
elastic
elastic
audio: 5Kb-1Mb
video:10Kb-5Mb
same as above
few Kbps
elastic
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no
file transfer
e-mail
web documents
real-time audio/
video
stored audio/video
interactive games
financial apps
Application
Data loss
Bandwidth
Time Sensitive

## Slide 450: Lecture Overview
Application layer
  Client-server
  Application requirements
Background
  TCP vs. UDP
  Byte ordering
Socket I/O
  TCP/UDP server and client
  I/O multiplexing

## Slide 451: Server and Client
TCP/UDP
IP
Ethernet Adapter
Server
TCP/UDP
IP
Ethernet Adapter
Clients
Server and Client exchange messages over the network through a common Socket API
Socket API
hardware
kernel
space
user
space
ports

## Slide 452: User Datagram Protocol(UDP): An Analogy
Postal Mail
Single mailbox to receive messages
Unreliable 
Not necessarily in-order delivery
Each letter is independent
Must address each reply
Example UDP applications
Multimedia, voice over IP
UDP
Single socket to receive messages
No guarantee of delivery
Not necessarily in-order delivery
Datagram – independent packets
Must address each packet
Postal Mail
Single mailbox to receive letters
Unreliable 
Not necessarily in-order delivery
Letters sent independently
Must address each reply

## Slide 453: Transmission Control Protocol (TCP): An Analogy
TCP
Reliable – guarantee delivery
Byte stream – in-order delivery
Connection-oriented – single socket per connection
Setup connection followed by data transfer
Telephone Call
Guaranteed delivery
In-order delivery
Connection-oriented
Setup connection followed by conversation
Example TCP applications
  Web, Email, Telnet

## Slide 454: Network Addressing Analogy
412-268-8000 ext.123
Central Number
Applications/Servers
Web
Port 80
Mail
Port 25
Exchange
Area Code
412-268-8000 ext.654
IP Address
Network No.
Host Number
Telephone No
15-441 Students
Clients
Professors at CMU
Network Programming
Telephone Call
Port No.
Extension

## Slide 455: Concept of Port Numbers
  Port numbers are used to identify “entities” on a host
  Port numbers can be
    Well-known (port 0-1023)
    Dynamic or private (port 1024-65535)
  Servers/daemons usually use well-known ports
    Any client can identify the server/service
    HTTP = 80, FTP = 21, Telnet = 23, ...
    /etc/service defines well-known ports
  Clients usually use dynamic ports
    Assigned by the kernel at run time
TCP/UDP
IP
Ethernet Adapter
NTP
daemon
Web server
port 123
port 80

## Slide 456: Names and Addresses
Each attachment point on Internet is given unique address
  Based on location within network – like phone numbers
Humans prefer to deal with names not addresses
  DNS provides mapping of name to address
  Name based on administrative ownership of host

## Slide 457: Internet Addressing Data Structure
#include <netinet/in.h>
/* Internet address structure */
struct in_addr {
u_long s_addr; /* 32-bit IPv4 address */
}; /* network byte ordered */
/* Socket address, Internet style. */
struct sockaddr_in {
u_char sin_family; /* Address Family */
u_short sin_port; /* UDP or TCP Port# */
/* network byte ordered */
struct in_addr sin_addr; /* Internet Address */
char sin_zero[8]; /* unused */
};
sin_family = AF_INET selects Internet address family

## Slide 458: Byte Ordering
Big Endian
  Sun Solaris, PowerPC, ...
Little Endian
  i386, alpha, ...
Network byte order = Big Endian
128
2
194
95
union {
u_int32_t addr; /* 4 bytes address */
char c[4];
} un;
/* 128.2.194.95 */
un.addr = 0x8002c25f;
/* c[0] = ? */
c[0] c[1] c[2] c[3]
95
194
2
128

## Slide 459: Byte Ordering Functions
Converts between host byte order and network byte order
  ‘h’ = host byte order
  ‘n’ = network byte order
  ‘l’ = long (4 bytes), converts IP addresses
  ‘s’ = short (2 bytes), converts port numbers
#include <netinet/in.h>
unsigned long int htonl(unsigned long int hostlong);
unsigned short int htons(unsigned short int hostshort);
unsigned long int ntohl(unsigned long int netlong);
unsigned short int ntohs(unsigned short int netshort);

## Slide 460: Lecture Overview
Application layer
  Client-server
  Application requirements
Background
  TCP vs. UDP
  Byte ordering
Socket I/O
  TCP/UDP server and client
  I/O multiplexing

## Slide 461: What is a Socket?
A socket is a file descriptor that lets an application read/write data from/to the network
socket returns an integer (socket descriptor)
  fd < 0 indicates that an error occurred
  socket descriptors are similar to file descriptors
AF_INET: associates a socket with the Internet protocol family
SOCK_STREAM: selects the TCP protocol
SOCK_DGRAM: selects the UDP protocol
int fd; /* socket descriptor */
if ((fd = socket(AF_INET, SOCK_STREAM, 0)) < 0) }
perror(“socket”);
exit(1);
}

## Slide 462
TCP
IP
Ethernet Adapter
Web Server
Port 80
For example: web server
What does a web server need to do so that a web client can connect to it?
TCP Server

## Slide 463
Since web traffic uses TCP, the web server must create a socket of type SOCK_STREAM
int fd; /* socket descriptor */
if((fd = socket(AF_INET, SOCK_STREAM, 0)) < 0) {
perror(“socket”);
exit(1);
}
socket returns an integer (socket descriptor)
  fd < 0 indicates that an error occurred
AF_INET associates a socket with the Internet protocol family
SOCK_STREAM selects the TCP protocol
Socket I/O: socket()

## Slide 464
A socket can be bound to a port
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
/* create the socket */
srv.sin_family = AF_INET; /* use the Internet addr family */
srv.sin_port = htons(80); /* bind socket ‘fd’ to port 80*/
/* bind: a client may connect to any of my addresses */
srv.sin_addr.s_addr = htonl(INADDR_ANY);
if(bind(fd, (struct sockaddr*) &srv, sizeof(srv)) < 0) {
perror("bind"); exit(1);
}
Still not quite ready to communicate with a client...
Socket I/O: bind()

## Slide 465: Socket I/O: listen()
listen indicates that the server will accept a connection
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
/* 1) create the socket */
/* 2) bind the socket to a port */
if(listen(fd, 5) < 0) {
perror(“listen”);
exit(1);
}
Still not quite ready to communicate with a client...

## Slide 466: Socket I/O: accept()
accept blocks waiting for a connection
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
struct sockaddr_in cli; /* used by accept() */
int newfd; /* returned by accept() */
int cli_len = sizeof(cli); /* used by accept() */
/* 1) create the socket */
/* 2) bind the socket to a port */
/* 3) listen on the socket */
newfd = accept(fd, (struct sockaddr*) &cli, &cli_len);
if(newfd < 0) {
perror("accept"); exit(1);
}
accept returns a new socket (newfd) with the same properties as the original socket (fd)
  newfd < 0 indicates that an error occurred

## Slide 467: Socket I/O: accept() continued...
struct sockaddr_in cli; /* used by accept() */
int newfd; /* returned by accept() */
int cli_len = sizeof(cli); /* used by accept() */
newfd = accept(fd, (struct sockaddr*) &cli, &cli_len);
if(newfd < 0) {
perror("accept");
exit(1);
}
How does the server know which client it is?
  cli.sin_addr.s_addr contains the client’s IP address
  cli.sin_port contains the client’s port number
Now the server can exchange data with the client by using read and write on the descriptor newfd.
Why does accept need to return a new descriptor?

## Slide 468: Socket I/O: read()
read can be used with a socket
read blocks waiting for data from the client but does not guarantee that sizeof(buf) is read
int fd; /* socket descriptor */
char buf[512]; /* used by read() */
int nbytes; /* used by read() */
/* 1) create the socket */
/* 2) bind the socket to a port */
/* 3) listen on the socket */
/* 4) accept the incoming connection */
if((nbytes = read(newfd, buf, sizeof(buf))) < 0) {
perror(“read”); exit(1);
}

## Slide 469: TCP Client
TCP
IP
Ethernet Adapter
2 Web Clients
For example: web client
How does a web client connect to a web server?

## Slide 470: Dealing with IP Addresses
struct sockaddr_in srv;
srv.sin_addr.s_addr = inet_addr(“128.2.35.50”);
if(srv.sin_addr.s_addr == (in_addr_t) -1) {
fprintf(stderr, "inet_addr failed!\n"); exit(1);
}
Converting a numerical address to a string:
IP Addresses are commonly written as strings (“128.2.35.50”), but programs deal with IP addresses as integers.
struct sockaddr_in srv;
char *t = inet_ntoa(srv.sin_addr);
if(t == 0) {
fprintf(stderr, “inet_ntoa failed!\n”); exit(1);
}
Converting strings to numerical address:

## Slide 471: Translating Names to Addresses
Gethostbyname provides interface to DNS
Additional useful calls
  Gethostbyaddr – returns hostent given sockaddr_in
  Getservbyname
    Used to get service description (typically port number)
    Returns servent based on name
#include <netdb.h>
struct hostent *hp; /*ptr to host info for remote*/
struct sockaddr_in peeraddr;
char *name = “www.cs.cmu.edu”;
peeraddr.sin_family = AF_INET;
hp = gethostbyname(name)
peeraddr.sin_addr.s_addr = ((struct in_addr*)(hp->h_addr))->s_addr;

## Slide 472: Socket I/O: connect()
connect allows a client to connect to a server...
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by connect() */
/* create the socket */
/* connect: use the Internet address family */
srv.sin_family = AF_INET;
/* connect: socket ‘fd’ to port 80 */
srv.sin_port = htons(80);
/* connect: connect to IP Address “128.2.35.50” */
srv.sin_addr.s_addr = inet_addr(“128.2.35.50”);
if(connect(fd, (struct sockaddr*) &srv, sizeof(srv)) < 0) {
perror(”connect"); exit(1);
}

## Slide 473: Socket I/O: write()
write can be used with a socket
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by connect() */
char buf[512]; /* used by write() */
int nbytes; /* used by write() */
/* 1) create the socket */
/* 2) connect() to the server */
/* Example: A client could “write” a request to a server */
if((nbytes = write(fd, buf, sizeof(buf))) < 0) {
perror(“write”);
exit(1);
}

## Slide 474: Review: TCP Client-Server Interaction
socket()
bind()
listen()
accept()
write()
read()
read()
TCP Server
close()
socket()
TCP Client
connect()
write()
read()
close()
connection establishment
data request
data reply
end-of-file notification
from UNIX Network Programming Volume 1, figure 4.1

## Slide 475: UDP Server Example
UDP
IP
Ethernet Adapter
NTP
daemon
Port 123
For example: NTP daemon
What does a UDP server need to do so that a UDP client can connect to it?

## Slide 476: Socket I/O: socket()
The UDP server must create a datagram socket…
int fd; /* socket descriptor */
if((fd = socket(AF_INET, SOCK_DGRAM, 0)) < 0) {
perror(“socket”);
exit(1);
}
socket returns an integer (socket descriptor)
  fd < 0 indicates that an error occurred
AF_INET: associates a socket with the Internet protocol family
SOCK_DGRAM: selects the UDP protocol

## Slide 477: Socket I/O: bind()
A socket can be bound to a port
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
/* create the socket */
/* bind: use the Internet address family */
srv.sin_family = AF_INET;
/* bind: socket ‘fd’ to port 80*/
srv.sin_port = htons(80);
/* bind: a client may connect to any of my addresses */
srv.sin_addr.s_addr = htonl(INADDR_ANY);
if(bind(fd, (struct sockaddr*) &srv, sizeof(srv)) < 0) {
perror("bind"); exit(1);
}
Now the UDP server is ready to accept packets…

## Slide 478: Socket I/O: recvfrom()
read does not provide the client’s address to the UDP server
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
struct sockaddr_in cli; /* used by recvfrom() */
char buf[512]; /* used by recvfrom() */
int cli_len = sizeof(cli); /* used by recvfrom() */
int nbytes; /* used by recvfrom() */
/* 1) create the socket */
/* 2) bind to the socket */
nbytes = recvfrom(fd, buf, sizeof(buf), 0 /* flags */,
(struct sockaddr*) &cli, &cli_len);
if(nbytes < 0) {
perror(“recvfrom”); exit(1);
}

## Slide 479: Socket I/O: recvfrom() continued...
nbytes = recvfrom(fd, buf, sizeof(buf), 0 /* flags */,
(struct sockaddr*) cli, &cli_len);
The actions performed by recvfrom
  returns the number of bytes read (nbytes)
  copies nbytes of data into buf
  returns the address of the client (cli)
  returns the length of cli (cli_len)
  don’t worry about flags

## Slide 480: UDP Client Example
TCP
IP
Ethernet Adapter
2 UDP Clients
ports
How does a UDP client communicate with a UDP server?

## Slide 481: Socket I/O: sendto()
write is not allowed
Notice that the UDP client does not bind a port number
  a port number is dynamically assigned when the first sendto is called
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by sendto() */
/* 1) create the socket */
/* sendto: send data to IP Address “128.2.35.50” port 80 */
srv.sin_family = AF_INET;
srv.sin_port = htons(80);
srv.sin_addr.s_addr = inet_addr(“128.2.35.50”);
nbytes = sendto(fd, buf, sizeof(buf), 0 /* flags */,
(struct sockaddr*) &srv, sizeof(srv));
if(nbytes < 0) {
perror(“sendto”); exit(1);
}

## Slide 482: Review: UDP Client-Server Interaction
socket()
bind()
recvfrom()
sendto()
UDP Server
socket()
UDP Client
sendto()
recvfrom()
close()
blocks until datagram received from a client
data request
data reply
from UNIX Network Programming Volume 1, figure 8.1

## Slide 483: The UDP Server
UDP
IP
Ethernet Adapter
UDP Server
Port 2000
Port 3000
How can the UDP server service multiple ports simultaneously?

## Slide 484: UDP Server: Servicing Two Ports
int s1; /* socket descriptor 1 */
int s2; /* socket descriptor 2 */
/* 1) create socket s1 */
/* 2) create socket s2 */
/* 3) bind s1 to port 2000 */
/* 4) bind s2 to port 3000 */
while(1) {
recvfrom(s1, buf, sizeof(buf), ...);
/* process buf */
recvfrom(s2, buf, sizeof(buf), ...);
/* process buf */
}
What problems does this code have?

## Slide 485: Socket I/O: select()
int select(int maxfds, fd_set *readfds, fd_set *writefds,
fd_set *exceptfds, struct timeval *timeout);
FD_CLR(int fd, fd_set *fds); /* clear the bit for fd in fds */
FD_ISSET(int fd, fd_set *fds); /* is the bit for fd in fds? */
FD_SET(int fd, fd_set *fds); /* turn on the bit for fd in fds */
FD_ZERO(fd_set *fds); /* clear all bits in fds */
maxfds: number of descriptors to be tested
  descriptors (0, 1, ... maxfds-1) will be tested
readfds: a set of fds we want to check if data is available
  returns a set of fds ready to read
  if input argument is NULL, not interested in that condition
writefds: returns a set of fds ready to write
exceptfds: returns a set of fds with exception conditions

## Slide 486: Socket I/O: select()
int select(int maxfds, fd_set *readfds, fd_set *writefds,
fd_set *exceptfds, struct timeval *timeout);
struct timeval {
long tv_sec; /* seconds /
long tv_usec; /* microseconds */
}
timeout
  if NULL, wait forever and return only when one of the descriptors is ready for I/O
  otherwise, wait up to a fixed amount of time specified by timeout
    if we don’t want to wait at all, create a timeout structure with timer value equal to 0
Refer to the man page for more information

## Slide 487: Socket I/O: select()
int s1, s2; /* socket descriptors */
fd_set readfds; /* used by select() */
/* create and bind s1 and s2 */
while(1) {
FD_ZERO(&readfds); /* initialize the fd set */
FD_SET(s1, &readfds); /* add s1 to the fd set */
FD_SET(s2, &readfds); /* add s2 to the fd set */
if(select(s2+1, &readfds, 0, 0, 0) < 0) {
perror(“select”);
exit(1);
}
if(FD_ISSET(s1, &readfds)) {
recvfrom(s1, buf, sizeof(buf), ...);
/* process buf */
}
/* do the same for s2 */
}
select allows synchronous I/O multiplexing

## Slide 488
TCP
IP
Ethernet Adapter
Web Server
Port 80
How can a a web server manage
multiple connections simultaneously?
Port 8001
More Details About a Web Server

## Slide 489: Socket I/O: select()
int fd, next=0; /* original socket */
int newfd[10]; /* new socket descriptors */
while(1) {
fd_set readfds;
FD_ZERO(&readfds); FD_SET(fd, &readfds);
/* Now use FD_SET to initialize other newfd’s
that have already been returned by accept() */
select(maxfd+1, &readfds, 0, 0, 0);
if(FD_ISSET(fd, &readfds)) {
newfd[next++] = accept(fd, ...);
}
/* do the following for each descriptor newfd[n] */
if(FD_ISSET(newfd[n], &readfds)) {
read(newfd[n], buf, sizeof(buf));
/* process data */
}
}
Now the web server can support multiple connections...

## Slide 490: A Few Programming Notes: Representing Packets
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Length | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Type: 4-byte integer
Length: 2-byte integer
Checksum: 2-byte integer
Address: 4-byte IP address

## Slide 491: A Few Programming Notes: Building a Packet in a Buffer
struct packet {
u_int32_t type;
u_int16_t length;
u_int16_t checksum;
u_int32_t address;
};
/* ================================================== */
char buf[1024];
struct packet *pkt;
pkt = (struct packet*) buf;
pkt->type = htonl(1);
pkt->length = htons(2);
pkt->checksum = htons(3);
pkt->address = htonl(4);

## Slide 492: Socket Programming References
Man page
  usage: man <function name>
Textbook
  Sections 2.6, 2.7
  demo programs written in Java
Unix Network Programming : Networking APIs: Sockets and XTI (Volume 1)
  Section 2, 3, 4, 6, 8
  ultimate socket programming bible!

## Slide 493: Interrupts
When you are at home sitting on your lazy boy how do you know when someone wants to talk to you on the phone?
  Do you periodically get up and pick up the phone to see if someone is there?
  Or do you wait till the phone rings to answer it?

## Slide 494: Interrupts
The first scenario shows a person doing what is known as polling.
The second case illustrates an interrupt-driven person.

## Slide 495: Polling
AKA busy waiting; looping program
Continues checking status register until a particular state exists
Are we there yet? Are we there yet? Are we there yet?
What happens if something occurs at other devices while the processor is busy waiting??

## Slide 496: Interrupt
Device sends a special signal to CPU when data arrives.
Wake me up when we get there.
Responds to hardware interrupt signal by interrupting current processing.
Now CPU can perform tasks before and after interrupt instead of just polling!! Good!
The signaling is done by a Progrmmable Interrupt Controller (PIC).

## Slide 497: Interrupt Flow
Completes current instruction
Saves current state to status registers
Identify source
Jump to and activate Interrupt Service Routing (ISR)
Return to original program (RTI) and restore state
Register
Interrupt driven
CPU
I/O
device
I/O
device

## Slide 498: Interrupts: Flow Chart
SOFTWARE
INTERRUPT
STACK MPU REGISTER CONTENTS
SET APPROPRIATE BIT IN CCR
LOAD INTERRUPT VECTOR INTO PROGRAM COUNTER
VECTOR TABLE
HARDWARE
INTERRUPT
MASK SET?
N
Y
EXECUTE INTERRUPT SERVICE ROUTINE
$FFC0
$FFFF
CONTINUE MAIN PROGRAM

## Slide 499: Interrupt Purpose
To modify or do additional instructions based on internal requests and/or external devices.
Provide a means for suspending current instructions for more important tasks.
Hardware (called Interrupts or Resets)
  Reset
  User-defined interrupt
  Timer operations
  CPU operations monitor failure
Software
  Illegal instruction
  SWI

## Slide 500: Interrupt Purpose / Application Cont.
Coordinating I/O operations
  Notifies the CPU that an input is ready or an output can be changed
Timing
  Periodic (clock-driven) interrupts remind the CPU of the passage of time
    Multi-tasking
    Updating counters
    Timing during interactive programs
Errors
  Interrupts can notify of error situations

## Slide 501: Types of Interrupts
Ignorable interrupts (or Maskable)
  Most often used
  Good for using when computer needs to do something more important
  When the interrupt mask is set interrupts are hidden and therefore are ignored.
Non-ignorable interrupts (Non-maskable)
  NMI’s take precedence and interrupt any task

## Slide 502: Stacking Order
When an interrupt occurs:
2. PIC pushes on stack: PC accumulators and registers CCR
3. PIC sets the I-bit Masks interrupts - can’t interrupt an interrupt
4. Looks up vector of highest-priority interrupt
5. Branches to interrupt service routine
Executes until RTI is encountered
6. Restores accumulators and registers CCR from stack (note: this includes restoring the I-bit of CCR)
7. Returns to instruction after the one that was interrupted
(note: other interrupts may be pending now)
1. Finish execution of the current instruction Note: Non-maskable interrupts and resets happen immediately

## Slide 503: Controlling Interrupts
Exists as bit 4 in the Condition Code Register (CCR)
  When set (I=1) interrupts will be inhibited and placed as pending
  When cleared (I=0) interrupt servicing will be allowed when asked
The I bit is always set while servicing an interrupt; Interrupts can’t nest
Set during RESET to allow minimum system initialization

## Slide 504: I Bit continued
Can also be set by software to prevent execution of maskable interrupts
  SEI (SEt Interrupt Mask)
Can be cleared by software instructions
  CLI (CLear Interrupt Mask)
Automatically cleared by RTI instruction

## Slide 505: Deferred Interrupt Handling
Standard ISR Processing Standard ISR processing will typically involve recording the reason for the interrupt clearing the interrupt then performing any processing necessitated by the interrupt all within the ISR itself.
Deferred Interrupt Processing Deferred interrupt processing will typically involve recording the reason for the interrupt and clearing the interrupt within the ISR but then unblocking an RTOS task so the processing necessitated by the interrupt can be performed by the unblocked task rather than within the ISR.

## Slide 506: Deferred Interrupt Handling
With reference to the image above:
  At time t2: A low priority task is pre-empted by an interrupt.
  At time t3: The ISR returns directly to a task that was unblocked from within the ISR. The majority of interrupt processing is performed within the unblocked task.
  At time t4: The task that was unblocked by the ISR returns to the Blocked state to wait for the next interrupt allowing the lower priority application task to continue its execution.

## Slide 507: CHAPTER 10
8051SERIAL PORT PROGRAMMING

## Slide 508: Basics of Serial Communication
Computers transfer data in two ways:
  Parallel
    Often 8 or more lines (wire conductors) are used to transfer data to a device that is only a few feet away
  Serial
    To transfer to a device located many meters away, the serial method is used
      The data is sent one bit at a time

## Slide 509: Basics of Serial Communication
  At the transmitting end, the byte of data must be converted to serial bits
    Using a parallel-in-serial-out shift register
  At the receiving end, the serial data is received and packed into byte
    Using a serial-in-parallel-out shift register

## Slide 510: Basics of Serial Communication
  When the distance is short, the digital signal can be transferred as it is on a simple wire and requires no modulation
  If data is to be transferred on the telephone line, it must be converted from 0s and 1s to audio tones
    This conversion is performed by a device called a modem, “Modulator/demodulator”

## Slide 511: Basics of Serial Communication
Serial data communication uses two methods:
  Synchronous method transfers a block of data at a time
  Asynchronous method transfers a single byte at a time
It is possible to write software to use either of these methods
  The programs can be tedious and long

## Slide 512: Basics of Serial Communication
There are special IC chips made by many manufacturers for serial communications:
  UART (universal asynchronous receiver transmitter)
  USART (universal synchronous asynchronous receiver transmitter)

## Slide 513: Half- and Full-Duplex Transmission
If data can be transmitted and received, it is a duplex transmission
  If data transmitted one way a time, it is referred to as half duplex
  If data can go both ways at a time, it is full duplex
This is contrast to simplex transmission

## Slide 515: Start and Stop Bits
A protocol is a set of rules agreed by both the sender and receiver on:
  How the data is packed
  How many bits constitute a character
  When the data begins and ends
Asynchronous serial data communication is widely used for character-oriented transmissions
  Each character is placed in between start and stop bits, this is called framing

## Slide 516: Start and Stop Bits (cont.)
    The start bit is always one bit
    The stop bit can be one or two bits
    The start bit is always a 0 (low)
    The stop bit(s) is 1 (high)
Block-oriented data transfers use the synchronous method

## Slide 518: Start and Stop Bits (cont.)
Due to the extended ASCII characters, 8-bit ASCII data is common
  In older systems, ASCII characters were 7-bit
In modern PCs the use of one stop bit is standard
  In older systems, two stop bits were used
    Due to the slowness of the receiving mechanical device
    To give the device sufficient time to organize itself before transmission of the next byte

## Slide 519: Start and Stop Bits (cont.)
Assuming that we are transferring a text file of ASCII characters using 1 stop bit
  We have a total of 10 bits for each character
    This gives 20% overhead
In some systems, to maintain data integrity, the parity bit of the character byte is included in the data frame
  UART chips allow programming of the parity bit for odd-, even-, and no-parity options

## Slide 520: Data Transfer Rate
The rate of data transfer in serial data communication is stated in bps (bits per second)
Another widely used terminology for bps is baud rate
  It is modem terminology and is defined as the number of signal changes per second
    In modems, there are occasions when a single change of signal transfers several bits of data

## Slide 521: Data Transfer Rate (cont.)
  As far as the conductor wire is concerned, the baud rate and bps are the same
The data transfer rate of given computer system depends on communication ports incorporated into that system
  IBM PC/XT could transfer data at the rate of 100 to 9600 bps
  Pentium-based PCs transfer data at rates as high as 56K bps
  In asynchronous serial data communication, the baud rate is limited to 100K bps

## Slide 522: RS232 Standards
An interfacing standard RS232 was set by the Electronics Industries Association (EIA) in 1960
  The standard was set long before the advent of the TTL logic family, its input and output voltage levels are not TTL compatible
  A 1 is represented by -3 ~ -25 V
  A 0 bit is +3 ~ +25 V
    Making -3 to +3 undefined

## Slide 524: RS232 Standards (cont.)
Since not all pins are used in PC cables, IBM introduced the DB-9 version of the serial I/O standard

## Slide 525: Data Communication Classification
Current terminology classifies data communication equipment as:
  DTE (data terminal equipment)
    Terminal and computers that send and receive data
  DCE (data communication equipment)
    Communication equipment, such as modems
The simplest connection between a PC and microcontroller at least requires:
  Three pins, TxD, RxD, and ground

## Slide 526: RS232 Pins
DTR (data terminal ready)
  When terminal is turned on, it sends out signal DTR to indicate that it is ready for communication
DSR (data set ready)
  When DCE is turned on and has gone through the self-test, it assert DSR to indicate that it is ready to communicate

## Slide 527: RS232 Pins (cont.)
RTS (request to send)
  When the DTE device has byte to transmit, it asserts RTS to signal the modem that it has a byte of data to transmit
CTS (clear to send)
  When the modem has room for storing the data it is to receive, it sends out signal CTS to DTE to indicate that it can receive the data now

## Slide 528: RS232 Pins (cont.)
DCD (data carrier detect)
  The modem asserts signal DCD to inform the DTE that a valid carrier has been detected and that contact between it and the other modem is established
RI (ring indicator)
  An output from the modem and an input to a PC indicates that the telephone is ringing
  It goes on and off in synchronous with the ringing sound

## Slide 529: 8051 Connection to RS232
A line driver such as the MAX232 chip is required to convert RS232 voltage levels to TTL levels, and vice versa
8051 has two pins that are used specifically for transferring and receiving data serially
  These two pins are called TxD and RxD
    Part of the port 3 group (P3.0 and P3.1)
    These pins are TTL compatible
      They require a line driver to make them RS232 compatible

## Slide 531: MAX233
To save board space, some designers use MAX233 chip from Maxim
  MAX233 performs the same job as MAX232
    But eliminates the need for capacitors
    MAX233 and MAX232 are not pin compatible

## Slide 532: Serial Communication Programming
To allow data transfer between the PC and an 8051 system without any error
  The baud rate of 8051 system must match the baud rate of the PC’s COM port

## Slide 535: SBUF Register
SBUF is an 8-bit register used solely for serial communication
  For a byte data to be transferred via the TxD line, it must be placed in the SBUF register
    The moment a byte is written into SBUF, it is framed with the start and stop bits and transferred serially via the TxD line
  SBUF holds the byte of data when it is received by 8051 RxD line
    When the bits are received serially via RxD, the 8051 deframes it by eliminating the stop and start bits, and then placing the byte in SBUF

## Slide 536: SCON Register
SCON is an 8-bit register used to program the start bit, stop bit, and data bits of data framing, among other things

## Slide 537: SCON Register (cont.)
SM0, SM1
  They determine the framing of data by specifying the number of bits per character, and the start and stop bits
SM2
  This enables the multiprocessing capability of the 8051

## Slide 538: SCON Register (cont.)
REN (receive enable)
  When it is high, it allows 8051 to receive data on RxD pin
  If low, the receiver is disable
TI (transmit interrupt)
  When 8051 finishes the transfer of 8-bit character
    It raises TI flag to indicate that it is ready to transfer another byte
    TI bit is raised at the beginning of the stop bit

## Slide 539: SCON Register (cont.)
RI (receive interrupt)
  When 8051 receives data serially via RxD, it gets rid of the start and stop bits and places the byte in SBUF register
    It raises the RI flag bit to indicate that a byte has been received and should be picked up before it is lost
    RI is raised halfway through the stop bit
SCON is a bit-addressable register

## Slide 540: Programming Serial Data Transmitting
In programming the 8051 to transfer character bytes serially
  TMOD register is loaded with the value 20H
    Indicating the use of timer 1 in mode 2 (8-bit auto-reload) to set baud rate
  The TH1 is loaded with one of the values to set baud rate for serial data transfer
  SCON register is loaded with the value 50H
    Indicating serial mode 1, where an 8-bit data is framed with start and stop bits

## Slide 541: Programming Serial Data Transmitting
  TR1 is set to 1 to start timer 1
  TI is cleared by CLR TI instruction
  The character byte to be transferred serially is written into SBUF register
  The TI flag bit is monitored with the use of instruction JNB TI, xx to see if the character has been transferred completely
  To transfer the next byte, go to step 5

## Slide 544: Importance of TI Flag
The steps that 8051 goes through in transmitting a character via TxD
  The byte character to be transmitted is written into the SBUF register
  The start bit is transferred
  The 8-bit character is transferred on bit at a time
  The stop bit is transferred
    It is during the transfer of the stop bit that 8051 raises the TI flag
      Indicating that the last character was transmitted

## Slide 545: Importance of TI Flag (cont.)
  By monitoring the TI flag, we make sure that we are not overloading the SBUF
    If we write another byte into the SBUF before TI is raised, the untransmitted portion of the previous byte will be lost
  After SBUF is loaded with a new byte, the TI flag bit must be forced to 0 by CLR TI
    In order for this new byte to be transferred
By checking the TI flag bit, we know whether or not the 8051 is ready to transfer another byte

## Slide 546: Importance of TI Flag (cont.)
It must be noted that TI flag bit is raised by 8051 itself when it finishes data transfer
  It must be cleared by the programmer with instruction CLR TI
    If we write a byte into SBUF before the TI flag bit is raised, we risk the loss of a portion of the byte being transferred
  The TI bit can be checked by
    The instruction JNB TI, xx
    Using an interrupt

## Slide 547: Programming Serial Data Receiving
In programming the 8051 to receive character bytes serially
  TMOD register is loaded with the value 20H
    Indicating the use of timer 1 in mode 2 (8-bit auto-reload) to set baud rate
  TH1 is loaded to set baud rate
  SCON register is loaded with the value 50H
    Indicating serial mode 1, where an 8-bit data is framed with start and stop bits
  TR1 is set to 1 to start timer 1

## Slide 548: Programming Serial Data Receiving
  RI is cleared by CLR RI instruction
  The RI flag bit is monitored with the use of instruction JNB RI,xx to see if an entire character has been received yet
  When RI is raised, SBUF has the byte, and its contents are moved into a safe place
  To receive the next character, go to step 5

## Slide 550
MOVC

## Slide 553: Importance of RI Flag
In receiving bit via its RxD pin, 8051 goes through the following steps
  It receives the start bit
    Indicating that the next bit is the first bit of the character byte it is about to receive
  The 8-bit character is received one bit at a time
  The stop bit is received
    When receiving the stop bit 8051 makes RI = 1,
      Indicating that an entire character byte has been received and must be picked up before it gets overwritten by an incoming character

## Slide 554: Importance of RI Flag (cont.)
  By checking the RI flag bit when it is raised
    We know that a character has been received and is sitting in the SBUF register
      We copy the SBUF contents to a safe place in some other register or memory before it is lost
  After the SBUF contents are copied, the RI flag bit must be forced to 0 by CLR RI
    In order to allow the next received character byte to be placed in SBUF
      Failure to do this causes loss of the received character
By checking the RI flag bit, we know when the 8051 has received a character byte

## Slide 555: Importance of RI Flag (cont.)
  If we failed to copy SBUF into a safe place, we risk the loss of the received byte
  It must be noted that RI flag bit is raised by 8051 when it finish receive data
  It must be cleared by the programmer with instruction CLR RI
  If we copy SBUF into a safe place before the RI flag bit is raised, we risk copying garbage
The RI bit can be checked by
  The instruction JNB RI, xx
  Using an interrupt

## Slide 556: Doubling Baud Rate
There are two ways to increase the baud rate of data transfer
  To use a higher frequency crystal
    The system crystal is fixed
  To change a bit in the PCON register
    PCON register is an 8-bit register
      It is not a bit-addressable register
    When 8051 is powered up, SMOD is zero
    We can set it to high by software and thereby double the baud rate

## Slide 558
TI, H_1
A_1

## Slide 562: Programming the Second Serial Port
Many new generations of 8051 microcontroller have two serial ports
  Like DS89C4x0 and DS80C320
  The second serial port of DS89C4x0 uses pins P1.2 and P1.3 for the Rx and Tx lines
  The second serial port uses some reserved SFR addresses for the SCON and SBUF
    There is no universal agreement among the makers as to which addresses should be used
    The SFR addresses of C0H and C1H are set aside for SBUF and SCON of DS89C4x0

## Slide 564: Programming the Second Serial Port
    The DS89C4x0 technical documentation refers to these registers as SCON1 and SBUF1
    The first ones are designated as SCON0 and SBUF0
    Upon reset, DS89c4x0 uses Timer 1 for setting baud rate of both serial ports

## Slide 565: Programming the Second Serial Port
      While each serial port has its own SCON and SBUF registers
  SBUF and SCON refer to the SFR registers of the first serial port
  Since the older 8051 assemblers do not support this new second serial port, we need to define them in program
    To avoid confusion, in DS89C4x0 programs we use SCON0 and SBUF0 for the first and SCON1 and SBUF1for the second serial ports

## Slide 567
SJMP FN
SBUF1 EQU 0C1H

## Slide 568
SJMP LN

## Slide 569: Time and Clock Synchronisation

## Slide 570: Famous example
Scud rockets launched by Iraq towards Israel
Ground-based Patriot missiles fire back
But missiles always missed the warhead!
Why?

## Slide 571: Famous example
Scud rockets launched by Iraq towards Israel
Ground-based Patriot missiles fire back
But missiles always missed the warhead!
Why?
  After 72 hours of waiting control system was out of sync relative to Patriot guidance system
  “be at (x,y,z) at time t” was misinterpreted!

## Slide 572: What is real-time? Is there any other kind?
A real-time computer system is a computer system where the correctness of the system behavior depends not only on the logical results of the computations, but also on the physical time when these results are produced.
By system behavior we mean the sequence of outputs in time of a system.

## Slide 573: Real-time means reactive
A real-time computer system must react to stimuli from its environment
The instant when a result must be produced is called a deadline.
If a result has utility even after the deadline has passed, the deadline is classified as soft, otherwise it is firm.
If severe consequences could result if a firm deadline is missed, the deadline is called hard.
Example: Consider a traffic signal at a road before a railway crossing. If the traffic signal does not change to red before the train arrives, an accident could result.

## Slide 574: Distributed RT system model
From the POV of an outside observer, a real-time (RT) system can be decomposed into three communicating subsystems:
  a controlled object (the physical subsystem, the behavior of which is governed by the laws of physics),
  a “distributed” computer subsystem (the cyber system, the behavior of which is governed by the programs that are executed on digital computers)
  a human user or operator
The distributed computer system consists of computational nodes that interact by the exchange of messages.
A computational node can host one or more computational components.

## Slide 575: Design Challenges in Distributed Systems
Theoretically, a distributed system features the same design challenges as a centralized embedded system in terms of performance, power consumption, battery life, etc.
However, an additional challenge exists: synchronization between nodes

## Slide 576: Definition of time
Newtonian physics time model is adequate for most temporal phenomena and is much simpler than relativistic time
Time is modeled as an infinite set [T] with the following properties:
  {T} is an ordered set, that is, if p and q are any two instants, then either p is simultaneous with q, or p precedes q, or q precedes p, where these relations are mutually exclusive. We call the order of instants on the timeline the temporal order.
  {T} is a dense set. This means that there is at least one q between p and r iff p is not the same instant as r, where p, q, and r are instants.

## Slide 577: Events in the time model
A section of the time line between two different instants is called a duration.
An event takes place at an instant of time and does not have a duration.
If two events occur at the same instant, then the two events are said to occur simultaneously.
Instants are totally ordered; however, events are only partially ordered,
Events can be totally ordered if another criterion is introduced to order events that occur simultaneously

## Slide 578: Causal order
In many real time systems determining cause and effect relations between events is of interest, especially determining the primary event
Temporal order is necessary but not sufficient to establish causal order

## Slide 579: Global time
An important yet challenging task is maintaining a consistent global time in a distributed real-time system
There is no global clock, only local clocks
Local clocks drift arbitrarily
No local clock is always correct
A global time is an abstract notion that is approximated by properly selected microticks from the synchronized local physical clocks of an ensemble.

## Slide 580: Global time
Assume a set of nodes, each one with its own local physical clock that ticks with granularity . Assume that all of the clocks are internally synchronized with a precision Π, i.e., for any two clocks j, k, and all microticks i
It is then possible to select a subset of the microticks of each local clock k for the generation of the local implementation of a global notion of time.
We call such a selected local microtick i a macrotick (or a tick) of the global time.
For example, every tenth microtick of a local clock k may be interpreted as the global tick, the macrotick , of this clock (see Fig. 3.2).
If it does not matter at which clock k the (macro) tick occurs, we denote the tick ti without a superscript.
A global time is thus an abstract notion that is approximated by properly selected microticks from the synchronized local physical clocks of an ensemble.

## Slide 581: Reasonable global time
The global time t is called reasonable, if all local implementations of the global time satisfy the condition
g>Π
Then for a single event e, that is observed by any two different clocks of the ensemble, their global time-stamps can differ by at most one tick.
This is the best we can achieve.

## Slide 582: Temporal order
When to events differ by less than two ticks temporal order cannot be maintained

## Slide 583: Errors in duration measurement

## Slide 584: Logical Clocks
For many DS algorithms, associating an event to an absolute real time is not essential, we only need to know an unambiguous order of events
    Lamport's timestamps
    Vector timestamps

## Slide 585: Logical Clocks (Cont.)
Synchronization based on “relative time”.
      Example: Unix make (Is output.c updated after the generation of output.o?)
“relative time” may not relate to the “real time”.
What’s important is that the processes in the Distributed System agree on the ordering in which certain events occur.
Such “clocks” are referred to as Logical Clocks.

## Slide 586: Example: Why Order Matters?
  Replicated accounts in New York(NY) and San Francisco(SF)
  Two updates occur at the same time
    Current balance: $1,000
    Update1: Add $100 at SF; Update2: Add interest of 1% at NY
    Whoops, inconsistent states!

## Slide 587: Lamport Algorithm
Clock synchronization does not have to be exact
  Synchronization not needed if there is no interaction between machines
  Synchronization only needed when machines communicate
  i.e. must only agree on ordering of interacting events

## Slide 588: Lamport’s “Happens-Before” Partial Order
Given two events e & e’, e < e’ if:
Same process: e <i e’, for some process Pi
Same message: e = send(m) and e’=receive(m) for some message m
Transitivity: there is an event e* such that e < e* and e* < e’

## Slide 589: Concurrent Events
Given two events e & e’:
If neither e < e’ nor e’< e, then e || e’
P1
P2
P3
Real Time
a
b
c
f
d
e
m1
m2
Notes: Note that if two events happen without any message, then we can't say anything about their relative occurrence in time.
In this example a <= b <= c <= d <= f, but we can say little about e other than e <= f. We say that events such as a and e are concurrent.
Note also that “happens before” does not demonstrate causality. There is merely the potential for causality.

## Slide 590: Lamport Logical Clocks
Substitute synchronized clocks with a global ordering of events
  ei < ej  LC(ei) < LC(ej)
  LCi is a local clock: contains increasing values
    each process i has own LCi
  Increment LCi on each event occurrence
  within same process i, if ej occurs before ek
    LCi(ej) < LCi(ek)
  If es is a send event and er receives that send, then
    LCi(es) < LCj(er)

## Slide 591: Lamport Algorithm
Each process increments local clock between any two successive events
Message contains a timestamp
Upon receiving a message, if received timestamp is ahead, receiver fast forward its clock to be one more than sending time

## Slide 592: Lamport Algorithm (cont.)
Timestamp
  Each event is given a timestamp t
  If es is a send message m from pi, then t=LCi(es)
  When pj receives m, set LCj value as follows
    If t < LCj, increment LCj by one
      Message regarded as next event on j
    If t ≥ LCj, set LCj to t+1

## Slide 593: Lamport’s Algorithm Analysis (1)
Claim: ei < ej  LC(ei) < LC(ej)
Proof: by induction on the length of the sequence of events relating to ei and ej
P1
P2
P3
Real Time
a
b
c
f
d
e
m1
m2
1
2
3
5
4
1
g
5

## Slide 594: Lamport’s Algorithm Analysis (2)
LC(ei) < LC(ej)  ei < ej ?
Claim: if LC(ei) < LC(ej), then it is not necessarily true that ei < ej
P1
P2
P3
Real Time
a
b
c
f
d
e
m1
m2
1
2
3
5
4
1
g
2

## Slide 595: Total Ordering of Events
Happens before is only a partial order
Make the timestamp of an event e of process Pi be:
(LC(e),i)
(a,b) < (c,d) iff a < c, or a = c and b < d

## Slide 596: Application: Totally-Ordered Multicasting
  Message is timestamped with sender’s logical time
  Message is multicast (including sender itself)
  When message is received
    It is put into local queue
    Ordered according to timestamp
    Multicast acknowledgement
  Message is delivered to applications only when
    It is at head of queue
    It has been acknowledged by all involved processes

## Slide 597: Application: Totally-Ordered Multicasting
Update 1 is time-stamped and multicast. Added to local queues.
Update 2 is time-stamped and multicast. Added to local queues.
Acknowledgements for Update 2 sent/received. Update 2 can now be processed.
Acknowledgements for Update 1 sent/received. Update 1 can now be processed.
(Note: all queues are the same, as the timestamps have been used to ensure the “happens-before” relation holds.)

## Slide 598: Limitation of Lamport’s Algorithm
ei < ej  LC(ei) < LC(ej)
However, LC(ei) < LC(ej) does not imply ei < ej
  for instance, (1,1) < (1,3), but events a and e are concurrent
P1
P2
P3
Real Time
a
b
c
f
d
e
m1
m2
(1,1)
(2,1)
(3,2)
(5,3)
(4,2)
(1,3)
g
(2,3)

## Slide 599: Synchronizing Clocks
External clock synchronization (Cristian)
Internal clock synchronization (Gusella & Zatti)
Network Time Protocol (Mills)

## Slide 600: Logical Clocks
Pros:
  Can be used to totally order events (Lamport)
  Can be used to partially order events (Fidge)
  Can be used to determine “happened before” relationships (Comparison Property)
Cons:
  Do not represent real time
  Cannot be used to determine order of events in relation to events external to the system

## Slide 601: Physical Clocks
Are used to closely approximate real time
Pros:
  Can be used to record the occurrence of events for later analysis
  Can be used to instruct a system to take certain actions when real time deadlines occur
  Can be used to order the occurrence of related events observed by different systems
Cons:
  Every clock must be synchronized
  Clocks can be incorrect

## Slide 602: Clock Correctness
A physical clock H is correct for a real-time interval [ti, tj], if
(1 – p)(tj – ti) ≤ H(tj) – H(ti) ≤ (1 + p)(tj – ti)
Where p is the maximum clock drift rate specified by the clock manufacturer

## Slide 603: Clock Drift Rate
Most clocks have a non-zero drift rate (p)
  Usually of the order 10-6 Hz
Assume p = 0.000001
  Day: 0.0864 seconds
  Week: 0.6048 seconds
  Month: 2.5920 seconds
  Year: 31.536 seconds
Hence, if the clock drifts more than 31.536 seconds in one year, the clock is not correct

## Slide 604: Rapport
Rapport:
  When one clock is synchronized with another clock
Two methods of reaching rapport
  Internal clock synchronization:
    Maintaining processor clocks within some maximum deviation of each other
  External clock synchronization:
    Maintaining processor clocks within some maximum deviation of a clock external to the system

## Slide 605: Internal Clock Synchronization
For all pairs of processes i and j, and for any real time t:
|Ci(t) – Cj(t)| ≤ D
Where:
  Cx is the clock of process x
  D is a constant

## Slide 606: External Clock Synchronization
For any process i, and for any real time t:
|Ci(t) – E(t)| ≤ D
Where:
  Cx is the clock of process x
  D is a constant
  E is a clock external to the system

## Slide 607: Internal vs. External
Internal:
  All clocks agree within the bound D
  Entire system can drift arbitrarily far from real time
External:
  All clocks are accurate within the bound D
  Externally synchronized clocks are also internally synchronized with a bound of 2D
    Some clock could be within –D of external clock
    Some clock could be within +D of external clock

## Slide 608: Cristian Algorithm
An external clock synchronization method
Assumptions:
  Process clocks are correct
  Unbounded random message delays
  Timeout delay is used to let processes continue to work despite process failures and lost messages
Probabilistic:
  Does not guarantee successful remote clock readings
  If successful, the reading precision is known

## Slide 609: Cristian Algorithm
At real time t1, a client sends a request message (“time=?”) to the external clock server
t1
Server
Client
(“time=?”)
E(t)
C(t)

## Slide 610: Cristian Algorithm
At real time t2, the server receives the request
t1
Server
Client
(“time=?”)
E(t)
C(t)
t2

## Slide 611: Cristian Algorithm
At real time t3, the server sends its time in a message (“time=”, E(t3)) to the client
t1
Server
Client
(“time=?”)
E(t)
C(t)
t2
(“time=”, E(t3))
t3

## Slide 612: Cristian Algorithm
At real time t4, the client receives the message and sets its clock to E(t3) plus half of the round trip delay
t1
Server
Client
(“time=?”)
E(t)
C(t)
t2
(“time=”, E(t3))
t3
t4
C(t4) = E(t3) + (R/2)
R = C(t4) – C(t1)

## Slide 613
t1
Server
Client
(“time=?”)
E(t)
C(t)
t2
(“time=”, E(t3))
t3
t4
C(t4) = ?
R = ?

## Slide 614: Maximum Error
The maximum error e that P can make when reading Q’s clock is half the length of the interval
Hence,
e = D(1 + 2p) – min

## Slide 615: Synchronizing Clocks
External clock synchronization (Cristian)
Internal clock synchronization (Gusella & Zatti)
Network Time Protocol (Mills)

## Slide 616: Clock Difference Algorithm
At real time t1, node A sends a TimeStamp message request to node B
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)

## Slide 617: Clock Difference Algorithm
At real time t2, node B responds with a TimeStampReply message that carries CB(t2)
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)
t2
TimeStampReply

## Slide 618: Clock Difference Algorithm
At real time t3, node A receives B’s reply and calculates the difference between the clocks as
ΔAB(t) = –––––––––––– – CB(t2)
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)
t2
TimeStampReply
t3
ΔAB(t) = (CA(t1) + CA(t3))/2 – CB(t2)
CA(t1) + CA(t3)
2

## Slide 619: Clock Difference Example #1
t1 = 10ms, t2 = 20ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 25ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 25 = -5ms
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)
t2
TimeStampReply
t3
ΔAB(t) = (CA(t1) + CA(t3))/2 – CB(t2)

## Slide 620: Clock Difference Example #2
t1 = 10ms, t2 = 12ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 17ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 17 = 3ms
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)
t2
TimeStampReply
t3
ΔAB(t) = (CA(t1) + CA(t3))/2 – CB(t2)

## Slide 621: Clock Difference Example #3
t1 = 10ms, t2 = 28ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 33ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 33 = -13ms
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)
t2
TimeStampReply
t3
ΔAB(t) = (CA(t1) + CA(t3))/2 – CB(t2)

## Slide 622: Maximum Clock Difference Error
Let TmAB and TmBA be the minimal possible transmission times from A to B and vice versa
If the round trip is bounded by Tmax, then the maximum error of ΔAB is
ε = ––––––––––––––––––––– ≥ 0
Tmax – 2*min(TmAB, TmBA)
2

## Slide 623: Clock Difference Example #2
t1 = 10ms, t2 = 12ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 17ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 17 = 3ms
TmAB = 2ms, TmBA = 2ms, Tmax = 20ms
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)
t2
TimeStampReply
t3
ΔAB(t) = (CA(t1) + CA(t3))/2 – CB(t2)

## Slide 624: Clock Difference Example #2
t1 = 10ms, t2 = 12ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 17ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 17 = 3ms
TmAB = 2ms, TmBA = 2ms, Tmax = 20ms
ε = (Tmax – 2*min(TmAB, TmBA))/2 ≥ 0
ε = (20 – 2*2)/2 = 8ms
True clock difference = CA(t1) – CB(t1) = 10 – 15 = -5ms
Calculated clock difference = ΔAB(t) = 3ms
Clock difference error = ΔAB(t) – (CA(t1) – CB(t1)) = 8ms

## Slide 625: Clock Difference Example #2
t1 = 10ms, t2 = 12ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 17ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 17 = 3ms
TmAB = 2ms, TmBA = 2ms, Tmax = 40ms
ε = (Tmax – 2*min(TmAB, TmBA))/2 ≥ 0
ε = (40 – 2*2)/2 = 18ms
True clock difference = CA(t1) – CB(t1) = 10 – 15 = -5ms
Calculated clock difference = ΔAB(t) = 3ms
Clock difference error = ΔAB(t) – (CA(t1) – CB(t1)) = 8ms

## Slide 626: Clock Difference Example #3
t1 = 10ms, t2 = 28ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 33ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 33 = -13ms
TmAB = 2ms, TmBA = 2ms, Tmax = 20ms
t1
Node B
Node A
TimeStamp
CB(t)
CA(t)
t2
TimeStampReply
t3
ΔAB(t) = (CA(t1) + CA(t3))/2 – CB(t2)

## Slide 627: Clock Difference Example #3
t1 = 10ms, t2 = 28ms, t3 = 30ms
CA(t1) = 10ms, CB(t1) = 15ms, CB(t2) = 33ms, CA(t3) = 30ms
ΔAB(t) = (10 + 30)/2 – 33 = -13ms
TmAB = 2ms, TmBA = 2ms, Tmax = 20ms
ε = (Tmax – 2*min(TmAB, TmBA))/2 ≥ 0
ε = (20 – 2*2)/2 = 8ms
True clock difference = CA(t1) – CB(t1) = 10 – 15 = -5ms
Calculated clock difference = ΔAB(t) = -13ms
Clock difference error = ΔAB(t) – (CA(t1) – CB(t1)) = -8ms

## Slide 628: Berkeley Algorithm
Performs internal synchronization
Uses a master-slave approach:
  An election algorithm is used to pick the master
  The master periodically requests all slaves to send their clock values to it
  The clock difference algorithm is used to determine the difference between each clock and the master’s
  A fault-tolerant averaging function is used to determine the average time difference of the system
  The master then sends a clock adjustment to each process to internally synchronize the system

## Slide 629: Averaging Function
Selects the largest set of clocks that do not differ from each other more than ϒ and averages the differences of these clocks
Prevents malfunctioning clocks and clocks with abnormally large drift rates from adversely affecting the synchronization process
Clocks not selected by the fault-tolerant averaging function are considered faulty

## Slide 630: Berkeley Example #1
System = {A, B, C, D, E}, where A is the master
True clock differences:
  CA(t1) – CA(t1) = 30 – 30 = 0ms
  CA(t1) – CB(t1) = 30 – 15 = 15ms
  CA(t1) – CC(t1) = 30 – 45 = -15ms
  CA(t1) – CD(t1) = 30 – 30 = 0ms
  CA(t1) – CE(t1) = 30 – 35 = -5ms
Calculated clock differences:
  ΔAA(t) = 0ms
  ΔAB(t) = (30 + 50)/2 – 25 = 15ms
  ΔAC(t) = (30 + 50)/2 – 55 = -15ms
  ΔAD(t) = (30 + 50)/2 – 40 = 0ms
  ΔAE(t) = (30 + 50)/2 – 45 = -5ms

## Slide 631: Berkeley Example #1
Calculated clock differences:
  ΔAA(t) = 0ms
  ΔAB(t) = (30 + 50)/2 – 25 = 15ms
  ΔAC(t) = (30 + 50)/2 – 55 = -15ms
  ΔAD(t) = (30 + 50)/2 – 40 = 0ms
  ΔAE(t) = (30 + 50)/2 – 45 = -5ms
Assume ϒ = 20ms, the averaging function will select {A, C, D, E} because it is the largest set with range ϒ
The average clock difference is calculated:
Δ(t) = (0 + -15 + 0 + -5)/4 = -5ms

## Slide 632: Berkeley Example #1
Clock adjustments are calculated:
  δA = Δ(t) + ΔAA(t) = -5 + 0 = -5ms
  δB = Δ(t) + ΔAB(t) = -5 + 15 = 10ms
  δC = Δ(t) + ΔAC(t) = -5 + -15 = -20ms
  δD = Δ(t) + ΔAD(t) = -5 + 0 = -5ms
  δE = Δ(t) + ΔAE(t) = -5 + -5 = -10ms
The master A then sends these adjustments to each process, which in turn directly applies the adjustment to its clock value

## Slide 633: Berkeley Example #1
Applied clock adjustments:
  CA(t1 + 100) = CA(t1 + 100) + δA = (30 + 100) + -5 = 125ms
  CB(t1 + 100) = CB(t1 + 100) + δB = (15 + 100) + 10 = 125ms
  CC(t1 + 100) = CC(t1 + 100) + δC = (45 + 100) + -20 = 125ms
  CD(t1 + 100) = CD(t1 + 100) + δD = (30 + 100) + -5 = 125ms
  CE(t1 + 100) = CE(t1 + 100) + δE = (35 + 100) + -10 = 125ms
Perfect synchronization achieved with perfect conditions (e.g., consistent message delays)

## Slide 634: Berkeley Example #2
System = {A, B, C, D, E}, where A is the master
True clock differences:
  CA(t1) – CA(t1) = 30 – 30 = 0ms
  CA(t1) – CB(t1) = 30 – 15 = 15ms
  CA(t1) – CC(t1) = 30 – 45 = -15ms
  CA(t1) – CD(t1) = 30 – 30 = 0ms
  CA(t1) – CE(t1) = 30 – 35 = -5ms
Calculated clock differences:
  ΔAA(t) = 0ms
  ΔAB(t) = (30 + 46)/2 – 25 = 13ms
  ΔAC(t) = (30 + 50)/2 – 55 = -15ms
  ΔAD(t) = (30 + 56)/2 – 40 = 3ms
  ΔAE(t) = (30 + 60)/2 – 45 = 0ms

## Slide 635: Berkeley Example #2
Calculated clock differences:
  ΔAA(t) = 0ms
  ΔAB(t) = (30 + 46)/2 – 25 = 13ms
  ΔAC(t) = (30 + 50)/2 – 55 = -15ms
  ΔAD(t) = (30 + 56)/2 – 40 = 3ms
  ΔAE(t) = (30 + 60)/2 – 45 = 0ms
Assume ϒ = 15ms, the averaging function will select {A, B, D, E} because it is the largest set with range ϒ
The average clock difference is calculated:
Δ(t) = (0 + 13 + 3 + 0)/4 = 4ms

## Slide 636: Berkeley Example #2
Clock adjustments are calculated:
  δA = Δ(t) + ΔAA(t) = 4 + 0 = 4ms
  δB = Δ(t) + ΔAB(t) = 4 + 13 = 17ms
  δC = Δ(t) + ΔAC(t) = 4 + -15 = -11ms
  δD = Δ(t) + ΔAD(t) = 4 + 3 = 7ms
  δE = Δ(t) + ΔAE(t) = 4 + 0 = 4ms
The master A then sends these adjustments to each process, which in turn directly applies the adjustment to its clock value

## Slide 637: Berkeley Example #2
Applied clock adjustments:
  CA(t1 + 100) = CA(t1 + 100) + δA = (30 + 100) + 4 = 134ms
  CB(t1 + 100) = CB(t1 + 100) + δB = (15 + 100) + 17 = 132ms
  CC(t1 + 100) = CC(t1 + 100) + δC = (45 + 100) + -11 = 134ms
  CD(t1 + 100) = CD(t1 + 100) + δD = (30 + 100) + 7 = 137ms
  CE(t1 + 100) = CE(t1 + 100) + δE = (35 + 100) + 4 = 139ms
Approximate synchronization achieved with less-than-perfect conditions

## Slide 638: Amortization
Negative clock adjustment values are possible
To preserve monotonicity, adjustments are implemented by slowing down or speeding up the clock counter rate

## Slide 639: Synchronizing Clocks
External clock synchronization (Cristian)
Internal clock synchronization (Gusella & Zatti)
Network Time Protocol (Mills)

## Slide 640: Network Time Protocol (NTP)
Used to synchronize Internet computer clocks since 1979
Approximately 25 million NTP servers and clients worldwide
NTP is used by PCs, supercomputers, embedded systems, home routers, and even battery backup systems

## Slide 641: NTP Hierarchy
Highest level: primary servers
  Synchronized to a reference clock (e.g., a cesium clock or GPS)
  Stratum 1
Mid level: secondary servers
  Synchronized to a primary server or peer
  Stratum N+1, where N is the minimum hop count to a primary server
Lowest level: user workstation
  Synchronized to a secondary server
Clock accuracy decreases by level

## Slide 642: NTP Usage Examples
Public primary servers:
  U.S. Naval Observatory (USNO)
  National Institute of Standards and Technology (NIST)
  Government agencies in many other countries
Public secondary servers:
  National and regional service providers
Private NTP networks:
  U.S. Government agencies
  Public institutions and universities
  Private corporations

## Slide 643: NTP Example
Stratum 1
Stratum 2
Stratum 2
Stratum 3
Stratum 3
Stratum 3
Reference Clock

## Slide 644: NTP Example
Stratum 1
Stratum 2
???
Stratum 3
Stratum 3
???
Reference Clock

## Slide 645: NTP Example
Stratum 1
Stratum 2
Stratum 3
Stratum 3
Stratum 3
Stratum 3
Reference Clock

## Slide 646: NTP Modes
Broadcast/Multicast
  Server sends synchronization information to all clients at once
Server/Client
  Servers send synchronous information to individual clients based on a schedule or requests
Peer
  Each peer shares its time information but no process has authority over another

## Slide 647: Broadcast/Multicast Mode
Stratum 1
Stratum 2
Stratum 2
Stratum 3
Stratum 3
Stratum 3
Reference Clock

## Slide 648: Server/Client Mode
Stratum 1
Stratum 2
Stratum 2
Stratum 3
Stratum 3
Stratum 3
Reference Clock

## Slide 649: Peer Mode
Stratum 1
Stratum 2
Stratum 2
Stratum 3
Stratum 3
Stratum 3
Reference Clock

## Slide 650: NTP Architecture
Peer process runs when a packet is received
Poll process sends packets at intervals determined by the clock discipline process and remote server
Remote Servers
Network
Clock Filter
Clock Filter
Clock Filter
Selection
and
Clustering
Algorithms
Combining
Algorithm
Loop Filter
VFO
Clock Discipline
Process
System Process
Peer/Poll Processes
Clock Adjust
Process

## Slide 651: NTP Architecture
System process runs when a new update is received
Remote Servers
Network
Clock Filter
Clock Filter
Clock Filter
Selection
and
Clustering
Algorithms
Combining
Algorithm
Loop Filter
VFO
Clock Discipline
Process
System Process
Peer/Poll Processes
Clock Adjust
Process

## Slide 652: NTP Architecture
Clock discipline process implements clock time adjustments
Remote Servers
Network
Clock Filter
Clock Filter
Clock Filter
Selection
and
Clustering
Algorithms
Combining
Algorithm
Loop Filter
VFO
Clock Discipline
Process
System Process
Peer/Poll Processes
Clock Adjust
Process

## Slide 653: NTP Architecture
Clock adjust process controls the variable frequency oscillator (VFO) frequency, which furnishes the time reference to produce the timestamps
Remote Servers
Network
Clock Filter
Clock Filter
Clock Filter
Selection
and
Clustering
Algorithms
Combining
Algorithm
Loop Filter
VFO
Clock Discipline
Process
System Process
Peer/Poll Processes
Clock Adjust
Process

## Slide 654: Clock Selection Algorithm
Determines from among all peers a suitable subset capable of providing the most accurate and trustworthy time.
  Interval intersections are used to determine “falsetickers”
  Clustering and maximum likelihood principles to improve accuracy
  Resulting offsets of subset are combined on a weighted-average basis

## Slide 655: Clock Discipline Algorithm
Uses a feedback loop in which the combined offset is processed by the loop filter to control the variable frequency oscillator (VFO) frequency

## Slide 656: Clock Adjust Algorithm
Implements the VFO as a programmable counter using a combination of hardware and software components
Furnishes the time reference to produce timestamps used in timing calculations

## Slide 657: Precision Time Protocol
IEEE1588v2
TICTOC BOF IETF Prague 2007

## Slide 658: Agenda
Status
PTPv1 overview
PTPv2 major additions
Transparent clocks
PTP and TICTOC

## Slide 659: The Precision Time Protocol (PTP)
PTPv1 published in 2002
Industries involved:
  v1: Industrial Automation, T&M, Military, Power Generation and Distribution
  v2 : Audio-Visio Bridges (802.1AS), Telecom and Mobile
Symposia in 2003, 2004, 2005, and 2006. 2007 in Vienna
Products: Microprocessors, GPS Linked Clocks, Boundary Clocks, NIC Cards, Protocol Stacks, RF Instrumentation, Aircraft Flight Monitoring Instruments, etc.
Information: http://ieee1588.nist.gov
Version 2 PAR approved March 2005. Technical work completed

## Slide 660: PTPv1 objectives
Sub-microsecond synchronization
Intended for relatively localized systems
Applicable to networks supporting multicast
Simple, administration free installation
Support heterogeneous systems of clocks with varying precision, resolution and stability
Minimal resource requirements on networks and host components

## Slide 661: Protocol overview
Timing Protocol
  Align slaves to master time
  Measure delay between master and slave
  Measure per-link delay (v2)
Synchronization Hierarchy ‘routing’ Protocol
  Automatic Best Master Clock Algorithm
  Determines the master-slave synchronization clock tree hierarchy
Management Protocol
  Configuration and performance monitoring

## Slide 662: PTP Master-Slave Hierarchy
*Clock symbols taken from ITU-T SG15 ‘synchronization modeling components – time’ contribution #249 Geneva-2007 by Mike Gilson of BT

## Slide 663: Timing Protocol Operation

## Slide 664: Precision using HW time-stamping

## Slide 665: 1-step and 2-step clocks
1-step clock updates accurate timestamp (t1) in Sync message
2-step clock sends accurate timestamp (t1) in a Follow_Up message
  Simplify design while avoiding queuing noise
  Ease integration of security extensions

## Slide 666: PTPv2 major additions
Synchronization accuracies better than 1 nanosecond
Higher sampling/message rates
Unicast communication
Correction for asymmetry
Transparent clocks
Redundancy
Configurable synchronization hierarchy
Decouple sync messaging from hierarchy signaling
Formal mechanisms for message extensions
Mappings to UDP/IPv4&6, Ethernet w/o VLAN, (also DeviceNet™, PROFINET, ControlNet™)

## Slide 667: Sync and Delay-Req formats

## Slide 668: End-to-End Transparent Clocks
E2E TCs cancel queuing and processing delays

## Slide 669: Peer-to-Peer Transparent Clocks
P2P TCs cancel queuing, processing and propagation delays

## Slide 670: Transparent Clock Example
The Master sends a SYNC message containing a Origin Time Stamp field (which contains the Master's Time of Day), and a Correction Field (CF). The Master sets the CF to 0 prior to sending the SYNC message.
As the SYNC message arrives at the first bridge, the bridge uses its time stamping clock to capture the time the message starts arriving at its physical port. Similarly as the SYNC message starts to leave the bridge's physical port heading toward the Slave, it captures the time the message starts leaving the physical port. It can calculate the Residence Time (RT) of the message, which is the delay through bridge, by taking the difference of the two captured time stamps2. As a 1-Step device, the bridge will add its residence time to the CF of the SYNC message as it leaves the exiting physical interface heading towards the Slave. In the figure, this is shown as SumCF.

## Slide 671: Transparent Clock Example
The SYNC message arrives at the second bridge which also calculates its Residence Time and "adds" it to the CF portion of the SYNC message. The CF is accumulative as makes its way to the Slave. The Slave then receives the SYNC message, and captures its time stamp (T2) and extracts and stores away both T1 and CF from the message.
Similarly in the reverse direction, the Slave sends out a DELAY REQUEST message to the Master with CF=0 and captures T3, and the bridges add their Residence Time to the CF portion of the DELAY REQUEST message in an additive way. When the DELAY REQUEST message arrives at the Master, the Master time stamps as usual (T4). The Master then takes both the T4 captured time stamp and the CF that arrived and sends a DELAY RESPONSE to the Slave

## Slide 672: Transparent Clock Example
The Slave now has in this one sequence of SYNC, DELAY REQUEST, DELAY RESPONSE messages: T1, T2 and accumulative CF in the forward direction, as well as T4, T3 and the accumulative CF in the reverse direction. At this point, the time delay error that was introduced by both bridges (shown as Delta) has been told to the Slave via the accumulative CFs. From the figure, this is shown as SumCF = Delta-Forward or Delta-Reverse. The Slave can effectively subtract out the bridge's residence time (which may be small under low traffic load conditions, or large under high load conditions) during each message sequence. This leaves the Slave with the wire delay and thus is the same as in the first case above when no bridges were used.

## Slide 673: Transparent Clock Example
Note: It is important to note that the End-to-End delay mechanism in IEEE 1588 is not immune to Layer2 or Layer 3 topology changes. Even though the bridges that implement End-to-End Transparent Clock effectively take their portion of the delay out of the equation, they do not take the wire delay out of the equation. If a topology change results in more wire delay or less wire delay, then the Slave will see a change in the computed delay with the Master and take some amount of time to stabilize its clock as it readjusts to the new delay.

## Slide 674: Peer Delay Measurement (Optional)

## Slide 675: E2E TC Enabled PSN
Packet queuing and processing is removed

## Slide 676: P2P TC Enabled PSN
Topology change does not effect slave performance

## Slide 677: PTP protocol extensions
Define a profile that selects optional feature set, default and range of values
Define TLV extension to messages
Define flag-fields to be carried in event messages
Define alternate management scheme (SNMP)
Define alternate synchronization hierarchy selection (routing) algorithm
Define additional transport mapping (PTP over MPLS)
Define alternate clock quality levels and attributes

## Slide 678: Shared memory architectures

## Slide 679: Shared memory architectures
Multiple CPU’s (or cores)
One memory with a global address space
  May have many modules
  All CPUs access all memory through the global address space
All CPUs can make changes to the shared memory
  Changes made by one processor are visible to all other processors?
Data parallelism or function parallelism?

## Slide 680: Shared memory architectures
How to connect CPUs and memory?

## Slide 681: Shared memory architectures
One large memory
  One the same side of the interconnect
    Mostly Bus
  Memory reference has the same latency
  Uniform memory access (UMA)
Many small memories
  Local and remote memory
  Memory latency is different
  Non-uniform memory access (NUMA)

## Slide 682: UMA Shared memory architecture (mostly bus-based MPs)
Many CPUs and memory modules connect to the bus
  dominates server and enterprise market, moving down to desktop
Faster processors began to saturate bus, then bus technology advanced
  today, range of sizes for bus-based systems, desktop to large servers (Symmetric Multiprocessor (SMP) machines).

## Slide 683: Bus bandwidth in Intel systems

## Slide 684: Front side bus(FSB) bandwidth in Intel systems
Pentium D | 133 MHz-200 MHz | 4 | 64-bit | 4256 MB/s-6400 MB/s
Pentium Extreme Edition | 200 MHz-266 MHz | 4 | 64-bit | 6400 MB/s-8512 MB/s
Pentium M | 100 MHz-133 MHz | 4 | 64-bit | 3200 MB/s-4256 MB/s
Core Solo | 133 MHz-166 MHz | 4 | 64-bit | 4256 MB/s-5312 MB/s
Core Duo | 133 MHz-166 MHz | 4 | 64-bit | 4256 MB/s-5312 MB/s
Core 2 Solo | 133 MHz-200 MHz | 4 | 64-bit | 4256 MB/s-6400 MB/s
Core 2 Duo | 133 MHz-333 MHz | 4 | 64-bit | 4256 MB/s-10656 MB/s
Core 2 Quad | 266 MHz-333 MHz | 4 | 64-bit | 8512 MB/s-10656 MB/s
Core 2 Extreme | 200 MHz-400 MHz | 4 | 64-bit | 6400 MB/s-12800 MB/s

## Slide 685: NUMA Shared memory architecture
Identical processors, processors have different time for accessing different part of the memory.
Often made by physically linking SMP machines (Origin 2000, up to 512 processors).
The current generation SMP interconnects (Intel Common System interface (CSI) and AMD hypertransport) have this flavor, but the processors are close to each other.

## Slide 686: Various SMP hardware organizations

## Slide 687: Cache coherence problem
Due to the cache copies of the memory, different processors may see the different values of the same memory location.
Processors see different values for u after event 3.
With a write-back cache, memory may store the stale date.
This happens frequently and is unacceptable to applications.

## Slide 688: Bus Snoopy Cache Coherence protocols
Memory: centralized with uniform access time and bus interconnect.
Example: All Intel MP machines like diablo
Notes: 688

## Slide 689: Bus Snooping idea
Send all requests for data to all processors (through the bus)
Processors snoop to see if they have a copy and respond accordingly.
  Cache listens to both CPU and BUS.
  The state of a cache line may change by (1) CPU memory operation, and (2) bus transaction (remote CPU’s memory operation).
Requires broadcast since caching information is at processors.
  Bus is a natural broadcast medium.
  Bus (centralized medium) also serializes requests.
Dominates small scale machines.

## Slide 690: Types of snoopy bus protocols
Write invalidate protocols
  Write to shared data: an invalidate is sent to the bus (all caches snoop and invalidate copies).
Write broadcast protocols (typically write through)
  Write to shared data: broadcast on bus, processors snoop and update any copies.

## Slide 691: An Example Snoopy Protocol (MSI)
Invalidation protocol, write-back cache
Each block of memory is in one state
  Clean in all caches and up-to-date in memory (shared)
  Dirty in exactly one cache (exclusive)
  Not in any cache
Each cache block is in one state:
  Shared: block can be read
  Exclusive: cache has only copy, its writable and dirty
  Invalid: block contains no data.
Read misses: cause all caches to snoop bus (bus transaction)
Write to a shared block is treated as misses (needs bus transaction).

## Slide 692: MSI protocol state machine for CPU requests

## Slide 693: MSI protocol state machine for Bus requests

## Slide 694: MSI protocol state machine (combined)

## Slide 701: Some snooping cache variations
Basic Protocol
  Three states: MSI.
  Can optimize by refining the states so as to reduce the bus transactions in some cases.
Berkeley protocol
  Five states, M  owned, exclusive, owned shared.
Illinois protocols (five states)
MESI protocol (four states)
  M  modified and Exclusive.
  Used by Intel MP systems.

## Slide 702: Multiple levels of caches
Most processors today have on-chip L1 and L2 caches.
Transactions on L1 cache are not visible to bus (needs separate snooper for coherence, which would be expensive).
Typical solution:
  Maintain inclusion property on L1 and L2 cache so that all bus transactions that are relevant to L1 are also relevant to L2: sufficient to only use the L2 controller to snoop the bus.
  Propagating transactions for coherence in the hierarchy.

## Slide 703: Large share memory multiprocessors
The interconnection network is usually not a bus.
No broadcast medium  cannot snoop.
Needs a different kind of cache coherence protocol.

## Slide 704: Basic idea
Use a similar idea of snoopy bus
  Snoopy bus with the MSI protocol
    Cache line has three states (M, S, and I)
    Whenever we need a cache coherence operation, we tell the bus (central authority).
  CC protocol for large SMPs
    Cache line has three states
    Whenever we need a cache coherence operation, we tell the central authority
      serializes the access
      performs the cache coherence operations using point-to-point communication.
        It needs to know who has a cache copy, this information is stored in the directory.

## Slide 705: Cache coherence for large SMPs
Use a directory for each cache line to track the state of every block in the cache.
  Can also track the state for all memory blocks  directory size = O(memory size).
Need to used distributed directory
  Centralized directory becomes the bottleneck.
    Who is the central authority for a given cache line?
Typically called cc-NUMA multiprocessors

## Slide 706: ccNUMA multiprocessors

## Slide 707: Directory based cache coherence protocols
Similar to snoopy protocol: three states
  Shared: > 1 processors have the data, memory up-to-date
  Uncached: not valid in any cache
  Exclusive: 1 processor has data, memory out-of-date
Directory must track:
  Cache state
  Which processors have data when it is in shared state
    Bit vector, 1 if a particular processor has a copy
    Id and bit vector combination

## Slide 708: Directory based cache coherence protocols
No bus and do not want to broadcast
Typically 3 processors involved:
  Local node where a request originates
  Home node where the memory location of an address resides (this is the central authority for the page)
  Remote node has a copy a cache block (exclusive or shared)

## Slide 709: Directory protocol messages example

## Slide 710: Directory based CC protocl in action
Local node (L): WriteMiss(P, A) to home node
Home node: cache line in shared state at processors P1, P2, P3
Home node to P1, P2, P3: invalidate(P, A)
Home node: cache line in exclusive state at processor L.

## Slide 711: Summary
Share memory architectures
  UMA and NUMA
  Bus based systems and interconnect based systems
Cache coherence problem
Cache coherence protocols
  Snoopy bus
  Directory based

## Slide 712: Realtime Programming Tasks
Signal Conversion
Advanced C
Digital Filters
Digital Sampling
Finite State Machines

## Slide 713: Signal Conversion
For the acquisition of physical quantities there are sensors which convert a physical quantity to be measured into an electrical signal (= a function of time).
Analog signals are continuous in value (real valued) and they can be continuous in time or time discrete.
Digital signals are discrete in value and either time discrete or continuous in time.
Since computers can process time discrete and value discrete signals only analog sensor input signals have to be converted into digital (time- and value discrete) signals.

## Slide 714: Signal Conversion
value
continuous
value
discrete
time
discrete
time
continuous
analog signal
digital signal

## Slide 715: Signal Conversion
x(t)
fg
Computer-I/O
N
x(kTs)
Qx[k]
technical
process
A
D
Conv-x
SH
sensor
It is usually ensured that the signal x(t) has no higher frequency components some limit frequency fg ≤ 0.5·fs . This is indicated by the analog low-pass filter with cutoff frequency fg  sampling theorem

## Slide 716: Signal Conversion
x(t)
fg
Computer-I/O
N
x(kTs)
Qx[k]
technical
process
A
D
Conv-x
SH
sensor
The amplitudes of the signal x(k·Ts) are still value continuous (real valued) but values change only at discrete times k·Ts (= sampling)
In a second step the time discrete signal x(k·Ts) is converted into a value discrete signal using an ADC i.e. the real value x is approximated by an integer number Qx out of a sequence (0 … N-1) such that x ≈ Qx·cx with cx as some conversion factor
The quantization error e = x - Qx·cx with the sampling process can be minimized since high resolution AD- and DA-converters are available  e can be usually neglected

## Slide 717: Signal Conversion
After that Qx[k] is a digital signal (time- and value discrete) which can be stored and processes in the computer. With increasing time the index k increases e.g. the sequence { Qx[k-2] Qx[k-1] Qx[k] } is the sequence of the last two recent and the actual sampling value. Example:
{ Qx[k-2] 9 5 -1
Qx[k-1] 5 -1 2
Qx[k] -1 2 7
} k=0 k=1 k=2 …
a sequence Qx[k] as actual sampling value and with Qx[k-1] as the previous and Qx[k-2] as the pre-previous sample.

## Slide 718: Sampling Theorem
This is the fundamental theorem of digital signal processing.
If the bandwidth condition is violated i.e. the bandwidth is greater than half the sampling frequency the analog signal can not be uniquely reconstructed from the sampling due to irreparable signal distortion known as aliasing
A digital sampling system sampling at frequency fs must ensure that an analog signal is bandlimited before sampling an upper frequency limit fg ≤ 0.5 fs .
0.5 fs is also called Nyquist frequency. Thus the sequence clearly determines the associated analog signal which couldn't be processed by a digital computer directly!
An analog signal sampled at constant frequency fs can be reconstructed from the discrete-time sequence of samples (up to a finite delay) if the bandwidth B is not greater than half the sampling frequency thus B < 0.5 fs.

## Slide 719: Sampling Theorem
From the sampling theorem follows how the analog signal x(t-t) can be reconstructed from the discrete time sequence x[k]  by lowpass filtering of the discrete time signal:
fg
Computer-I/O
N
x(t-t)
x(kTs)
Qx[k]
techn.
process
D
A
Conv-x
Sample
actor
The reconstruction is done by a periodic pulse train sampling the DA converted thus value discrete signal which is finally (analog) lowpass filtered at cutoff frequency fg = 0.5fs
The output of the so-called reconstruction lowpass is x(t-t) which is apart from a certain constant time delay t the analog signal x(t) !

## Slide 720: Sampling – Real Time Conditions
A typical requirement for max. jitter (average deviation) of sampling period is 0.1% to 1
With digital sampling systems
strict periodicity of the sampling process in the AD and the DA conversion
to comply with the Nyquist condition (the analog lowpass filters - before any ADC and -after any DAC- with the right cutoff frequency)
shall be respected.
Action | Time Condition
input of a sample of an analog signal | exact periodic sampling at k∙Ts
computation of a signal sample | Deadline bei tmax = (k+1)∙Ts
output of the calculated signal sample | exact periodic sampling at (k+1)∙Ts

## Slide 721: Example: Digital Control Box
Controlling the Temperature of an Engine
  Read in Temperature via ADC
  Calculate Heater Output according to control task
  Output via DAC
  Loop
while (ADC_busy) // status
ADDA Task (periodic time Ts)
// wait
SendQueue(q1 ADC_data)
Start_ADC() // Sample&Hold
Periodic Timer-Events
DAC_output(y) // busy waiting
while (1) // forever
Control task
x = ReceiveQueue(q1)
y = Control(x) // digital control
SendQueue(q2 y)
y = ReceiveQueue(q2)

## Slide 722: Advanced C Programming
Real Time Programming Concepts

## Slide 723: Concepts in this section
typedef’s
Fixed-Point Math
Overflow Protection
Switch Debouncing
State Machines
Filtering
Oversampling

## Slide 724: Good Coding Practices
Signed (good) vs Unsigned (bad) Math
  for physical calculations
Use Braces { Always }
Simple Readable Code
  Concept of Self Documenting Code
  Code as if your grandmother is reading it
Never use Recursion
  (watch your stack)
Treat Warnings as Errors

## Slide 725: Typedef’s
Using Naturally Named Data Types

## Slide 726: Why Typedef?
You use variable with logical names why not use data types with logical names?
Is an int 8-bits or 16-bits? What’s a long? Better question: why memorize it?
Most integer data types are platform dependent!!!
typedef’s make your code more portable.

## Slide 727: How to use typedef’s
Create a logical data type scheme. For example a signed 8-bit number could be s8.
Create a typedef.h file for each microcontroller platform you use.
#include typedef.h in each of your files.
Use your new data type names.

## Slide 728: typedef.h Example
typedef unsigned char u8;
typedef signed char s8;
typedef unsigned short u16;
typedef signed short s16;
typedef unsigned long u32;
typedef signed long s32;
In your code:
unsigned char variable;
Is replaced with:
u8 variable;

## Slide 729: Fixed-Point Math
Fractional Numbers Using Integer Data Types

## Slide 730: Creating Fractions
Fractions are created by using extra bits below your whole numbers.
The programmer is responsible for knowing where the decimal place is.
Move the decimal place by using the shift operator (<< or >>).
Shifting is multiplying by powers of 2. Ex.: x<<5 = x*2^5; x>>5 = x*2^-5

## Slide 731: Fixed Point Fraction Example
A/D Sample (10-bit)
Fractional part
Shift left by 6 (i.e. A2D << 6;):
Whole part

## Slide 732: Fractional Example continued
We know 5/2 = 2.5
If we used pure integers 5/2 = 2 (i.e. the number is rounded toward negative infinity)
Using a fixed-point fractional portion can recover the lost decimal portion.

## Slide 733: Fractional Example continued
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
= 5
A/D Sample (10-bit)
Fractional part
Shift left by 6 (i.e. A2D << 6;):
Whole part
0
0
0
0
0
1
0
1
0
0
0
0
0
0
0
0
= 5.0

## Slide 734: Fractional Example continued
Divide by 2 (i.e. A2D / 2;):
Fractional part
Whole part
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
The whole part: 0000000010(binary) = 2(decimal)
The fractional part: 100000(binary) = 32 (huh???)
Fractional part
Whole part
0
0
0
0
0
1
0
1
0
0
0
0
0
0
0
0

## Slide 735: Fractional Example continued
Divide by 2 (i.e. A2D / 2;):
Fractional part
Whole part
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
The fractional part: 100000(binary) = 32 (huh???)
How many different values can the fractional part be?
Answer: we have 6 bits => 2^6 values = 64 values
(i.e.) 111111 + 1(binary) = 64(decimal)
Therefore:
Fractional part is actually 32/64 = 0.5

## Slide 736: Fractional Example conclusion
Divide by 2 (i.e. A2D / 2;):
Fractional part
Whole part
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
By using a fixed-point fractional part we can have 5/2 = 2.5
The more bits you use in your fractional part the more accuracy you will have.
Accuracy is 2^-(fraction bits).
For example if we have 6 bits in our fractional part (like the above example) our accuracy is 2^-6 = 0.015625. In other words every bit is equal to 0.015625

## Slide 737: Fractional Example example
Adding 2.5 + 2.5
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
Once our math operations are complete we right shift our data to regain our original resolution and data position.
If we look diving and adding multiple values using this method we can see the benefit of fixed point math. This example assumes we are adding two 5/2 operations as shown.
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
1
0
0
0
0
0
0
0
0
+
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
= 5
0
Without using the fixed point math the result of the addition would have been 4 due to the truncation of the integer division.

## Slide 738: Overflow Protection
Making Sure Your Code Is Predictable

## Slide 739: What is Overflow? Why is it Bad?
Overflow is when you try to store a number that is too large for its data type.
For example what happens to the following code?
s8 test = 100;
test = test + 50;
answer: -105
(that’s not good!!!)

## Slide 740: Integer Data Types: Valid Ranges
u8 : 0 - 255
s8 : -128 - 127
u16 : 0 - 65535
s16 : -32768 - 32767
u32 : 0 - 4.294967295e9
s32 : -2.147483648e9 - 2.147483647e9
Note: ranges given are decimal.

## Slide 741: Overflow Protection Methods
Create a new temporary variable using a data type with a larger range to do the calculation.
Compare the sign of the variable before and after the calculation. Did the sign change when it shouldn’t have? (for signed variables)
Compare the variable after the calculation to the value before. Did the value decrease when it should have increased?

## Slide 742: Overflow Protection Example 1
s16 add16(s16 adder1 s16 adder2); // prototype
S16 add16(s16 adder1 s16 adder2)
{
s32 temp = (s32)adder1 + (s32)adder2;
if (temp > 32767) // overflow will occur
return 32767;
else if (temp < -32768) // underflow
return -32768;
else
return (s16)temp;
}
*This example uses a s32 (larger) data value for overflow checking

## Slide 743: Overflow Protection Example 2
// prototype
s16 addTo16bit(s16 start s16 adder);
S16 addTo16bit(s16 start s16 adder)
{
s16 temp = start;
start += adder;
if ((start > 0) && (adder > 0) && (temp <= 0))
return 32767; // Overflow occurred
else if ((start < 0) && (adder < 0) && (temp >= 0))
return -32768; // Underflow occurred
else
return start;
}
*This example uses 16 bit values only to check for overflow on signed
values this provides improved efficiency on 16 bit platforms.

## Slide 744: Overflow Protection Example 3
// prototype
u16 addToUnsigned16bit(u16 start s16 adder);
S16 addToUnsigned16bit(u16 start s16 adder)
{
u16 temp = start;
start += adder;
if ((adder > 0) && (start < temp))
return 65536; // Overflow occurred
else if ((adder < 0) && (start > temp))
return 0; // underflow occurred
else
return start;
}
*This example checks for overflow on unsigned values

## Slide 745: Switch Debouncing
Having Confidence in Switch Inputs

## Slide 746: Why Debounce? When to Use It?
Debouncing a switch input reduces erroneous inputs.
Use debouncing when pressing a switch starts a sequence or changes the state of something.

## Slide 747: When to Debounce Examples
Debounce when a single push of the switch changes a state. Examples:
- pneumatic gripper
- motorized gripper where a single push causes the motor to go until a limit switch is reached
Do not debounce if constant driver input is needed.

## Slide 748: What is Debouncing?
Basically debouncing means to require a certain number of samples before you confirm the switch input.
Various debounce schemes can be used:
- require N consecutive samples (i.e. reset the counter if one sample fails)
- count up / count down (i.e. if one sample fails decrement the counter by 1 rather than resetting to zero.

## Slide 749: Debounce Example
// debounce opening gripper
if (!pneumaticGripperOpenState)
{
if (gripperOpenSwitch == ON)
gripperOpenDebCount++;
else
gripperOpenDebCount = 0;
if (gripperOpenDebCount >= DEBOUNCE_LIMIT)
{
gripperOpenDebCount = 0;
pneumaticGripperOpenState = TRUE;
}
}

## Slide 750: State Machines
Systematic Approach to Complicated Logic

## Slide 751: Finite State Machine - Definition
FSA - Finite State Automation
Models of a behavior of a system or a complex object, with a limited number of defined conditions or modes.
Four Elements:
- States - define behavior and may produce actions.
- State Transitions - movement from one state to another.
- Rules/Conditions - must be met to allow a state transition.
- Input Events - Externally or internally generated, may possible trigger rules and lead to state transitions.

## Slide 752: Finite State Machine - Definition
Initial state - provides a starting point.
Current state - remembers the product of the last state transition.

## Slide 753: DFSM nonDFSM
FSM is typically used as a type of control system where knowledge is represented in the states, and actions are constrained by rules.
An adopted AI technique initially used for language representation.
Two main types of FSM.
Deterministic FSM, meaning that given an input and the current state, the state transition can be predicted.
Non-deterministic finite state machine. This is where given the current state; the state transition is not predictable. It may be the case that multiple inputs are received at various times, means the transition from the current state to another state cannot be known until the inputs are received (event driven).
Non deterministic FSM example : Use a random number generator to select a triggered rule. Adds unpredictability. ( Example : MoveUnit action may be both EvadeEnemy state and AttackEnemy state ). [ State may involve one or more actions ].

## Slide 754: Fuzzy State Machines
In AI and computer games “a player feels like they are playing against a realistic simulation of intelligence, and not against a reproduction of a sequence of actions.”
The "sequence" which is one of the key benefits of FSM, should not be blindingly obvious in computer games. There are a number of extensions to FSM and workarounds for "mixing up" the sequence to make it harder to predict actions. One of these non-deterministic approaches involves the application of another proven artificial intelligence technique; Fuzzy Logic, called Fuzzy State Machines (FuSM).
A fuzzy value can be applied to various state transitions. When a conflict set is encountered the higher the fuzzy value for a transition, the higher the likelihood of the state transition.
An implementation of FuSM may involve the assignment of fuzzy values to various inputs to represent the degree an input is defined. The fuzzy system would use these weighted input values in the evaluation of rules, triggering only state transitions whose assessed value is above a specified threshold.

## Slide 755: Representing a Finite State Machine
It can be represented using a state transition table which shows the current state, input, any outputs, and the next state.
Input Current State | Input0 Input1 …. Inputn
State0 State1 …. Staten | Next State / Output …. Next State / Output …. …. …. …. …. …. …. …. ….

## Slide 756: Representing a Finite State Machine
It can also be represented using a state diagram which has the same information as the state transition diagram.
State0
State1
Input / Output
Input / Output

## Slide 757: State Machines: Definition of Terms
State Diagram
  Illustrates the form and function of a state machine. Usually drawn as a bubble-and-arrow diagram.
State
  A uniquely identifiable set of values measured at various points in a digital system.
Next State
  The state to which the state machine makes the next transition, determined by the inputs present when the device is clocked.
Branch
  A change from present state to next state.
Mealy Machine
  A state machine that determines its outputs from the present state and from the inputs.
Moore Machine
  A state machine that determines its outputs from the present state only.

## Slide 758: Present State and Next State
On a well-drawn state diagram, all possible transitions will be visible, including loops back to the same state. From this diagram it can be deduced that if the present state is State 5, then the previous state was either State 4 or 5 and the next state must be either 5, 6, or 7.
State 6
State 7
State 5
State 4
For any given state, there is a finite number of possible next states. On each clock cycle, the state machine branches to the next state. One of the possible next states becomes the new present state, depending on the inputs present on the clock cycle.

## Slide 759: Moore and Mealy Machines
Both these machine types follow the basic characteristics of state machines, but differ in the way that outputs are generated.
Moore Machine:
  Outputs are independent of the inputs, ie outputs are effectively produced from within the state of the state machine.
Mealy Machine:
  Outputs can be determined by the present state alone, or by the present state and the present inputs, ie outputs are produced as the machine makes a transition from one state to another.

## Slide 760: Moore Machine Diagrams
State 2
x,y
State 1
q,r
a,b
i,j
Input condition that
must exist in order
to execute these
transitions from
State 1
Output condition that
results from being in
a particular present
state
The Moore State Machine
output is shown inside the
state bubble, because the
output remains the same as
long as the state machine
remains in that state.
The output can be arbitrarily
complex but must be the
same every time the
machine enters that
state.

## Slide 761: Moore Machine Diagrams
Outputs are generated as products
of the states.
In this example the states define
what to do ; such as apply power
to the light globe.

## Slide 762: Mealy Machine Diagrams
State 2
State 1
a,b
q,r
i,j
x,y
Input condition that
must exist in order
to execute these
transitions from
State 1
Output condition that
results from being in
a particular present
state
The Mealy State Machine generates outputs based on:
The Present State, and
The Inputs to the M/c.
So, it is capable of generating many different patterns of output signals for the same state, depending on the inputs present on the clock cycle.
Outputs are shown on transitions since they are determined in the same way as is the next state.

## Slide 763: Mealy Machine Diagrams
Outputs are generated as products of
the transitions between states. In example the light is affected by the process of changing states.

## Slide 764: Moore vs. Mealy FSM (1)
Moore and Mealy FSMs Can Be Functionally Equivalent
Mealy FSM Has Richer Description and Usually Requires Smaller Number of States
  Smaller circuit area

## Slide 765: Moore vs. Mealy FSM (2)
Mealy FSM Computes Outputs as soon as Inputs Change
  Mealy FSM responds one clock cycle sooner than equivalent Moore FSM
Moore FSM Has No Combinational Path Between Inputs and Outputs
  Moore FSM is less likely to have a shorter critical path

## Slide 766: FSM Advantages
Simple
Predictable ( deterministic FSM ) - given a set of inputs and a known current state, the state transition can be predicted, allowing for easy testing.
Due to their simplicity, FSMs are quick to design, quick to implement and quick in execution.
FSM is an old knowledge representation and system modeling technique, and its been around for a long time, as such it is well proven even as an artificial intelligence technique, with lots of examples to learn from.
Easy to transfer from a meaningful abstract representation to a coded implementation.

## Slide 767: FSM Disadvantages
The predictable nature of deterministic FSMs can be unwanted in some domains such as computer games (non-DFSM tries to solve this).
The conditions for state transitions are ridged, meaning they are fixed.
Not suited to all problem domains, should only be used when a systems behavior can be decomposed into separate states with well defined conditions for state transitions. This means that all states, transitions and conditions need to be known up front and be well defined !!

## Slide 768: Example: Vending Machine
Takes only quarters and dollar bills
Won't hold more than $1.00
Sodas cost $.75
Possible actions (inputs)
  deposit $.25 (25)
  deposit $1.00 ($)
  push button to get soda (soda)
  push button to get money returned (ret)

## Slide 769: Classic Example: Vending Machine
State: description of the internal settings of the machine, e.g. how much money has been depositied and not spent
Finite states: 0, 25, 50, 75, 100,
Rules: determine how inputs can change state

## Slide 770: Example: Vending Machine
0
25
50
75
100
000
001
010
011
100
ret
ret
ret
ret
soda
soda
100
25
25
25
25
Inputs
25 = 00
100 = 01
soda = 10
ret = 11

## Slide 771: AI Example: Computer Game
The goal : to use a computer game to illustrate the conceptual workings of a FSM based on a practical rather than theoretical implementation.
First person computer game called Quake, under GNU General Public License.
Quake makes extensive use of FSMs as a control mechanism governing the entities that exist in the game world.
Quake is a good example, and a good learning tool that can show the power of both very simple finite state machines such as the rocket, and slightly more complex FSM made up of a hierarchy of FSM and motivated by goals, such as the Shambler monster.

## Slide 772: Quake Computer Game
A rocket in Quake is fired from the Rocket Launcher weapon which may be possessed and operated by a human player.
Full life cycle of a rocket from Quake:
Blue : states.
Orange : triggers.
Black : Entry and
exit point.
Arrows : state
transitions.

## Slide 773: Quake - layered/hierarchical FSM
A Shambler is a big bad monster entity from the single player component of Quake. Its mission in life is to kill the player, once it is aware of the player.
Full life cycle of a shambler monster from Quake:
Blue : states.
Orange : triggers.
Black : Entry and
exit point.
Arrows : state
transitions.
Example of sub states : the monster can only perform one attack per execution of the attack state. Melee - close, Missile - far. Depends on inputs. Use random number in melee to add unpredictability.

## Slide 774: What is a state machine?
A state machine is a method for organizing complicated logic.
A state machine is broken up into discrete states. Logic is defined to switch from one state to another.
Only one state can be active at any time.
It takes one sample (i.e. one time through the code) to switch from one state to another.

## Slide 775: When should I use a state machine?
When performing an automated routine which has many steps.
When the logic is very large and/or difficult to grasp. (Like C programming: break up a large program into smaller functions)
When the problem has physical states (like a light – it has two states: ON and OFF).

## Slide 776: StateCharts: recap of classical automata
Classical automata:
Moore-automata: Y =  (Z); Z+ =  (X, Z)
Mealy-automata Y =  (X, Z); Z+ =  (X, Z)
Internal state Z
input X
output Y
Next state Z+ computed by function  Output computed by function 
Z0
Z1
Z2
Z3
e=1
e=1
e=1
e=1
0
1
2
3
clock
Moore- + Mealy automata=finite state machines (FSMs)

## Slide 777: StateCharts
Classical automata not useful for complex systems (complex graphs cannot be understood by humans).
 Introduction of hierarchy  StateCharts [Harel, 1987]
StateChart = the only unused combination of
„flow“ or „state“ with „diagram“ or „chart“
Used here as a (prominent) example of a model of computation based on shared memory communication.
  appropriate only for local (non-distributed) systems

## Slide 778: Introducing hierarchy
FSM will be in exactly one of the substates of S if S is active (either in A or in B or ..)

## Slide 779: Definitions
  Current states of FSMs are also called active states.
  States which are not composed of other states are called basic states.
  States containing other states are called super-states.
  Super-states S are called OR-super-states, if exactly one of the sub-states of S is active whenever S is active.
superstate
substates

## Slide 780: Default state mechanism
Try to hide internal structure from outside world!
 Default state
Filled circle indicates sub-state entered whenever super-state is entered.
Not a state by itself!

## Slide 781: History mechanism
For input m, S enters the state it was in before S was left (can be A, B, C, D, or E).
If S is entered for the first time, the default mechanism applies.
History and default mechanisms can be used hierarchically.
(behavior different from last slide)

## Slide 782: Combining history and default state mechanism
same meaning

## Slide 783: Concurrency
Convenient ways of describing concurrency req. AND-super-states: FSM is in all (immediate) sub-states of a super-state; Example:

## Slide 784: Entering and leaving AND-super-states
Line-monitoring and key-monitoring are entered and left, when service switch is operated.

## Slide 785: Types of states
In StateCharts, states are either
  basic states, or
  AND-super-states, or
  OR-super-states.

## Slide 786: Timers
Since time needs to be modeled in embedded &
cyber-physical systems, timers need to be modeled.
In StateCharts, special edges can be used for timeouts.
If event a does not happen while the system is in the left state for 20 ms, a timeout will take place.

## Slide 787: Using timers in an answering machine
.

## Slide 788: General form of edge labels
Events:
  Exist only until the next evaluation of the model
  Can be either internally or externally generated
Conditions:
  Refer to values of variables that keep their value until they are reassigned
Reactions:
  Can either be assignments for variables
  or creation of events
Example:
  service-off [not in Lproc] / service:=0
event [condition] / reaction

## Slide 789: Coffee Machine Example
idle
00
coffee+milk
00
+sugar
00
make 07
right
left
left
coffee
00
right
make 03
right
+sugar
00
make
05
right
left
make 01
right
left
left
ready
ready
ready
ready
state
output
State is changed through input.
Output IS NOT state change
Moore State Machine:
Each state has exactly one output

## Slide 790: Coffee Machine
state S | input | state S+ | output
00 idle (initial) | left right | 03: coffee+milk 01: coffee | 0 0
01 coffee | left right | 05: make coffee 03: coffee+sugar | 0 0
02 coffee+milk | left right | 06: make coffee+milk 04: coffee+milk+sugar | 0 0
03 coffee+sugar | left right | 00: idle 07: make coffee+sugar | 0 0
04 coffee+milk+sugar | left right | 00: idle 08: make coffee+milk+sugar | 0 0
05 make coffee | !ready ready | 05: make coffee 00: idle | 01
06 make coffee+milk | !ready ready | 06: make coffee+milk 00: idle | 03
07 make coffee+sugar | !ready ready | 07: make coffee+sugar 00: idle | 05
08 make coffee+milk+sugar | !ready ready | 08: make coffee+milk+sugar 00: idle | 07
State Transition Table

## Slide 791: Coffee Machine FSM - Code
// ---------------------------------------------------------------------------
// the FSM states for the Coffee Automata
// ----------------------------------------------------------------------------
enum { FSM_STATE_IDLE
FSM_STATE_COFFEE FSM_STATE_COFFEE_MILK FSM_STATE_COFFEE_SUGAR FSM_STATE_COFFEE_MILK_SUGAR
FSM_STATE_MAKE_COFFEE FSM_STATE_MAKE_COFFEE_MILK FSM_STATE_MAKE_COFFEE_SUGAR FSM_STATE_MAKE_COFFEE_MILK_SUGAR
};
// ----------------------------------------------------------------------------
int fsm_state = FSM_STATE_IDLE;
// ----------------------------------------------------------------------------
// ----------------------------------------------------------------------------
// the FSM outputs one for each state (Moore Automata model)
// ----------------------------------------------------------------------------
const int fsm_output[NUM_FSM_STATES] = { // output is fsm_output[fsm_state]
0 // bit0: add coffee
0 0 // bit1: add milk
0 0 // bit2: add sugar
1 3
5 7
};

## Slide 792: Coffee Machine FSM - Code
// ----------------------------------------------------------------------------
// the FSM inputs
// ----------------------------------------------------------------------------
enum { FSM_INP_NONE=0 FSM_INP_LEFT FSM_INP_RIGHT FSM_INP_READY };

## Slide 793: Coffee Machine FSM - Code
int fsm_tic(int fsm_inp) // called periodically e.g. each 50 ms
{
// ------------------------------------------------------------
// the FSM transients realizing the state transient table
// ------------------------------------------------------------
switch (fsm_state) {
case FSM_STATE_IDLE:
if (fsm_inp == FSM_INP_LEFT) fsm_state = FSM_STATE_COFFEE;
if (fsm_inp == FSM_INP_RIGHT) fsm_state = FSM_STATE_COFFEE_MILK;
break;
case FSM_STATE_COFFEE:
if (fsm_inp == FSM_INP_LEFT) fsm_state = FSM_STATE_MAKE_COFFEE;
if (fsm_inp == FSM_INP_RIGHT) fsm_state = FSM_STATE_COFFEE_SUGAR;
break;
case FSM_STATE_COFFEE_MILK:
if (fsm_inp == FSM_INP_LEFT) fsm_state = FSM_STATE_MAKE_COFFEE_MILK;
if (fsm_inp == FSM_INP_RIGHT) fsm_state = FSM_STATE_COFFEE_MILK_SUGAR;
break;
case FSM_STATE_COFFEE_SUGAR:
if (fsm_inp == FSM_INP_LEFT) fsm_state = FSM_STATE_IDLE;
if (fsm_inp == FSM_INP_RIGHT) fsm_state = FSM_STATE_MAKE_COFFEE_SUGAR;
break;

## Slide 794: Coffee Machine FSM - Code
case FSM_STATE_COFFEE_MILK_SUGAR:
if (fsm_inp == FSM_INP_LEFT) fsm_state = FSM_STATE_IDLE;
if (fsm_inp == FSM_INP_RIGHT) fsm_state = FSM_STATE_MAKE_COFFEE_MILK_SUGAR;
break;
case FSM_STATE_MAKE_COFFEE:
case FSM_STATE_MAKE_COFFEE_MILK:
case FSM_STATE_MAKE_COFFEE_SUGAR:
case FSM_STATE_MAKE_COFFEE_MILK_SUGAR:
if (fsm_inp == FSM_INP_READY) fsm_state = FSM_STATE_IDLE;
break;
default:
; // no state change
}
OUTPUT(fsm_output[fsm_state]); // Moore FSM: one output per state
return fsm_state;
}

## Slide 795: Recipe for Realizing a Moore FSM in C
• Analyze the problem before coding plot a state diagram define the states
• Use enums to encode states in a well readable form
• Define outputs as enums with suitable encoding e.g. as bit-fields
• Define input conditions causing the state transitions as enums as well
• Realize a periodicaly called fsm_tic function realize transients and outputs

## Slide 796: Safe and Efficient One-Hot State Machine
  Based on a presentation by
  Jason Zheng,
  Sunant Katanyoutanant, Martin Le
  Jet Propulsion Laboratory

## Slide 797: Motivation
Finite State Machines (FSM) are important building blocks of avionic control systems.
Single Event Upsets (SEU) can corrupt FSM state registers
Substantial research done in making FSM safer
Asynchronous Nature of SEU complicates mitigation mechanisms

## Slide 798: Roadmap
How do asynchronous SEU affect FSM logic? How to recover when SEU occur?
  A: Analyze SEU effects in three time zones within a clock cycle
What improvements can we make to the existing mitigation methods?
  A: Speed up FSM and error-detection logic
How to implement the improvements?
  A: Fast implementation with Python scripts

## Slide 799: Overview
Background Information
Asynchronous SEU Analysis (Question 1+2)
Existing Mitigation Methods
Challenge
One-Hot with Pipelined XNOR (Question 3)

## Slide 800: Background - FSM
Set of States S1…Sn
Set of Inputs I1…Im
Set of Outputs O1…Ok
Output Function (OF)
Next State Function (NS)
This is a Moore FSM, but our research apply to Mealy FSM as well
OF
NS
Current
State
Register
Next State
Input
Output
Register

## Slide 801: Background – State Encoding
Each state Si is represented by a binary pattern Pi, where i is an arbitrary index.
A mapping from the state index i to Pi is the state encoding function E.
Binary (sequential) encoding: E(i) = i; i = 1,2,…,n
One-hot encoding: E(i) = 2i; i = 0,1,…,n-1
Others: grey, johnson, hamming-2, etc.

## Slide 802: Overview
Background Information
Asynchronous SEU Analysis
Existing Mitigation Methods
Challenge
One-Hot with Pipelined XNOR

## Slide 803: SEU – First Look
Single Event Upsets are radiation-induced errors caused by passing charged particles
Two effects of SEU on current state
  Error state: an erroneous but legal state
  Illegal state: an undefined state (FSM stuck)
Asynchronous nature of SEU complicates the effect on the next state
  No effect (SEU occur in green zone)
  Erroneous or illegal next state (red zone)
  Uncertain (yellow zone)

## Slide 804: SEU w/o Detection/Correction
SEU in Red: erroneous or illegal next state (corrupted state has enough time to alter the next state)
Yellow: next state is uncertain
  Corrupted state traverses through some, but not all, logic paths
  Correct state (SEU happens before t1-Ts and Ts < Tmin)
  Meta-stable (SEU happens after t1-Ts and Ts > Tmin)
Critical Path in FSM
Tmax
Setup
Ts
t0
t1
Tmin

## Slide 805: SEU w/ Detection/Correction
Red zone: no error detection - illegal or erroneous next state
SEU occur in yellow zone: still uncertain next state
  Corrupted state traverses through some, but not all, logic paths
  Correct state
  Meta-stable
Green = detectable or fixable SEU
Setup
Ts
Reset
Tr
Critical Path in FSM
Tmax
Tmin
Error Detection Td
t0
t1

## Slide 806: Logic Glitches (SET)
Single Event Tensions (SET) are not SEU, but analysis applies
Green Zone: logic glitches can self-recover
Yellow Zone: uncertain (distance to t1 and timing)
  Erroneous result
  Correct result (glitch happens too late)
  Meta-stable result
Critical Path in FSM
Setup
Glitch
Settle
Time
t0
t1

## Slide 807: Expanding the Green Zone
Setup time = fixed
Cycle time = fixed
Yellow is dominated by Tmax (slowest FSM logic delay)
Red is dominated by Td - Tmax
Must speed up both FSM and detection logic!
FSM - Tmax
Error Detection - Td
More Deterministic

## Slide 808: Overview
Background Information
Asynchronous SEU Analysis
Existing Mitigation Methods
Challenge
One-Hot with Pipelined XNOR

## Slide 809: Existing Mitigation Methods
SEU Correction
  Triple Modular Redundancy (TMR)
  Hamming-3 Companion States (h3)
SEU Detection
  The “default” case (full-state lookup)
  Hamming-2 (h2)
  One-hot + XNOR tree (1hot_s)

## Slide 810: Triple Modular Redundancy
FSM1
FSM2
FSM3
Voting
Logic
Output
Simple concept
Tried-and-hard
Applicable to any synchronous logic

## Slide 811: Hamming-3 Companion States
Every legal state has m companion states, where m = width of state register.
n * (m+1) ≤ 2m (compare to n ≤ 2m), where n = number of legal states
One bit-flip turns a legal state into a companion state
Corrects one bit of error by looking up the legal states and all possible companion states
A 16-state FSM need 112 companion states

## Slide 812: Hamming-3
0000000
0000001
0000010
0000100
0001000
0010000
0100000
1000000
Total number of states:
27 = 128
Number of legal states:
27 / (7+1) = 16
Hamming distance between two strings of equal length is the number of positions at which the corresponding symbols are different. In other words, it measures the minimum number of substitutions required to change one string into the other, or the minimum number of errors that could have transformed one string into the other.

## Slide 813: The “Default” Case
always @ *
case (state)
st1: nextState = …
st2: nextState = …
…
default: nextState = …
endcase
OF
NS
State
Register
Next State
Input
Illegal state?
Synchronous
Reset
Output
Register

## Slide 814: The “Default” Case (cont.)
Cannot detect error when SEU flips state registers to another defined state
Big performance hit and area overhead with sparse encoding
Some logic synthesizers ignore default states to optimize FSM

## Slide 815: Binary + Parity (Hamming-2)
Minimum hamming distance of 2
E(n) = n + parity(n)
Can detect single-bit error by XORing all the bits
Slightly slower than binary encoding but more robust
Tested and preferred by JPL Avionics Electronics Section
Example H-2 Code:
00000
00011
00101
00110
01001
…
11110

## Slide 816: One-hot + XNOR
1-bit State Lookup
Sparse code
Use multi-input XNOR logic to detect illegal states
XNOR can be tricky to implement
XNOR Logic levels = log2N-1
OF
NS
State
Register
Next State
Input
XNOR
Synchronous
Reset
Output
Register
one-hot is a group of bits among which the legal combinations of values are only those with a single high (1) bit and all the others low (0)

## Slide 817: A 16-Input XNOR Tree Example
F is a 4-bit adder with some modifications
G is a 4-input XNOR
Works well for 4-LUT (Look-Up Table) architectures
Most synthesis tools cannot generate optimal XNOR tree
Must use synthesis directives to prevent logic pruning
F
F
F
F
F
F
G

## Slide 818: XNOR
Input |  |  | Output
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 819: Overview
Background Information
Asynchronous SEU Analysis
Existing Mitigation Methods
Challenge
One-Hot with Pipelined XNOR

## Slide 820: Can We Do Better?
What is “better?”
  More deterministic under asynchronous SEU
  Faster logic (smaller red zone)
  Small area overhead
  Easy to code
Our approach: one-hot with pipelined XNOR detection

## Slide 821: Overview
Background Information
Asynchronous SEU Analysis
Existing Mitigation Methods
Challenge
One-Hot with Pipelined XNOR

## Slide 822: Why One-hot?
One-hot is fast (one-bit state look-up)
XNOR can detect multiple-bit errors (most of the time)
XNOR is moderate in area consumption
XNOR tree lends itself to pipelining
But there are trade-offs…
F
F
F
F
F
F
G

## Slide 823: Pipelining Trade-off
Reset Delays
Logic levels
Deterministic Level
Chance of Single-Bit Flip
LXNOR: XNOR w/o pipeline
LFSM: FSM w/o XNOR
SEU on pipeline register can cause false-positive reset
# of Pipeline Stages
Reset Delays
Levels of Logic
LXNOR
LFSM

## Slide 824: Filtering
Smoothing Your Signals

## Slide 825: Filter Types
Filters are classified by what they allow to pass through (NOT what they filter out).
For example a low pass filter (abv. LPF) allows low frequencies to pass through – it therefore removes high frequencies.
The most common filters are: high pass filters low pass filters and band pass filters.
We will only cover low pass filters.

## Slide 826: Low Pass Filters
Low Pass Filters (LPFs) are used to smooth out the signal.
Common applications:
  Removing sensor noise
  Removing unwanted signal frequencies
  Signal averaging

## Slide 827: Low Pass Filters continued
There are two basic types of filters:
  Infinite Impulse Response (IIR)
  Finite Impulse Response (FIR)
FIR filters are moving averages
IIR filters act just like electrical resistor-capacitor filters. IIR filters allow the output of the filter to move a fixed fraction of the way toward the input.

## Slide 828: Moving Average (FIR) Filter Example
#define WINDOW_SIZE 16
s16 inputArray[WINDOW_SIZE];
u8 windowPtr;
s32 filter;
s16 temp;
s16 oldestValue = inputArray[windowPtr];
filter += input - oldestValue;
inputArray[windowPtr] = input;
if (++windowPtr >= WINDOW_SIZE)
{
windowPtr = 0;
}

## Slide 829: Moving Average Filter Considerations
For more filtering effect use more data points in the average.
Since you are adding a lot of numbers there is a high chance of overflow – take precautions

## Slide 830: IIR Filter Example (Floating Point)
#define FILTER_CONST 0.8
static float filtOut;
static float filtOut_z;
float input;
// filter code
filtOut_z = filtOut;
filtOut = input + FILTER_CONST * (filtOut_z – input);
// optimized filter code (filtOut_z not needed)
filtOut = input + FILTER_CONST * (filtOut – input);

## Slide 831: IIR Filter Example (Fixed Point)
// filter constant will be 0.75. Get this by
// (1 – 2^-2). Remember X * 2^-2 = X >> 2
#define FILT_SHIFT 2
static s16 filtOut;
s16 input;
// filter code
filtOut += (input - filtOut) >> FILT_SHIFT;

## Slide 832: IIR Filter Example (Fixed Point)
Whoa! How did we get from
filtOut = input + FILTER_CONST * (filtOut – input);
To
filtOut += (input - filtOut) >> FILT_SHIFT;
Math:
filtOut = input + (1 - 2^-2) * (filtOut – input)
= input + filtOut – input – 2^-2*filtOut + 2^-2*input
= filtOut + 2^-2 * (input – filtOut)
filtOut += (input – filtOut) >> 2

## Slide 833: IIR Filter Considerations (Fixed Point)
For more filtering effect make the shift factor bigger.
Take precautions for overflow.
You can get more resolution by using more shift factors. For example have your filter constant be
(1 – 2^-SHIFT1 – 2^-2SHIFT2)
(you’ll have to work out the math!)

## Slide 834: Oversampling
Gain resolution and make your data more reliable.

## Slide 835: Oversampling Basics
Simple oversampling: sample more data (i.e. faster sample rate) than you need and average the samples.
Even if you don’t sample faster averaging (or filtering the data) can be beneficial.

## Slide 836: Oversampling Effects
Helps to smooth the data.
Helps to hide a bad or unreliable sample.
Increases A/D resolution if noise is present.

## Slide 837: Oversampling Effects
0.3!!!

## Slide 838: Optimizations
Make your code run faster.

## Slide 839: Optimizations
Use fixed point math not floating point.
If possible do not use data types larger than the microcontroller’s native data type.
When possible use bit-shifts instead of multiplying or dividing.
  WARNING: some micro/compiler combinations do not properly handle signed shifts (the FRC controller is a good example).
For high speed interrupts: use as little code as possible; try and move any processing to the slower code outside of the interrupt.
Use overflow to your advantage.

## Slide 840: Example (Using Overflow)
Very efficient 8-sample FIR filter:
static u8 filtIndex = 0;
filtOut += (a2dInput - filtArray[(filtIndex & 0x07)]);
filtArray[(filtIndex & 0x07)] = a2dInput;
filtIndex++;
Compare the above filter to the FIR filter example given in the Filtering portion of the presentation. Note that it eliminates the need for if statements. The overflow automatically handles wrapping the array index.
This concept will work as long as the size of the filter is a power of 2.

## Slide 841: Serial IO - revisited
Serial Port Access
Buffering
Timing
Byte vs Text

## Slide 842: Serial - Introduction
In computing a serial port is a serial communication physical interface through which information transfers in or out one bit at a time (in contrast to a parallel port).
Usually this means the RS-232 standard or less frequently RS-485 . They are a very basic method of communication with devices still in common use for scientific equipment. However most modern desktop and laptop computers do not come with serial ports and instead we use them via a USB converter.

## Slide 843: Accessing Serial Ports - Python
Similar Library available in C/C++
#!/usr/bin/env python
import serial
ser = serial.Serial(
port='/dev/ttyUSB0’
baudrate=9600
bytesize=serial.EIGHTBITS
parity=serial.PARITY_NONE
stopbits=serial.STOPBITS_ONE
)
# 8 here is specific to the data transmitted.
print ser.read(size=8)
ser.close()

## Slide 844: Why ser.read(size = 8)?
Communication Protocoll Datasheet could read
<sign><3 characters – integer °C><decimal point><1 character – tenths of °C><C><Enter>
In ASCII coding each character is one byte so each temperature from the thermometer is eight bytes.
Note the <Enter> as the End of Line Character which is Carriage Return rather than Newline
This is important for reading complete lines
It comes from typewriters…carriage return goes to position1 on the same line newline moves to the next line.

## Slide 845: Adding time information
#!/usr/bin/env python
from datetime import datetime
import serial
ser = serial.Serial(
port='/dev/ttyUSB0’
baudrate=9600
)
print datetime.utcnow().isoformat() ser.read(size=8)
ser.close()
This will deliver something like:
2014-03-06T11:55:43.852953 +025.3C

## Slide 846: Timing Issues
A major problem with the above code is the line:
print datetime.utcnow().isoformat() ser.read(size=8)
It is not immediately obvious that the datetime.utcnow() call can return in advance of the ser.read() call which will stall until the thermometer returns data.
Consequently the timing can be far off.

## Slide 847: Timing issues
To ensure that the timestamp and the temperature line up as closely as possible we can store the data in a variable and output the variable and the time at the same time reducing the gap between them:
datastring = ser.read(size=8)
print datetime.utcnow().isoformat() datastring
This will reduce the delay between timestamp and time of transmission of the data.

## Slide 848: Continuous Logging
#!/usr/bin/env python
from datetime import datetime
import serial
ser = serial.Serial(
port='/dev/ttyUSB0’
baudrate=9600
)
while ser.isOpen():
datastring = ser.read(size=8)
print datetime.utcnow().isoformat() datastring
ser.close()

## Slide 849: Final Version using Readline
#!/usr/bin/env python
'''This version of the readserial program demonstrates using python to write an output file'''
from datetime import datetime
import serial, io
outfile='/tmp/serial-temperature.tsv'
ser = serial.Serial(
port='/dev/ttyUSB0’,
baudrate=9600,
)
sio = io.TextIOWrapper( #defines a pair of encoding operations that always transform
io.BufferedRWPair(ser, ser, 1), #the data before it is sent to the serial connection or read
encoding='ascii', newline='\r’
)
with open(outfile,'a') as f: #appends to existing file
while ser.isOpen():
datastring = sio.readline() #we can now use readline to read until EOL
#\t is tab; \n is line separator
f.write(datetime.utcnow().isoformat() + '\t' + datastring + '\n’)
f.flush() #included to force the system to write to disk
ser.close()

## Slide 850: Continous Logging Issues
Serial Data is buffered
Serial Read Commands read from the buffer
If more than one dataset accumulates in the buffer the timing is wrong
Solution
  Either read faster than the buffer is filled
  Read all the buffer whenever you read and sort the data
  Assign times by interpolation if there is more than one data item in the buffer.
  Make the sender wait for a request to send before sending data

## Slide 851: Triggering and Closing Serial transmission
import serial
import numpy as np
from matplotlib import pyplot as plt
import time
# make sure that at an abnormal exit the serial connection is closed.
import atexit
def close_serial():
ser.close()
atexit.register(close_serial)
ser = serial.Serial('COM9’, 9600 timeout=0)
time.sleep(10) #Wait to avoid reading issues
timepoints = []
buffer = []
# flush any junk left in the serial buffer
ser.flushInput()
#send the 'g' string over the air that will start transmission.
ser.write(ser.write(bytearray('g‘’, ascii')))
while len(buffer) <= 210: #this needs to vary according to how long things take in the code
waiting = ser.in_waiting # find num of bytes currently waiting in hardware
buffer += [chr(c) for c in ser.read(waiting)] # read them convert to ascii

## Slide 852: Serial Byte order…Endianness
Big-Endian Little-Endian
C-type name initial value memory at offset memory at offset
of variable +0 +1 +2 +3 +0 +1 +2 +3
int32_t longVar = 0x0a0b0c0d; 0Ah 0Bh 0Ch 0Dh 0Dh 0Ch 0Bh 0Ah
int16_t shortVar = 0x0c0d; 0Ch 0Dh 0Dh 0Ch
A simple way to remember is "In Little Endian, the Least significant byte goes into the Lowest-addressed slot".
So in the example in the table, 0Dh, the least significant byte, in a Little-Endian system goes into slot +0.

## Slide 853: Serial – Converting Bytes to ASCII
>>>from struct import *
>>>pack('hhl', 1, 2, 3)
b'\x00\x01\x00\x02\x00\x00\x00\x03’
>>>unpack('hhl’, b'\x00\x01\x00\x02\x00\x00\x00\x03')
(1, 2, 3)
>>> calcsize('hhl’)
8
hhl means “short int, short int, long int” Similar Functions are available in other languages

## Slide 854: Serial Conclusion
Serial Connections are simple to set up
They are always buffered
You need to ensure that you read the right amount of data in the right amount of time
Timing serial data is best done by the sender!
You need to handle conversion to and from bytes, as that is usually what is transferred.

## Slide 855: Lab Experiment 1 – Key Concepts
Setting up a project
Setting a timer interrupt
Creating a heartbeat task
Creating a time slice scheduling task using ISR
Creating a binary Non-Preemtive FTS scheduler
Measuring Execution Times
Setting up an AD conversion task
Integrating an AD conversion task in the schedule

## Slide 856: Lab Experiment 1 - Scheduler
Timer_ISR() calls FTS Scheduler!

## Slide 857: Lab Experiment 1 – Heartbeat Tasks

## Slide 858: Lab Experiment 1 – AD Conversion
Read AD – then toggle Level Display LED

## Slide 859: Lab Experiment 2 – Key Concepts
Create a FreeRtos Project
Work with Rtos Tasks
Create a heartbeat blink in Rtos
Create a AD-DA Task in Rtos
  Control timing and sequence of AD and DA operations
Create a PWM Task in Rtos
  Control pulsewidth and period of the PWM signal
Create a user input for the PWM control
Using critical section to protect serial communication

## Slide 860: Lab Experiment 2 - Tasks
Task Overview:
Main
  Creates Tasks
  handles Initialisation
Ioinit
  sets up timers
  sets up AD / PWM Modules
  sets up UART
  enables interrupts again
Blink
  heartbeat
Motor
  Send DAC to PWM output
UART
  communication
ADDA
  AD Conversion
  Set DAC value

## Slide 861: Lab Experiment 2 – ADDA Task

## Slide 862: Lab Experiment 2 – Motor Task

## Slide 863: Lab Experiment 2 – Critical Section
while(1)
{
c = 0;
ret = xSerialGetChar(hcom, &c, portMAX_DELAY); // <---- sync/mutex from UART RX IRQ
taskENTER_CRITICAL();
if (ret == pdTRUE) {
if (c_1 == 0x09) { // Message ID: set DAC <byte>
DAC_out = c;
// LED_Port ^= ( 1 << PC6 ) ; // XOR: toggle LED6 --> cmd indicator
} else if (c == 0x08) { // Message ID: toggle motor task
// toggle motor task
if (state_motor_task_suspended) {
vTaskResume(hMotorTask);
state_motor_task_suspended = 0;
} else {
vTaskSuspend(hMotorTask);
state_motor_task_suspended = 1;
}
}
c_1 = c; // save last char
} else {
LED_Port ^= ( 1 << PC7 ) ; // XOR: toggle LED7 --> RX error indicator
}
taskEXIT_CRITICAL();
}
}

## Slide 864: Lab Experiment 3 – Key Concepts
Manually flashing .hex files and using online diagnostics
Using Semaphores for task synchronization
Configuring FreeRTOS
FreeRTOS non-application tasks
Getting BECT/WECT from FreeRTOS Basic Application

## Slide 865: Lab Experiment 3 - Tasks

## Slide 866: Lab Experiment 3 -Execution

## Slide 867: Lab Experiment 3 – FreeRTOS Basic App

## Slide 868: Lab Experiment 3 – FreeRTOS Basic 2

## Slide 869: Lab Experiment 4 – Key Concepts
Multitasking
Suspending and Resuming Tasks
Implementing a physical control device
Measuring WCET
Dealing with complex code.

## Slide 870: Lab Experiment 4 - Tasks

## Slide 871: Lab Experiments 4 - Flowchart

## Slide 872: Lab Experiment 5 – Key Concepts
Refactor existing code
IPC using Message Queues
Control using physical controls
Control using UDP application (socket interface)
Control using uart (serial)

## Slide 873: Lab Experiment 5 – Tasks 1

## Slide 874: Lab Experiment 5- Tasks 2